## Slide 1: AHG 5 and 18: Entropy Coding Compression Efficiency for High Bit Depths
JCTVC-N0189
Broadcast & Professional Research Labs
Sony Europe Ltd.
Karl Sharman
Sony Corp.

## Slide 2: Background
Coding higher bit-depth data gradually becomes more costly.
For the sequences tested:
  For 16-bit data,
    Without lossless coding tools, the sequences are actually inflated at their useful operating range: (MSE <= 1, SNR >= 96.3, i.e. QP <= -32)
    The base-band video rate is 1920x1080x16x3x50 = ~ 5 Gbps.
    Lossless coding tools (PCM mode) are generally used.
  For 14-bit data,
    Without lossless coding tools, the sequences are inflated for a substantial part of their operating range: (MSE <= 0.5, SNR >= 81.3, i.e. at QP <= -26)
    The 14-bit base-band video rate is ~4.4 Gbps.
    In simple terms, 13-bit video data would be compressible; 14-bit video data would be better coded as raw / PCM.
    This occurs for AVC as well.

## Slide 3: Increase CABAC Efficiency
The addition of a “fixed bits” scheme to the entropy coding was proposed in M0178:
  Conceptually, the algorithm is (for a number of fixed bits BF):
  For each significant coefficient, C,
    split the value C into CMSB and CLSB, where CLSB comprises the BF least-significant bits of C.
    Code CMSB as for normal coefficients in a group.
    After the sign bits are coded, code the bits for CLSB using EP bins.
      (Sign bit hiding is based upon the entire coefficient C.)

## Slide 4: M0178 Fixed Bits results
From the studies at higher bit-depths, with
  MAX_TR_DYNAMIC_RANGE = bitDepth+6
  ENTROPY_CODING_DYNAMIC_RANGE = bitDepth+6
  Transform matrix precision = 14
  Transform skip enabled; TransQuant-Bypass, RDOQ and PCM disabled

## Slide 5: Extension of M0178 Fixed Bits
  The fixed bits scheme has been rolled into the Golomb Rice escape parameter scheme.
    This results in slightly reduced gains from the original scheme, but does not require additional stages in the entropy process.
    The reduction in gains is because the fixed bits applied to all non-zero coefficients, where as this scheme only applies to all escape coded coefficients.
  When BF fixed bits would have been used, now the Golomb Rice parameter cRiceParam is increased by BF at the start of the TU, and clipped to 4+BF during the processing.
  The question then remains on how to select BF.
    In M0178, BF was chosen by the encoder, with BF =max(0,-QP/6) being a reasonable estimate.
    However, an algorithm to adapt BF is now presented.

## Slide 6: Auto-adaptation
Auto-adaptation requires the value BF to be treated as a slice-scoped (cf context-variable) parameter.
  BF is initialised to 0 at the start of the slice.
  For each TU encoded/decoded:
    The variables undershootCount, overshootCount and totalCount are each initialised to 0.
    For each coefficient that requires an escape code, escapeCode, do: totalCount++ if (escapeCode > (3 << cRiceParam)) undershootCount++ else if ((escapeCode * 3) < (1 << cRiceParam)) overshootCount++
    At the end of encoding/decoding the TU, BF is adjusted according to the following pseudo-code: if ((undershootCount * 4) > totalCount) BF++ else if (((overshootCount * 2) > totalCount) && (BF > 0)) BF--
    (BF is naturally limited to ENTROPY_CODING_DYNAMIC_RANGE (as defined in JCTVC-N0188))

## Slide 7: Results – lossy and mixed coding
BD-rate changes using green channel PSNR for OldTownCross
  Other SVT sequences behave similarly. Traffic_12bit (padded to 16-bit) reaches -21.6% at 96dB.

## Slide 8: Results –AHG5 RExt conditions
The algorithm is not targeted for lower-bit-rate applications.
  However it does not degrade the system

## Slide 9: Results – standard AHG8 conditions
The adaptive algorithm, developed for high bit depths and/or high bit rates is also applicable to AHG8 lossless test conditions.

## Slide 10: Conclusion
The Golomb-Rice Parameter modification with auto-adaptation gives BD-rate efficiency improvements of:
      -30.3% at 96dB (16-bit operating point),
      -21.5% at 84dB (14-bit operating point),
      -8.25% at 72dB (12-bit operating point),
      -0.72% at 60dB (10-bit operating point) and
      +0.02% at 0dB (8-bit operating point)
      for SVT sequences, relative to the proposed higher internal accuracy system described in JCTVC-N0188.
    There are no significant changes at the RExt intra operating conditions.
In addition, the system has been tested using the AHG8 lossless test conditions, with intra BD-rate changes of:
    -1.6% (F), 0.0% (B), -16.4% (ScreenContent RGB), -8.3%, (ScreenContent 4:4:4) -2.4% (RangeExt).
    Similar savings for the inter test conditions
It is proposed that this modification is available for all high bit depth and high bit rate profiles, including lossless.