## Slide 1: AHG 5 and 18: Entropy Coding Throughput for High Bit Depths
JCTVC-N0190
Broadcast & Professional Research Labs
Sony Europe Ltd.
Karl Sharman
Sony Corp.

## Slide 2: Background (from JCTVC-M0178)
Many of the bits at QP<0 will be equi-probable (EP) bins.
EP bins require a subtraction to decode.
  The subtractions to decode multiple EP bins require sequential processing.
To decode N EP bins,
  The process can be thought of as a N-stage long division by ivlCurrRange1
An example of EP decoding is as follows:
      Note 1: ivlCurrRange is equivalent to m_uiRange in HM.

## Slide 3: Worked Example: ivlCurrRange = 458
bit-stream
ivlOffset = 303
1
0
0
1
0
1
1
1
1
1
1
1
0
1
0
DecodeBypass
ivlOffset = ivlOffset<<1 ivlOffset = ivlOffset | read_bits(1)
ivlOffset >= ivlCurrRange ?
ivlOffset = ivlOffset – ivlCurrRange
binVal = 1
binVal = 0
Done
?
Decoded bins:
No
Yes

## Slide 4: Worked Example: ivlCurrRange = 458
bit-stream
ivlOffset = 607
1
0
0
1
0
1
1
1
1
1
1
1
0
1
0
DecodeBypass
ivlOffset = ivlOffset<<1 ivlOffset = ivlOffset | read_bits(1)
ivlOffset >= ivlCurrRange ?
ivlOffset = ivlOffset – ivlCurrRange
binVal = 1
binVal = 0
Done
?
Decoded bins:
No
Yes

## Slide 5: Worked Example: ivlCurrRange = 458
bit-stream
ivlOffset = 607
1
0
0
1
0
1
1
1
1
1
1
1
0
1
0
DecodeBypass
ivlOffset = ivlOffset<<1 ivlOffset = ivlOffset | read_bits(1)
ivlOffset >= ivlCurrRange ?
ivlOffset = ivlOffset – ivlCurrRange
binVal = 1
binVal = 0
Done
?
Decoded bins:
No
Yes

## Slide 6: Worked Example: ivlCurrRange = 458
bit-stream
ivlOffset = 149
0
0
1
0
0
1
0
1
0
1
1
1
0
1
0
DecodeBypass
ivlOffset = ivlOffset<<1 ivlOffset = ivlOffset | read_bits(1)
ivlOffset >= ivlCurrRange ?
binVal = 0
Done
1
?
Decoded bins:
No
Yes
ivlOffset = ivlOffset – ivlCurrRange
binVal = 1

## Slide 7: Worked Example: ivlCurrRange = 458
bit-stream
ivlOffset = 149
0
1
0
0
1
0
1
0
1
1
1
0
1
0
0
DecodeBypass
ivlOffset = ivlOffset<<1 ivlOffset = ivlOffset | read_bits(1)
ivlOffset >= ivlCurrRange ?
ivlOffset = ivlOffset – ivlCurrRange
binVal = 1
binVal = 0
Done
1
Decoded bins:
No
Yes
?

## Slide 8: Worked Example: ivlCurrRange = 458
bit-stream
ivlOffset = 299
0
1
0
0
1
0
1
0
1
1
1
0
1
0
0
DecodeBypass
ivlOffset = ivlOffset<<1 ivlOffset = ivlOffset | read_bits(1)
ivlOffset >= ivlCurrRange ?
ivlOffset = ivlOffset – ivlCurrRange
binVal = 1
binVal = 0
Done
1
Decoded bins:
No
Yes
?

## Slide 9: Worked Example: ivlCurrRange = 458
bit-stream
ivlOffset = 299
0
1
0
0
1
0
1
0
1
1
1
0
1
0
0
DecodeBypass
ivlOffset = ivlOffset<<1 ivlOffset = ivlOffset | read_bits(1)
ivlOffset >= ivlCurrRange ?
ivlOffset = ivlOffset – ivlCurrRange
binVal = 1
binVal = 0
Done
1
Decoded bins:
No
Yes
?

## Slide 10: Worked Example: ivlCurrRange = 458
bit-stream
ivlOffset = 299
0
1
0
0
1
0
1
0
1
1
1
0
1
0
0
DecodeBypass
ivlOffset = ivlOffset<<1 ivlOffset = ivlOffset | read_bits(1)
ivlOffset >= ivlCurrRange ?
ivlOffset = ivlOffset – ivlCurrRange
binVal = 1
binVal = 0
Done
1
Decoded bins:
No
Yes
0

## Slide 11: Worked Example: ivlCurrRange = 458
bit-stream
ivlOffset = 299
1
0
0
1
0
1
0
1
1
1
0
1
0
0
1
DecodeBypass
ivlOffset = ivlOffset<<1 ivlOffset = ivlOffset | read_bits(1)
ivlOffset >= ivlCurrRange ?
ivlOffset = ivlOffset – ivlCurrRange
binVal = 1
binVal = 0
Done
1
Decoded bins:
No
Yes
0

## Slide 12: Background (continued)
However, when ivlCurrRange=256, the process can be significantly simplified:

## Slide 13: Worked Example: ivlCurrRange=256
bit-stream
ivlOffset = 189
0
1
0
1
1
1
1
0
1
1
1
0
1
0
1
DecodeBypass
ivlOffset = ivlOffset<<1 ivlOffset = ivlOffset | read_bits(1)
ivlOffset >= ivlCurrRange ?
ivlOffset = ivlOffset – ivlCurrRange
binVal = 1
binVal = 0
Done
?
Decoded bins:
No
Yes
8
7
6
5
4
3
2
1
0
Bit

## Slide 14: Worked Example: ivlCurrRange=256
bit-stream
ivlOffset = 189
0
1
0
1
1
1
1
0
1
1
1
0
1
0
1
DecodeBypass
ivlOffset = ivlOffset<<1 ivlOffset = ivlOffset | read_bits(1)
ivlOffset >= ivlCurrRange ?
ivlOffset = ivlOffset – ivlCurrRange
binVal = 1
binVal = 0
Done
?
Decoded bins:
No
Yes
Always 0
8
7
6
5
4
3
2
1
0
Bit

## Slide 15: Worked Example: ivlCurrRange=256
bit-stream
ivlOffset = 189
0
1
0
1
1
1
1
0
1
1
1
0
1
0
1
DecodeBypass
ivlOffset = ivlOffset<<1 ivlOffset = ivlOffset | read_bits(1)
Test bit 8 of ivlOffset
ivlOffset = ivlOffset – ivlCurrRange
binVal = 1
binVal = 0
Done
?
Decoded bins:
0
1
Always 0
8
7
6
5
4
3
2
1
0
Bit
NOTE: Since ivlOffset has been left-shifted by 1, the test/clear on bit 8 is equivalent to a test/clear on bit 7 in the above diagram.

## Slide 16: Worked Example: ivlCurrRange=256
bit-stream
ivlOffset = 189
0
1
0
1
1
1
1
0
1
1
1
0
1
0
1
DecodeBypass
ivlOffset = ivlOffset<<1 ivlOffset = ivlOffset | read_bits(1)
Test bit 8 of ivlOffset
Clear bit 8 of ivlOffset
binVal = 1
binVal = 0
Done
?
Decoded bins:
0
1
Always 0
8
7
6
5
4
3
2
1
0
Bit
NOTE: Since ivlOffset has been left-shifted by 1, the test/clear on bit 8 is equivalent to a test/clear on bit 7 in the above diagram.

## Slide 17: Worked Example: ivlCurrRange=256
bit-stream
ivlOffset = 189
0
1
0
1
1
1
1
0
1
1
1
0
1
0
1
DecodeBypass
ivlOffset = ivlOffset<<1 ivlOffset = ivlOffset | read_bits(1)
Test bit 8 of ivlOffset
binVal = ivlOffset bit 8
Clear bit 8 of ivlOffset
binVal = ivlOffset bit 8 Clear bit 8 of ivlOffset
Done
?
Decoded bins:
0
1
Always 0
8
7
6
5
4
3
2
1
0
Bit
NOTE: Since ivlOffset has been left-shifted by 1, the test/clear on bit 8 is equivalent to a test/clear on bit 7 in the above diagram.

## Slide 18: Worked Example: ivlCurrRange=256
bit-stream
ivlOffset = 189
0
1
0
1
1
1
1
0
1
1
1
0
1
0
1
DecodeBypass
ivlOffset = ivlOffset<<1 ivlOffset = ivlOffset | read_bits(1)
binVal = ivlOffset bit 8
Clear bit 8 of ivlOffset
Done
1
Decoded bins:
Always 0
8
7
6
5
4
3
2
1
0
Bit

## Slide 19: Worked Example: ivlCurrRange=256
bit-stream
ivlOffset = 189
0
1
0
1
1
1
1
0
1
1
1
0
1
0
1
DecodeBypass
binVal = ivlOffset bit 7
Clear bit 7 of ivlOffset
ivlOffset = ivlOffset<<1 ivlOffset = ivlOffset | read_bits(1)
Done
1
Decoded bins:
Always 0
8
7
6
5
4
3
2
1
0
Bit

## Slide 20: Worked Example: ivlCurrRange=256
bit-stream
ivlOffset = 189
0
1
0
1
1
1
1
0
1
1
1
0
1
0
1
DecodeBypass
Done
1
Decoded bins:
0
1
1
1
1
0
binVal = ivlOffset bit 7
Clear bit 7 of ivlOffset
ivlOffset = ivlOffset<<1 ivlOffset = ivlOffset | read_bits(1)

## Slide 21: Benefits When ivlCurrRange = 256
When ivlCurrRange = 256,
  The EP bins are directly visible in ivlOffset.
  N EP bins can be decoded just by looking at the N most-significant-but-one bits of ivlOffset concatenated with the bit-stream.
  Therefore, in this “aligned” case, decoding of EP bins is trivial.
  Throughput is now limited by bandwidth of buffer.
  Decoding of the worst case of a coefficient’s EP data should be possible within one stream operation.
    Decoding Exponential-Golomb bins just requires some simple logic to determine a shift on a shift register.
How best to achieve this state all of the time?

## Slide 22: Increase CABAC Throughput
Method 1
  The simple method to achieve this high throughput system is:
    Prior to EP bins (e.g. sign bits).
      Set ivlCurrRange = 256 (in encoder and decoder).
  This will waste (on average) 0.55 bits per alignment.
    When there is a large amount of bypass data, this loss is insignificant.

## Slide 23: Increase CABAC Throughput
Method 2
  To reduce the cost to ~0.30 bits per alignment, to align in the decoder:
    if (ivlCurrRange >= 384)
      if (ivlOffset < 256) nextEPBitIsZero = true
      else ivlOffset -= 128
    ivlCurrRange = 256
  This concept is developed further in the main document to reduce the loss, although this reduction is at the expense of implementation complexity.
    Method 2 is believed to be a reasonable trade-off.

## Slide 24: Refining the system
The alignment algorithm has been further refined over JCTVC-M0178 so that it can be used at higher QPs without a significant loss in coding efficiency.
The alignment algorithm is only employed if, for a given coefficient group, there are some non-sign bits that are bypass coded.
This means that for each group of 16 coefficients, the number of CABAC encoded bins is constrained:
  When alignment is used,
    16 (significant map) + 8 (>1 map) + 1 (>2 map) CABAC bins (Total of 25)
    + raw bypass bins
  When alignment is not used,
    16 (significant map) + 8 (>1 map) + 1 (>2 map) CABAC bins (Total of 25)
    + 16 CABAC EP bins (sign bits)

## Slide 25: Proposed System
The proposed system:
  Applies (Method 2) alignment prior to sign bit coding if there are some non sign bit bypass values to code
  The use of alignment is configured by a flag in the Sequence Parameter Set.
    This flag is not present for the Main profiles, and is inferred to be 0 (disabled) when not present.
  The alignment scheme could instead be selected by high bit-rate profiles/levels.

## Slide 26: Results
The conditional alignment has been analysed using the high bit depth operating points defined in N0188.
  The cost in BD-rates at target PSNRs are:
Although the proposal is not targeted at the standard RExt operating points, the results are shown below.

## Slide 27: Results
The proposal has also been tested using the AHG8 test conditions, as these are also high data rate scenarios, giving approximately a 0.4% bit rate loss:

## Slide 28: Conclusion
Throughput of CABAC at high bit depths and bit rates is a concern.
  There is significantly more data (CABAC EP bins) than at 8-bit operating points.
A method has been proposed to increase throughput.
  This causes the CABAC stream to be bit-aligned, allowing EP bins to be seen in ivlOffset as raw data.
  The alignment is only applied on a condition, which limits each group of 16-coefficients to:
    the number of CABAC-encoded bins to just 25, and
    either 16 EP sign bits, or raw escape data.
At the standard RExt intra conditions and standard AHG8 lossless conditions, 0.4% losses are observed.
At the high bit depth operating points, the overhead is less than 0.2%, which is negated by the gains shown in JCTVC-N0189.