## Slide 1: AHG5: 32x32 Scaling List Derivation for Chroma
JCTVC-N0192
Broadcast & Professional Research Labs
Sony Europe Ltd.
Karl Sharman
Sony Corp.

## Slide 2: Introduction
4:4:4 coding in HEVC RExt uses 32x32 chroma scaling lists.
Current working draft:
  does not specify the derivation of the 32x32 chroma scaling lists
Current software model:
  uses the luma 32x32 chroma scaling lists
  Has encoder option (not exercised) to define chroma 32x32 chroma scaling lists (but does not signal to the decoder)
This proposal is to suggest various possibilities.

## Slide 3: Scaling lists and syntax
The scaling lists are specified in the PPS.
  The 4x4 scaling lists are 16 syntax elements.
  Other scaling lists are 64 syntax elements, with sample repeat used to up-scale to the large dimensions.
The PPS does not know about the chroma format or profile
  These are specified in the SPS.
The PPS has an extension capability via the pps_extension_data_flag syntax element.
  But the specific method of creating extensions is not yet defined because HEVC V1 did not require them.

## Slide 4: 32x32 C Scaling List Method 1
Use the luma 32x32 scaling list for chroma
  Does not require any additional syntax.
  However, is the 32x32 chroma TU likely to be adaptively quantised in the same manner as the 32x32 luma TU?

## Slide 5: 32x32 C Scaling List Method 2
Use the PPS extension mechanism to define a 32x32 chroma 4:4:4 scaling list.
  What happens if the scaling list extension is not used?
    What is the fall-back position?
  Is the scaling list that different from others that have been defined?

## Slide 6: 32x32 C Scaling List Method 3
Use the chroma16x16 scaling list for chroma 32x32
  Does not require any additional syntax.
  It is proposed that the scaling lists from the same chrominance component but from the 16x16 size is likely to be similar/identical.

## Slide 7: Conclusion
3 different methods to define the 4:4:4 32x32 chroma scaling list have been presented.
It is proposed that the 32x32 chroma scaling lists are (by default) defined from the 16x16 chroma scaling lists.
  This does not prohibit the use of PPS extension data to define additional scaling lists, if the community believe that this overhead is warranted.