## Slide 1: [AHG16] JCTVC-N0202 - Key picture concept and single loop decoding
Christian Feldmann, Fabian Jäger, Mathias Wien
Notes: n: die Conclusions könnten noch knackiger werden. - Mach am besten bei den results auf einem einführungsslide noch klar, dass Du CTC für die Referenz hast, und was die mods für das Proposal sind (8:10:47 PM) mathias.wien: und die frage, wie man das signalisiert, sollten wir zumindest auf dem letzten Slide noch aufwerfen, vielleicht als TBD...

## Slide 2: 1 – Key Picture Concept
Key picture concept in SHM2.0
  1 Key picture per GOP (POC 0,8,…)
  BL key pictures:
    Use only other BL key pictures for inter prediction (POC -8,-16)
  BL non key pictures:
    Use EL reconstruction for inter prediction
    Use BL for TMVP
  Multi-loop decoding

## Slide 3: 1 – Results (vs. SHM2.0 CTC)
RA HEVC SNR |  |  | 
 | Y | U | V
Class A | -3,5% | -10,2% | -10,4%
Class B | -2,9% | -8,4% | -10,1%
Overall (Test vs Ref) | -3,1% | -8,9% | -10,2%
BL Drift |  |  | 
 | Y | U | V
Class A | 4,0% | 2,0% | 1,8%
Class B | 4,7% | 2,4% | 2,4%
Overall (Test vs Ref) | 4,5% | 2,3% | 2,2%
Class A | -0,17 dB | -0,04 dB | -0,03 dB
Class B | -0,12 dB | -0,03 dB | -0,04 dB
Overall (Test vs Ref) | -0,13 dB | -0,04 dB | -0,04 dB

## Slide 4: 2 – Key Picture Concept with Single Loop Decoding
Changes to support single loop decoding:
  Use unfiltered BL reference in EL
  Use constrained intra prediction in BL
  Only zero MV for BL prediction
Single loop decoding:
  Base layer Intra has to be decoded
  Base layer key pictures need to be decoded

## Slide 5: 2 – Results w/o BL Loop Filtering (vs. SHM2.0 CTC)
RA HEVC SNR |  |  | 
 | Y | U | V
Class A | 2,1% | -6,8% | -6,9%
Class B | 1,4% | -5,4% | -7,6%
Overall (Test vs Ref) | 1,6% | -5,8% | -7,4%
BL Drift |  |  | 
 | Y | U | V
Class A | 15,3% | 11,2% | 11,3%
Class B | 13,3% | 11,7% | 12,0%
Overall (Test vs Ref) | 13,9% | 11,5% | 11,8%
Class A | -0,61 dB | -0,23 dB | -0,21 dB
Class B | -0,34 dB | -0,15 dB | -0,19 dB
Overall (Test vs Ref) | -0,42 dB | -0,17 dB | -0,20 dB

## Slide 6: 2 – Results with Loop Filter for BL (vs. SHM2.0 CTC)
RA HEVC SNR |  |  | 
 | Y | U | V
Class A | 1,6% | -7,0% | -7,1%
Class B | 1,1% | -5,4% | -7,7%
Overall (Test vs Ref) | 1,2% | -5,8% | -7,5%
BL Drift |  |  | 
 | Y | U | V
Class A | 6,7% | 3,5% | 3,6%
Class B | 6,7% | 4,7% | 4,6%
Overall (Test vs Ref) | 6,7% | 4,4% | 4,3%
Class A | -0,28 dB | -0,07 dB | -0,07 dB
Class B | -0,17 dB | -0,06 dB | -0,08 dB
Overall (Test vs Ref) | -0,20 dB | -0,07 dB | -0,08 dB

## Slide 7: Summary and Conclusion
Use EL reconstruction for BL prediction
Drift when decoding BL  to be further studied
No low level changes
Multi-loop approach
  Increases EL performance (3% BD rate)
Single-loop decoding approach
  Performance loss 1.2% compared to SHM2.0 CTC
Proposal
  Study single-loop approach in CE
Thanks to InterDigital for cross checking