## Slide 1: JCTVC-N0206 Non-RCE3: Intra motion compensation with variable length intra MV coding
<number>
Do-Kyoung Kwon and Madhukar Budagavi
Texas Instruments Inc.
Notes: <number>

## Slide 2: Motivation
In screen content video, patterns (e.g. text characters, icons, lines etc.) can repeat within a picture
Intra motion compensation can code repeated patterns efficiently
<number>
- Repeated pattern (red) in screen content video

## Slide 3: Previous work (RCE3.3, JCTVC-N0205)
<number>
Intra motion compensation with fixed-length MV coding
  Either horizontal or vertical motion component is signaled
  Two encoder configs for search range
    Option 1: Horizontal and vertical motions are limited to -63 ~ 0
      Need to store 3 LCU lines
    Option 2: Horizontal motion is limited to -63 ~ 0, and vertical motion is limited so that a displaced block is included in the current LCU
      Need to store 2 left LCUs
  Absolute value of motion is always coded in 6 bits
current CU
Search
area
LCU
(64x64)
-63 – cuHeight
-cuHeight
-cuWidth
-63 - cuWidth
current CU
Search
area
-cuWidth
-63 - cuWidth
LCU
(64x64)
-cuHeight
- Search range, Option 1
- Search range, Option 2
Notes: <number>

## Slide 4: Proposed IntraMC
Intra motion compensation with variable-length MV coding
  Either horizontal or vertical motion component is signaled
  Horizontal motion is limited so that a displaced block does not go beyond 2 previous LCUs, and vertical motion is limited so that a displaced block is included in the current LCU
    Need to store 2 left LCUs
  Absolute value of motion is coded by the 3rd-order Exp-Golomb code
    Horizontal search range varies based on CU position and size
    Bigger search range for smaller CU compared with fixed-length MV coding
<number>
current CU
(16x16)
Search area
-cuWidth
LCU
(64x64)
-cuHeight
- Search range with variable length MV coding

## Slide 5: Experimental Results: Proposed vs. Rext-3.0 Anchor
<number>
- Lossy
- Lossless

## Slide 6: Experimental Results: Proposed vs. RCE3.3 Option 2 (3 LCU line buffer)
<number>
- Lossy
- Lossless

## Slide 7: Conclusions
The proposed intra MC provides significant coding gains in both lossless and lossy coding for screen content sequences
Friendly to the current HEVC architecture, so easy to be extended
Need to store 2 left LCUs additionally in the proposed method
More gain is expected by extending search ranges, etc.
<number>

## Slide 8: Experimental Results: Proposed (1 left LCU) vs. Rext-3.0 Anchor
<number>
- Lossy
- Lossless