## Slide 1: RCE1: EXP1/EXP4 The performance of extended chroma mode for non 4:2:0 format
B. Jeon
J. Kim
JCTVC-L0227

## Slide 2: Introduction
Intra chroma prediction : IntraFormLuma
  For HEVC, IntraFromLuma(LM chroma) mode was adopted as one of intra chroma prediction mode
  Principle of LM chroma for 4:2:0 sampling:
Chroma TU
: to be predicted
Luma TU
: reconstructed

## Slide 3: Proposed Method (I)
Extended intra chroma prediction mode for non 4:2:0 sampling
  We propose to use IntraFromLuma(LM chroma) mode for non 4:2:0 sampling
  Adaptation for 4:4:4 sampling (including RGB case)
    All luma samples are used
  Adaptation for 4:2:0 sampling
    Luma samples involved in the prediction are downsampled horizontally
    Above luma samples involved in the parameter derivation are downsampled horizontally
    Left luma samples involved in the parameter derivation are on
      EXP1) the corresponding column to the chroma sampling
      EXP4) the closest column to the block always

## Slide 4: Proposed Method (I) – EXP1&EXP4
  4:4:4 sampling
Chroma TU
: to be predicted
Luma TU
: reconstructed

## Slide 5: Proposed Method (I) – EXP1
  4:2:2 sampling
    Samples are predicted per each NxN transform block
    Left luma samples used to derive the parameters are on the closest column to the current block
Red circles indicate the locations of luma samples for prediction of chroma samples
Chroma TU
: to be predicted
Luma TU
: reconstructed

## Slide 6: Proposed Method (I) – EXP4
  4:2:2 sampling
    Left luma samples used to derive the parameters are on the 1 column left to the current block
Red circles indicate the locations of luma samples for prediction of chroma samples
Blue circles indicate the location of luma samples for derivation of parameters
Chroma TU
: to be predicted
Luma TU
: reconstructed

## Slide 7
Experimental Results in detail (I)
Performance of extended chroma intra prediction against HM-Range-extension10.1v3 –EXP1 (Main Tier)
 | All Intra Main-tier |  |  |  |  |  |  |  | 
 | Y | U | V | G psnr | B psnr | R psnr | psnrYUV | psnrGBR | psnrGBRm
RGB 4:4:4 | -17.4% | -22.1% | -27.9% | -19.7% | -17.9% | -18.7% | -18.8% | -18.8% | -18.6%
YCbCr 4:4:4 | -2.1% | -7.5% | -7.0% |  |  |  | -2.1% |  | 
YCbCr 4:2:2 | -1.8% | -5.6% | -4.4% |  |  |  | -1.8% |  | 
SC RGB 4:4:4 | -18.8% | -21.7% | -23.4% | -22.8% | -22.0% | -22.3% | -22.7% | -22.7% | -22.7%
SC YCbCr 4:4:4 | -6.0% | -8.1% | -7.0% |  |  |  | -6.1% |  | 
RExt | -7.5% | -12.2% | -13.8% | -19.7% | -17.9% | -18.7% | -8.1% | -18.8% | -18.6%
SC | -13.8% | -16.6% | -16.9% | -25.4% | -24.5% | -24.7% | -16.0% | -25.3% | -25.2%
Overall | -10.3% | -14.2% | -15.2% | -22.7% | -21.4% | -21.9% | -11.6% | -22.2% | -22.1%
Enc Time[%] | 115% |  |  |  |  |  |  |  | 
Dec Time[%] | #VALUE! |  |  |  |  |  |  |  | 
 | Random Access Main-tier |  |  |  |  |  |  |  | 
 | Y | U | V | G psnr | B psnr | R psnr | psnrYUV | psnrGBR | psnrGBRm
RGB 4:4:4 | -9.3% | -15.3% | -22.1% | -11.1% | -9.8% | -11.8% | -9.5% | -9.5% | -9.3%
YCbCr 4:4:4 | -0.9% | -7.7% | -5.6% |  |  |  | -0.9% |  | 
YCbCr 4:2:2 | -0.8% | -6.3% | -4.3% |  |  |  | -0.8% |  | 
SC RGB 4:4:4 | -9.4% | -13.4% | -16.1% | -17.8% | -17.1% | -17.3% | -17.7% | -17.7% | -17.7%
SC YCbCr 4:4:4 | -5.2% | -7.4% | -6.3% |  |  |  | -5.2% |  | 
RExt | -3.9% | -10.0% | -11.2% | -11.1% | -9.8% | -11.8% | -4.0% | -9.5% | -9.3%
SC | -8.4% | -12.0% | -13.0% | -20.0% | -19.2% | -19.4% | -13.4% | -19.9% | -19.9%
Overall | -5.7% | -10.8% | -11.9% | -15.6% | -14.5% | -15.6% | -7.8% | -14.7% | -14.6%
Enc Time[%] | 113% |  |  |  |  |  |  |  | 
Dec Time[%] | 130% |  |  |  |  |  |  |  | 
 | Low delay B Main-tier |  |  |  |  |  |  |  | 
 | Y | U | V | G psnr | B psnr | R psnr | psnrYUV | psnrGBR | psnrGBRm
RGB 4:4:4 | -3.2% | -7.2% | -11.2% | -4.2% | -3.5% | -4.5% | -2.9% | -2.9% | -2.8%
YCbCr 4:4:4 | -0.2% | -3.9% | -2.3% |  |  |  | -0.2% |  | 
YCbCr 4:2:2 | -0.3% | -3.9% | -2.8% |  |  |  | -0.3% |  | 
SC RGB 4:4:4 | -4.4% | -8.5% | -11.5% | -14.1% | -13.2% | -13.4% | -13.7% | -13.7% | -13.7%
SC YCbCr 4:4:4 | -3.4% | -5.3% | -4.5% |  |  |  | -3.5% |  | 
RExt | -1.3% | -5.1% | -5.7% | -4.2% | -3.5% | -4.5% | -1.2% | -2.9% | -2.8%
SC | -4.5% | -7.9% | -9.3% | -15.8% | -14.9% | -15.0% | -10.1% | -15.4% | -15.4%
Overall | -2.6% | -6.2% | -7.2% | -10.0% | -9.2% | -9.8% | -4.8% | -9.1% | -9.1%
Enc Time[%] | 113% |  |  |  |  |  |  |  | 
Dec Time[%] | 140% |  |  |  |  |  |  |  | 

## Slide 8
Experimental Results in detail (I)
Performance of extended chroma intra prediction against HM-Range-extension10.1v3 –EXP1 (High Tier)
All Intra High-tier |  |  |  |  |  |  |  | 
Y | U | V | G psnr | B psnr | R psnr | psnrYUV | psnrGBR | psnrGBRm
-13.6% | -16.9% | -22.0% | -15.4% | -14.4% | -15.0% | -15.0% | -15.0% | -15.0%
-2.3% | -4.8% | -6.3% |  |  |  | -2.2% |  | 
-1.5% | -2.9% | -2.8% |  |  |  | -1.5% |  | 
-20.3% | -23.0% | -24.3% | -21.7% | -20.9% | -21.1% | -21.6% | -21.6% | -21.7%
-5.9% | -6.5% | -5.8% |  |  |  | -5.9% |  | 
-6.2% | -8.6% | -10.9% | -15.4% | -14.4% | -15.0% | -6.6% | -15.0% | -15.0%
-15.3% | -17.3% | -17.7% | -24.4% | -23.5% | -23.7% | -16.1% | -24.4% | -24.4%
-9.9% | -12.1% | -13.6% | -19.9% | -19.0% | -19.4% | -10.5% | -19.7% | -19.7%
115% |  |  |  |  |  |  |  | 
#VALUE! |  |  |  |  |  |  |  | 
Random Access High-tier |  |  |  |  |  |  |  | 
Y | U | V | G psnr | B psnr | R psnr | psnrYUV | psnrGBR | psnrGBRm
-6.3% | -8.8% | -17.1% | -7.9% | -6.3% | -8.5% | -6.7% | -6.7% | -6.5%
-0.9% | -5.2% | -5.0% |  |  |  | -0.9% |  | 
-0.7% | -2.8% | -2.8% |  |  |  | -0.7% |  | 
-16.3% | -19.5% | -20.8% | -18.1% | -17.4% | -17.5% | -18.0% | -18.0% | -18.0%
-5.3% | -6.8% | -6.1% |  |  |  | -5.4% |  | 
-2.8% | -5.7% | -8.7% | -7.9% | -6.3% | -8.5% | -2.9% | -6.7% | -6.5%
-12.6% | -15.3% | -15.8% | -20.4% | -19.6% | -19.7% | -13.7% | -20.3% | -20.3%
-6.8% | -9.6% | -11.6% | -14.1% | -12.9% | -14.1% | -7.3% | -13.5% | -13.4%
116% |  |  |  |  |  |  |  | 
127% |  |  |  |  |  |  |  | 
Low delay B High-tier |  |  |  |  |  |  |  | 
Y | U | V | G psnr | B psnr | R psnr | psnrYUV | psnrGBR | psnrGBRm
-2.1% | -3.3% | -7.9% | -2.9% | -2.0% | -3.0% | -2.0% | -2.0% | -2.0%
-0.2% | -2.2% | -1.9% |  |  |  | -0.2% |  | 
-0.3% | -1.4% | -1.7% |  |  |  | -0.3% |  | 
-12.0% | -14.8% | -16.1% | -14.2% | -13.5% | -13.5% | -14.0% | -14.0% | -14.0%
-4.2% | -5.3% | -5.0% |  |  |  | -4.2% |  | 
-0.9% | -2.4% | -4.0% | -2.9% | -2.0% | -3.0% | -0.9% | -2.0% | -2.0%
-9.4% | -11.7% | -12.3% | -16.0% | -15.2% | -15.2% | -10.7% | -15.8% | -15.8%
-4.4% | -6.1% | -7.4% | -9.4% | -8.6% | -9.1% | -4.9% | -8.9% | -8.9%
116% |  |  |  |  |  |  |  | 
135% |  |  |  |  |  |  |  | 

## Slide 9
Experimental Results in detail (II)
Performance of extended chroma intra prediction against HM-Range-extension10.1v3 –EXP4 (Main Tier)
 | All Intra Main-tier |  |  |  |  |  |  |  | 
 | Y | U | V | G psnr | B psnr | R psnr | psnrYUV | psnrGBR | psnrGBRm
RGB 4:4:4 | -17.4% | -22.1% | -27.9% | -19.7% | -17.9% | -18.7% | -18.8% | -18.8% | -18.6%
YCbCr 4:4:4 | -2.1% | -7.5% | -7.0% |  |  |  | -2.1% |  | 
YCbCr 4:2:2 | -1.6% | -5.2% | -4.1% |  |  |  | -1.7% |  | 
SC RGB 4:4:4 | -18.8% | -21.7% | -23.4% | -22.8% | -22.0% | -22.3% | -22.7% | -22.7% | -22.7%
SC YCbCr 4:4:4 | -6.0% | -8.1% | -7.0% |  |  |  | -6.1% |  | 
RExt | -7.5% | -12.1% | -13.7% | -19.7% | -17.9% | -18.7% | -8.0% | -18.8% | -18.6%
SC | -13.8% | -16.6% | -16.9% | -25.4% | -24.5% | -24.7% | -16.0% | -25.3% | -25.2%
Overall | -10.3% | -14.1% | -15.1% | -22.7% | -21.4% | -21.9% | -11.6% | -22.2% | -22.1%
Enc Time[%] | 115% |  |  |  |  |  |  |  | 
Dec Time[%] | #VALUE! |  |  |  |  |  |  |  | 
 | Random Access Main-tier |  |  |  |  |  |  |  | 
 | Y | U | V | G psnr | B psnr | R psnr | psnrYUV | psnrGBR | psnrGBRm
RGB 4:4:4 | -9.3% | -15.3% | -22.1% | -11.1% | -9.8% | -11.8% | -9.5% | -9.5% | -9.3%
YCbCr 4:4:4 | -0.9% | -7.7% | -5.6% |  |  |  | -0.9% |  | 
YCbCr 4:2:2 | -0.7% | -5.8% | -3.9% |  |  |  | -0.7% |  | 
SC RGB 4:4:4 | -9.4% | -13.4% | -16.1% | -17.8% | -17.1% | -17.3% | -17.7% | -17.7% | -17.7%
SC YCbCr 4:4:4 | -5.2% | -7.4% | -6.3% |  |  |  | -5.2% |  | 
RExt | -3.9% | -9.9% | -11.1% | -11.1% | -9.8% | -11.8% | -4.0% | -9.5% | -9.3%
SC | -8.4% | -12.0% | -13.0% | -20.0% | -19.2% | -19.4% | -13.4% | -19.9% | -19.9%
Overall | -5.7% | -10.7% | -11.9% | -15.6% | -14.5% | -15.6% | -7.8% | -14.7% | -14.6%
Enc Time[%] | 113% |  |  |  |  |  |  |  | 
Dec Time[%] | 148% |  |  |  |  |  |  |  | 
 | Low delay B Main-tier |  |  |  |  |  |  |  | 
 | Y | U | V | G psnr | B psnr | R psnr | psnrYUV | psnrGBR | psnrGBRm
RGB 4:4:4 | -3.2% | -7.2% | -11.2% | -4.2% | -3.5% | -4.5% | -2.9% | -2.9% | -2.8%
YCbCr 4:4:4 | -0.2% | -3.9% | -2.3% |  |  |  | -0.2% |  | 
YCbCr 4:2:2 | -0.3% | -3.6% | -2.6% |  |  |  | -0.3% |  | 
SC RGB 4:4:4 | -4.4% | -8.5% | -11.5% | -14.1% | -13.2% | -13.4% | -13.7% | -13.7% | -13.7%
SC YCbCr 4:4:4 | -3.4% | -5.3% | -4.5% |  |  |  | -3.5% |  | 
RExt | -1.3% | -5.0% | -5.6% | -4.2% | -3.5% | -4.5% | -1.2% | -2.9% | -2.8%
SC | -4.5% | -7.9% | -9.3% | -15.8% | -14.9% | -15.0% | -10.1% | -15.4% | -15.4%
Overall | -2.6% | -6.2% | -7.1% | -10.0% | -9.2% | -9.8% | -4.8% | -9.1% | -9.1%
Enc Time[%] | 113% |  |  |  |  |  |  |  | 
Dec Time[%] | 160% |  |  |  |  |  |  |  | 

## Slide 10
Experimental Results in detail (II)
Performance of extended chroma intra prediction against HM-Range-extension10.1v3 –EXP4 (High Tier)
All Intra High-tier |  |  |  |  |  |  |  | 
Y | U | V | G psnr | B psnr | R psnr | psnrYUV | psnrGBR | psnrGBRm
-13.6% | -16.9% | -22.0% | -15.4% | -14.4% | -15.0% | -15.0% | -15.0% | -15.0%
-2.3% | -4.8% | -6.3% |  |  |  | -2.2% |  | 
-1.4% | -2.7% | -2.6% |  |  |  | -1.4% |  | 
-20.3% | -23.0% | -24.3% | -21.7% | -20.9% | -21.1% | -21.6% | -21.6% | -21.7%
-5.9% | -6.5% | -5.8% |  |  |  | -5.9% |  | 
-6.1% | -8.5% | -10.8% | -15.4% | -14.4% | -15.0% | -6.6% | -15.0% | -15.0%
-15.3% | -17.3% | -17.7% | -24.4% | -23.5% | -23.7% | -16.1% | -24.4% | -24.4%
-9.9% | -12.1% | -13.6% | -19.9% | -19.0% | -19.4% | -10.5% | -19.7% | -19.7%
116% |  |  |  |  |  |  |  | 
#VALUE! |  |  |  |  |  |  |  | 
Random Access High-tier |  |  |  |  |  |  |  | 
Y | U | V | G psnr | B psnr | R psnr | psnrYUV | psnrGBR | psnrGBRm
-6.3% | -8.8% | -17.1% | -7.9% | -6.3% | -8.5% | -6.7% | -6.7% | -6.5%
-0.9% | -5.2% | -5.0% |  |  |  | -0.9% |  | 
-0.6% | -2.5% | -2.6% |  |  |  | -0.6% |  | 
-16.3% | -19.5% | -20.8% | -18.1% | -17.4% | -17.5% | -18.0% | -18.0% | -18.0%
-5.3% | -6.8% | -6.1% |  |  |  | -5.4% |  | 
-2.8% | -5.6% | -8.6% | -7.9% | -6.3% | -8.5% | -2.9% | -6.7% | -6.5%
-12.6% | -15.3% | -15.8% | -20.4% | -19.6% | -19.7% | -13.7% | -20.3% | -20.3%
-6.8% | -9.6% | -11.5% | -14.1% | -12.9% | -14.1% | -7.3% | -13.5% | -13.4%
116% |  |  |  |  |  |  |  | 
145% |  |  |  |  |  |  |  | 
Low delay B High-tier |  |  |  |  |  |  |  | 
Y | U | V | G psnr | B psnr | R psnr | psnrYUV | psnrGBR | psnrGBRm
-2.1% | -3.3% | -7.9% | -2.9% | -2.0% | -3.0% | -2.0% | -2.0% | -2.0%
-0.2% | -2.2% | -1.9% |  |  |  | -0.2% |  | 
-0.3% | -1.3% | -1.6% |  |  |  | -0.2% |  | 
-12.0% | -14.8% | -16.1% | -14.2% | -13.5% | -13.5% | -14.0% | -14.0% | -14.0%
-4.2% | -5.3% | -5.0% |  |  |  | -4.2% |  | 
-0.9% | -2.3% | -4.0% | -2.9% | -2.0% | -3.0% | -0.9% | -2.0% | -2.0%
-9.4% | -11.7% | -12.3% | -16.0% | -15.2% | -15.2% | -10.7% | -15.8% | -15.8%
-4.4% | -6.1% | -7.4% | -9.4% | -8.6% | -9.1% | -4.8% | -8.9% | -8.9%
116% |  |  |  |  |  |  |  | 
155% |  |  |  |  |  |  |  | 

## Slide 11: Conclusion
We proposed including of extended intra chroma prediction (LM chroma mode) for non 4:2:0 sampling
We tested two sampling position of luma samples to derive the parameters
  EXP1 : most closest left column to the current block
  EXP4 : one column left from the current block