## Slide 1: Non-SCE3: Region based Inter-layer Cross-Color Filtering (JCTVC-N0229)
X. Li, W. Pu, J. Chen, M. Karczewicz (Qualcomm Inc.)
E. Alshina, A. Alshin, Y. Cho (Samsung Eletronics, Ltd)

## Slide 2: Overview
Region based inter-layer cross-color filtering is proposed on top of SCE3.4.2 (JCTVC-N0152)
  An inter-layer reference picture is adaptively partitioned into multiple (1, 4, or 16) regions in a quad-tree manner. Each region has its own inter-layer cross-color filter parameters
  8-point inter-layer cross-color filter as proposed in JCTVC-M0253
Simulation results and discussions
  Doubled coding gain compared to SCE3.4.2
  Similar memory access to that of SCE3.4.2
  Lower computational complexity compared to SCE3.4.2
Conclusions
Thanks Canon for crosschecking (JCTVC-N0311)

## Slide 3: Region based Inter-layer Cross-color Filtering
An inter-layer reference picture is adaptively partitioned into multiple (1, 4, or 16) regions in a quad-tree manner. Each region has its own inter-layer cross-color filter parameters – Better local adaptivity

## Slide 4: Proposed 8-poing Cross-shaped Filter
  Method in SCE3.4.2 (JCTVC-N0152)
  13 multiplications and 12 additions per chroma pixel
Proposed method (as in JCTVC-M0253)
    9 multiplications and 8 additions per chroma pixel
  Lower complexity in deriving filter parameters for one region
  Lower computational complexity at decoder

## Slide 5: R-D Performance
 | No partition (SCE3.4.2) |  |  | Up to 4 regions |  |  | Up to 16 regions |  |  | Up to 64 regions |  | 
 | Y | U | V | Y | U | V | Y | U | V | Y | U | V
AI | -0.8% | -7.5% | -8.5% | -1.2% | -8.9% | -18.5% | -1.4% | -11.1% | -22.0% | -1.3% | -11.7% | -22.2%
RA | -0.4% | -9.2% | -9.1% | -0.6% | -11.0% | -20.1% | -0.6% | -13.5% | -23.4% | -0.6% | -14.1% | -23.8%
LD-B | -0.2% | -7.1% | -7.5% | -0.4% | -8.7% | -16.8% | -0.3% | -10.1% | -18.9% | -0.3% | -10.2% | -18.8%
LD-P | -0.2% | -6.5% | -6.9% | -0.4% | -8.1% | -15.7% | -0.3% | -9.5% | -17.9% | -0.3% | -9.8% | -17.5%
Avg. | -0.4% | -7.6% | -8.0% | -0.6% | -9.2% | -17.8% | -0.7% | -11.0% | -20.6% | -0.6% | -11.5% | -20.6%
“Up to 16 regions” shows best tradeoff between coding performance and complexity

## Slide 6: Conclusions
Region based inter-layer cross-color filtering is proposed on top of SCE3.4.2 (JCTVC-N0152)
  No latency issue
  An inter-layer reference picture is adaptively partitioned into multiple (1, 4, or 16) regions
    Max region number may be level related
    Up to 16 regions for CTC
  8-point inter-layer cross-color filter
  14-bit shift instead of 16-bit shift in scaling process
Significant coding efficiency improvement by the proposed method is observed