## Slide 1
JCTVC-N0231
AHG 8: Intra mode coding for screen contents
Junghye Min,
Sunil Lee, Chanyul Kim

## Slide 2: Summary
Simplified intra mode coding method for screen contents is proposed.
    Intra modes from neighboring PUs are not considered to derive most probable modes.
Performance (AI )
 | Lossless | Lossy (Y,U,V)
SC RGB 444 | -0.7% | -1.0%/-0.8%/-0.8%
SC YUV 444 | -0.7% | -0.2%/-0.3%/-0.3%

## Slide 3: Introductions -1
Derivation process of most probable modes in the HM-10.1+RExt-3.0 is complicated.
Real time encoding/decoding is critical issue for screen contents coding.
Derivation process of
Most probable modes in
HM 10.1

## Slide 4: Introductions-2
One of characteristics of screen contents is correlation of patterns along horizontal and vertical directions.

## Slide 5: Proposed method
Without referring to neighbouring prediction units, three most probable modes MPM0, MPM1 and MPM2 are set as follows.
      MPM0 = INTRA_HOR
      MPM1 = INTRA_VER
      MPM2 = INTRA_ANGULAR_18

## Slide 6: Experimental results
Lossless
Max : pcb-layout (AI, -2.05%)
Lossy
Max: pcp-layout
(AI-2.5% -1.6% -1.7% )
 | All Intra HE Main-tier |  |  | All Intra HE High-tier |  |  | All Intra HE Super-High-tier |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class F | 0.4% | 0.1% | 0.1% | 0.4% | 0.3% | 0.3% | 0.4% | 0.3% | 0.4%
Class B | 1.8% | 0.6% | 0.6% | 1.2% | 0.7% | 0.8% | 0.7% | 0.6% | 0.7%
SC RGB 444 | -1.0% | -0.8% | -0.8% | -0.9% | -0.8% | -0.7% | -0.9% | -0.7% | -0.7%
SC YUV 444 | -0.2% | -0.3% | -0.3% | -0.1% | -0.3% | -0.2% | -0.1% | -0.2% | -0.1%
RangeExt | 1.4% | 0.8% | 0.8% | 0.8% | 0.5% | 0.6% | 0.5% | 0.4% | 0.4%
Enc Time[%] | 104% |  |  | 105% |  |  | 105% |  | 
Dec Time[%] | 100% |  |  | 100% |  |  | 100% |  | 
 | Random Access HE Main-tier |  |  | Random Access HE High-tier |  |  |  |  | 
 | Y | U | V | Y | U | V |  |  | 
Class F | 0.1% | -0.1% | -0.1% | 0.1% | 0.0% | 0.0% |  |  | 
Class B | 0.8% | 0.3% | 0.0% | 0.6% | 0.4% | 0.3% |  |  | 
SC RGB 444 | -1.0% | -0.8% | -0.8% | -0.9% | -0.7% | -0.7% |  |  | 
SC YUV 444 | -0.3% | -0.4% | -0.3% | -0.2% | -0.2% | -0.2% |  |  | 
RangeExt | 0.7% | 0.4% | 0.2% | 0.4% | 0.2% | 0.3% |  |  | 
Enc Time[%] | 101% |  |  | 101% |  |  |  |  | 
Dec Time[%] | 101% |  |  | 101% |  |  |  |  | 
 | Low delay B HE Main-tier |  |  | Low delay B HE High-tier |  |  |  |  | 
 | Y | U | V | Y | U | V |  |  | 
Class F | -0.4% | -0.4% | -0.5% | -0.1% | -0.1% | -0.2% |  |  | 
Class B | 0.2% | 0.1% | 0.0% | 0.1% | 0.1% | 0.1% |  |  | 
SC RGB 444 | -0.7% | -0.4% | -0.5% | -1.1% | -0.8% | -0.7% |  |  | 
SC YUV 444 | -0.5% | -0.2% | -0.5% | -0.5% | -0.4% | -0.4% |  |  | 
RangeExt | 0.4% | 0.2% | 0.1% | 0.2% | 0.1% | 0.2% |  |  | 
Enc Time[%] | 101% |  |  | 101% |  |  |  |  | 
Dec Time[%] | 104% |  |  | 103% |  |  |  |  | 
 | All Intra Main |  |  | Random Access Main |  |  | Low delay B Main |  | 
 | compression ratio |  | Bit-rate saving | compression ratio |  | Bit-rate saving | compression ratio |  | Bit-rate saving
 | Reference | Tested |  | Reference | Tested |  | Reference | Tested | 
Class F | 5.2 | 5.3 | -0.3% | 31.7 | 31.8 | -0.2% | 49.8 | 49.8 | -0.2%
Class B | 2.2 | 2.2 | -0.1% | 2.6 | 2.6 | 0.1% | 2.6 | 2.6 | 0.1%
SC RGB 444 | 10.1 | 10.1 | -0.7% | 100.4 | 101.2 | -0.4% | 381.6 | 384.7 | -0.5%
SC YUV 444 | 11.4 | 11.5 | -0.7% | 128.9 | 130.0 | -0.6% | 325.6 | 328.0 | -0.4%
RangeExt | 2.4 | 2.4 | 0.0% | 2.5 | 2.5 | 0.0% | 2.5 | 2.5 | 0.0%
Enc Time[%] | 100% |  |  | 102% |  |  | 102% |  | 
Dec Time[%] | 95% |  |  | 95% |  |  | 95% |  | 

## Slide 7: Conclusions
Proposed simplified intra mode coding method for screen contents.
Derivation process of most probable modes using neighboring intra modes was removed.
Provides gains of
  -0.7% for lossless
- -1.0%/-0.8%/-0.8% for lossy AI tests.
We would like to thank BBC Research & Development for the crosscheck of this proposal.

## Slide 8
Thank you !