## Slide 1: HLS: Extensions of motion-constrained tile sets SEI message for interactivity
Cheung Auyeung, Jun Xu
Sony Electronics Inc.
July 24, 2013

## Slide 2: Introduction to Tiled Streaming
Provide ROI that each user wants.
User selects ROI interactively
User selects ROI interactively

## Slide 3: Introduction to Tiled Streaming
All tiles are independently
decodable
User selects ROI interactively
User selects ROI interactively
Different user may want different ROI.

## Slide 4: Introduction to Tiled Streaming
All tiles are independently
decodable
User selects ROI interactively
User selects ROI interactively
Avoid CTU level transcoding
Avoid CTU level transcoding
Need to reduce complexity to serve all users.

## Slide 5: Properties for Tiled Streaming
All tiles are independently decodable (motion-constrained tiles).
The region of interests is not necessary determined at the beginning of the encode time of a CVS.
Once the region of interests are encoded in a CVS, they can be modified based on user interactivity without re-encoding the CVS at the CTU level.

## Slide 6: Current Limitation in MCTS SEI
The current motion-constrained tile sets (MCTS) SEI can be used to signal the location of independently decodable ROI.
But in general, it cannot signal the followings at the same time:
  All tiles are independently decodable
  The locations of the ROIs
Propose addition to MCTS to support all tiles are independently decodable and to signal the locations of the ROIs.

## Slide 7: Proposed MCTS Syntax
all_tiles_exact_sample_value_match_flag
  Similar to the definition of exact_sample_value_match_flag for a motion-constrained tile set, but apply to every tile.
motion_constrained_tile_sets( payloadSize ) { | Descriptor
all_tiles_exact_sample_value_match_flag | u(1)
num_sets_in_message_minus1 | ue(v)
for( i = 0; i <= num_sets_in_message_minus1; i++) { | 
mcts_id[ i ] | ue(v)
num_tile_rects_in_set_minus1[ i ] | ue(v)
for( j = 0; j <= num_tile_rects_in_set_minus1[ i ]; j++) { | 
top_left_tile_index[ i ][ j ] | ue(v)
bottom_right_tile_index[ i ][ j ] | ue(v)
} | 
if( ! all_tiles_exact_sample_value_match_flag) { | 
exact_sample_value_match_flag[ i ] | u(1)
} | 
} | 
} | 

## Slide 8: Conclusions
Proposed additions to MCTS SEI message to support tiled streaming:
  Signal the locations of the ROIs
  All tiles are independently decodable.
Propose to be adopted to an HEVC extension.