## Slide 1: SCE2 test 2.3 motion buffer modification results
Kiran Misra, Andrew Segall, Jie Zhao
(JCTVC-N0252)

## Slide 2: Background
In JCTVC-M0258
  During the motion mapping process, we propose to use motion information from a candidate enhancement layer motion field instead of the motion field mapped from the base layer when: (i) the candidate enhancement layer is valid and (ii) the candidate enhancement layer does not reference its own baselayer
Tested in SCE2 (single tool test 2.3)

## Slide 3: Proposed change
To the right is an illustration of EL motion data selectively replacing mapped BL motion data within the resampled motion storage buffer.
The EL motion data is selected only if it is valid (e.g. not intra) and if it does not reference its own BL.
The EL motion data reference picture list is selected as in HEVC, based on reference picture list status.

## Slide 4: Experimental Results
Anchor: SHM-2.0 reference index framework
Average luma BD rate
Syntax, semantics and decoding process changes included in contribution document
 | EL+BL |  | 
 | 2x | 1.5x | SNR
All-intra | 0.0% | 0.0% | 
Random access | -0.5% | -0.2% | -0.2%
Low delay B | 0.0% | 0.0% | 0.0%
Low delay P | 0.0% | 0.0% | 0.0%
Cross-check: JCTVC-N0122 (Thanks to ETRI)

## Slide 5: Complexity
Worst Case Complexity Analysis
  Addition of two slice level checks
    Is tool enabled?
    Is low delay condition true?
  Addition of following block level checks
    Is enhancement layer INTER?
    Does enhancement layer reference it’s baselayer
    Is delta POC in reference picture list?
    Is RPL length maximum?
    Each performed for list L0/L1
Is Enhancement
Layer INTER?
Does
EL reference
its BL?
Is deltaPOC
in reference picture
list?
Add deltaPOC
to RPL
Use upscaled
base layer motion
N
Y
Y
Use enhancement
layer motion
N
Is RPL length
maximum?
Scale enhancement layer
motion to first picture in RPL
JCTVC-N0233
Y
N
N

## Slide 6: Complexity
Discussion
  On “Is delta POC in referenced picture list?”
    During our last presentation, there was a question about the complexity of this test
    One solution is to search the list to see if the deltaPOC is present. In the worst case, this could be approximately 15 compares
    However, this can be implemented much more efficiently
      Pre-compute the availability of each delta POC for a slice (the RPL of the upsampled frame and candidate enhancement layer are known)
      The test then becomes a look up operation

## Slide 7: Run Times
Run Times
  Decoder performance 99.9% to 101.7% of SHM2.0
  Encoder performance 98.9% and 101.4% of SHM2.0

## Slide 8: Worst-case memory access
Worst case memory bandwidth
  Less than 0.5% increase in memory bandwidth (worst case)

## Slide 9: Worst-case memory access
Based on JCTVC-M0455 excel, with single layer HEVC as anchor.
SHM-2.0: 10 bytes per 16x16 region (JCTVC-M0455)
  200.20% (PU based/Pic based pointer) and 218.31% (Pic based copy) of single layer HEVC
Proposed: 20 bytes per 16x16 region
  200.40% (PU based/Pic based pointer) and 218.51% (Pic based copy) of single layer HEVC

## Slide 10: Conclusion
The resampled motion field buffer update mechanism using enhancement layer and reference layer motion information was proposed and tested in SCE2 (test 2.3).
The proposed changes achieve the following average luma BD rate improvements with SHM-2.0 reference index framework as anchors:
0.0%/0.0% (AI 2x/AI 1.5x)
-0.5%/-0.2%/-0.2% (RA 2x/RA 1.5x/RA SNR)
0.0%/0.0%/0.0% (LDB 2x/LDB 1.5x/LDB SNR)
0.0%/0.0%/0.0% (LDP 2x/LDP 1.5x/LDP SNR)
Recommend: Adopt to SHVC test model and working draft

## Slide 12: Additional Information
A note on motion field mapping performance
  Originally proposed in JCTVC-L0366
  Gains biased toward random access
  We observe similar performance with LD-P and LD-B
JCTVC-L0366