## Slide 1: Pipeline Friendly Intra Motion Compensation JCTVC-N0254
Chao Pang, Joel Sole, Liwei Guo, Marta Karczewicz, Rajan Joshi

## Slide 2: Introduction
Intra motion compensation (MC)
  As in JCTVC-N0205 (RCE3) and N0206
Current CU
Prediction
Current CTU
Left CTU
Left Left CTU

## Slide 3: Issues and Proposed Solutions
Issues in JCTVC-N0205
  Need to buffer 2 left CTUs
    Additional large buffer for the pre-filtered reconstructed samples
  Complexity and memory bandwidth increase due to interpolation filter
    Padding is performed when the neighboring pixels are not available
    Pixels from other CTUs might be used for the interpolation
  Fixed-length codes (0..63) of MV lead to limited search points
    Not flexible to allow for the signaling of all the positions in the search area
  A solution for each issue is proposed:
  Search area restriction
  Removal of interpolation filter
  Exponential-Golomb codes for MV coding

## Slide 4: (1) Search Area Restriction
Restriction 1: current CTU + left CTU
Restriction 2: current CTU + left 4 Columns
  Left 4 columns of current CTU are already buffered for the filtering process
Current CU
Prediction
Current CTU
Left CTU
Left Left CTU
Current CU
Prediction
Current CTU
Left CTU

## Slide 5: (2) Removal of Interpolation Filter
Interpolation process is removed from the intra prediction MC
  Integer-pixel resolution is used for both luma and chroma components
  For 4:2:0 and 4:2:2 color formats, rounding is applied to get the integer-pixel MV for chroma components

## Slide 6: (3) Improved MV Binarization
  Exponential-Golomb codes for MV coding
  An exponential-Golomb code with parameter 3 is used
  Allows signaling of all the positions within the search area

## Slide 7: Experimental Results
Results are provided step-by-step to assess the impact of each change:
  Interpolation filter ON vs. OFF
    Setting: with fixed length MV and search area restricted to the left CTU
  Exponential-Golomb vs. Fixed length
    Setting: without the interpolation filter and search area restricted to the left CTU
  Restriction of the search area
    2 left CTUs vs. 1 left CTU vs. 4 columns in the left CTU
    Setting: without the interpolation filter and with exponential-Golomb binarization

## Slide 8: Interpolation filter ON vs OFF (lossless)
 | All Intra Main |  |  | Random Access Main |  |  | Low delay B Main |  | 
 | compression ratio |  |  | compression ratio |  |  | compression ratio |  | 
 | Reference | Tested |  | Reference | Tested |  | Reference | Tested | 
Class F | 5.4 | 5.4 | 0.1% | 32.7 | 32.7 | 0.0% | 50.6 | 50.5 | 0.0%
Class B | 2.2 | 2.2 | 0.0% | 2.6 | 2.6 | 0.0% | 2.6 | 2.6 | 0.0%
SC RGB 444 | 14.1 | 14.1 | 0.0% | 142.8 | 142.8 | 0.0% | 555.2 | 555.2 | 0.0%
SC YUV 444 | 16.7 | 16.7 | 0.0% | 187.0 | 187.0 | 0.0% | 508.8 | 508.8 | 0.0%
RangeExt | 2.4 | 2.4 | 0.0% | 2.5 | 2.5 | 0.0% | 2.5 | 2.5 | 0.0%
Enc Time[%] | 103% |  |  | 103% |  |  | 98% |  | 
Dec Time[%] | 94% |  |  | 99% |  |  | 100% |  | 

## Slide 9: Interpolation filter ON vs OFF (lossy)
 | All Intra HE Main-tier |  |  | All Intra HE High-tier |  |  | All Intra HE Super-High-tier |  |  | 
 | Y | U | V | Y | U | V | Y |  | U | V
Class F | 0.3% | 0.3% | 0.1% | 0.3% | 0.3% | 0.1% | 0.3% |  | 0.2% | 0.2%
Class B | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% |  | 0.0% | 0.0%
SC RGB 444 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% |  | 0.0% | 0.0%
SC YUV 444 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% |  | 0.0% | 0.0%
RangeExt | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% |  | 0.0% | 0.0%
Enc Time[%] | 101% |  |  | 101% |  |  | 100% |  |  | 
Dec Time[%] | 99% |  |  | 99% |  |  | 99% |  |  | 
 | Random Access HE Main-tier |  |  | Random Access HE High-tier |  |  |  |  |  | 
 | Y | U | V | Y | U | V |  |  |  | 
Class F | 0.2% | 0.2% | 0.0% | 0.2% | 0.1% | 0.2% |  |  |  | 
Class B | 0.0% | -0.1% | -0.1% | 0.0% | 0.0% | 0.1% |  |  |  | 
SC RGB 444 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% |  |  |  | 
SC YUV 444 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% |  |  |  | 
RangeExt | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% |  |  |  | 
Enc Time[%] | 100% |  |  | 100% |  |  |  |  |  | 
Dec Time[%] | 96% |  |  | 97% |  |  |  |  |  | 
 | Low delay B HE Main-tier |  |  | Low delay B HE High-tier |  |  |  |  |  | 
 | Y | U | V | Y | U | V |  |  |  | 
Class F | 0.1% | 0.2% | 0.0% | 0.1% | 0.2% | 0.1% |  |  |  | 
Class B | 0.0% | 0.1% | -0.2% | 0.0% | -0.1% | -0.2% |  |  |  | 
SC RGB 444 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% |  |  |  | 
SC YUV 444 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% |  |  |  | 
RangeExt | 0.0% | 0.1% | -0.1% | 0.0% | 0.0% | -0.1% |  |  |  | 
Enc Time[%] | 100% |  |  | 102% |  |  |  |  |  | 
Dec Time[%] | 97% |  |  | 98% |  |  |  |  |  | 

## Slide 10: Exponential-Golomb MV vs. Fixed length MV (lossless)
 | All Intra Main |  |  | Random Access Main |  |  | Low delay B Main |  | 
 | compression ratio |  |  | compression ratio |  |  | compression ratio |  | 
 | Reference | Tested |  | Reference | Tested |  | Reference | Tested | 
Class F | 5.4 | 5.4 | -0.3% | 32.7 | 32.8 | -0.1% | 50.5 | 50.6 | -0.1%
Class B | 2.2 | 2.2 | 0.0% | 2.6 | 2.6 | 0.0% | 2.6 | 2.6 | 0.0%
SC RGB 444 | 14.1 | 14.2 | -1.1% | 142.8 | 144.5 | -0.7% | 555.2 | 565.1 | -0.8%
SC YUV 444 | 16.7 | 17.0 | -1.4% | 187.0 | 190.8 | -1.3% | 508.8 | 520.8 | -1.2%
RangeExt | 2.4 | 2.4 | 0.0% | 2.5 | 2.5 | 0.0% | 2.5 | 2.5 | 0.0%
Enc Time[%] | 101% |  |  | 100% |  |  | 102% |  | 
Dec Time[%] | 97% |  |  | 103% |  |  | 101% |  | 

## Slide 11: Exponential-Golomb MV vs. Fixed length MV (lossy)
 | All Intra HE Main-tier |  |  | All Intra HE High-tier |  |  | All Intra HE Super-High-tier |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class F | -0.6% | -0.7% | -0.7% | -0.6% | -0.6% | -0.6% | -0.5% | -0.6% | -0.5%
Class B | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
SC RGB 444 | -1.7% | -1.6% | -1.6% | -1.6% | -1.5% | -1.4% | -1.5% | -1.4% | -1.4%
SC YUV 444 | -2.0% | -1.9% | -2.0% | -1.9% | -1.9% | -1.9% | -1.9% | -1.8% | -1.8%
RangeExt | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Enc Time[%] | 98% |  |  | 98% |  |  | 99% |  | 
Dec Time[%] | 96% |  |  | 97% |  |  | 87% |  | 
 | Random Access HE Main-tier |  |  | Random Access HE High-tier |  |  |  |  | 
 | Y | U | V | Y | U | V |  |  | 
Class F | -0.5% | -0.4% | -0.6% | -0.4% | -0.4% | -0.5% |  |  | 
Class B | 0.0% | 0.0% | 0.1% | 0.0% | 0.0% | 0.0% |  |  | 
SC RGB 444 | -1.2% | -1.2% | -1.2% | -1.2% | -1.2% | -1.2% |  |  | 
SC YUV 444 | -1.8% | -1.7% | -1.8% | -1.9% | -1.9% | -1.9% |  |  | 
RangeExt | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% |  |  | 
Enc Time[%] | 103% |  |  | 102% |  |  |  |  | 
Dec Time[%] | 104% |  |  | 104% |  |  |  |  | 
 | Low delay B HE Main-tier |  |  | Low delay B HE High-tier |  |  |  |  | 
 | Y | U | V | Y | U | V |  |  | 
Class F | -0.2% | -0.1% | -0.3% | -0.2% | -0.2% | -0.2% |  |  | 
Class B | 0.0% | 0.0% | -0.1% | 0.0% | 0.0% | 0.0% |  |  | 
SC RGB 444 | -1.5% | -1.4% | -1.4% | -1.0% | -1.0% | -0.9% |  |  | 
SC YUV 444 | -1.0% | -1.0% | -0.9% | -1.0% | -0.9% | -0.9% |  |  | 
RangeExt | 0.0% | -0.2% | 0.0% | 0.0% | -0.1% | 0.0% |  |  | 
Enc Time[%] | 101% |  |  | 100% |  |  |  |  | 
Dec Time[%] | 98% |  |  | 97% |  |  |  |  | 

## Slide 12: Search Area
 | All Intra Main |  |  | Random Access Main |  |  | Low delay B Main |  | 
 | compression ratio |  | Bit-rate saving | compression ratio |  | Bit-rate saving | compression ratio |  | Bit-rate saving
 | Reference | Tested |  | Reference | Tested |  | Reference | Tested | 
Class F | 5.2 | 5.4 | -3.0% | 31.7 | 33.1 | -1.8% | 49.8 | 50.8 | -0.8%
Class B | 2.2 | 2.2 | 0.0% | 2.6 | 2.6 | 0.0% | 2.6 | 2.6 | 0.0%
SC RGB 444 | 10.1 | 14.7 | -24.0% | 100.4 | 148.9 | -19.0% | 381.6 | 590.7 | -16.8%
SC YUV 444 | 11.4 | 17.7 | -21.7% | 128.9 | 199.5 | -19.6% | 325.6 | 555.8 | -19.1%
RangeExt | 2.4 | 2.4 | 0.0% | 2.5 | 2.5 | 0.0% | 2.5 | 2.5 | 0.0%
2 CTU vs. Anchor
1 CTU vs. Anchor
 | All Intra Main |  |  | Random Access Main |  |  | Low delay B Main |  | 
 | compression ratio |  | Bit-rate saving | compression ratio |  | Bit-rate saving | compression ratio |  | Bit-rate saving
 | Reference | Tested |  | Reference | Tested |  | Reference | Tested | 
Class F | 5.2 | 5.4 | -2.5% | 31.7 | 32.8 | -1.4% | 49.8 | 50.6 | -0.7%
Class B | 2.2 | 2.2 | 0.0% | 2.6 | 2.6 | 0.0% | 2.6 | 2.6 | 0.0%
SC RGB 444 | 10.1 | 14.2 | -22.1% | 100.4 | 144.5 | -17.5% | 381.6 | 565.1 | -15.3%
SC YUV 444 | 11.4 | 17.0 | -19.3% | 128.9 | 190.8 | -17.4% | 325.6 | 520.8 | -16.8%
RangeExt | 2.4 | 2.4 | 0.0% | 2.5 | 2.5 | 0.0% | 2.5 | 2.5 | 0.0%
 | All Intra Main |  |  | Random Access Main |  |  | Low delay B Main |  | 
 | compression ratio |  | Bit-rate saving | compression ratio |  | Bit-rate saving | compression ratio |  | Bit-rate saving
 | Reference | Tested |  | Reference | Tested |  | Reference | Tested | 
Class F | 5.2 | 5.3 | -1.2% | 31.7 | 32.2 | -0.7% | 49.8 | 50.1 | -0.3%
Class B | 2.2 | 2.2 | 0.0% | 2.6 | 2.6 | 0.0% | 2.6 | 2.6 | 0.0%
SC RGB 444 | 10.1 | 12.6 | -15.3% | 100.4 | 127.7 | -12.1% | 381.6 | 492.9 | -10.7%
SC YUV 444 | 11.4 | 14.3 | -12.1% | 128.9 | 162.2 | -11.0% | 325.6 | 431.7 | -10.8%
RangeExt | 2.4 | 2.4 | 0.0% | 2.5 | 2.5 | 0.0% | 2.5 | 2.5 | 0.0%
4 columns vs. Anchor

## Slide 13: 2 CTUs vs. Anchor (lossy)
 | All Intra HE Main-tier |  |  | All Intra HE High-tier |  |  | All Intra HE Super-High-tier |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class F | -9.5% | -9.3% | -9.5% | -8.3% | -8.3% | -8.3% | -7.1% | -7.2% | -7.2%
Class B | -0.1% | -0.2% | -0.1% | -0.1% | -0.1% | -0.1% | 0.0% | 0.0% | 0.0%
SC RGB 444 | -30.9% | -30.9% | -31.2% | -30.3% | -30.4% | -30.5% | -29.7% | -29.6% | -29.7%
SC YUV 444 | -28.1% | -28.0% | -28.3% | -27.5% | -27.5% | -27.6% | -26.8% | -26.8% | -26.8%
RangeExt | 0.0% | -0.1% | -0.1% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Enc Time[%] | 126% |  |  | 128% |  |  | 129% |  | 
Dec Time[%] | 88% |  |  | 87% |  |  | 87% |  | 
 | Random Access HE Main-tier |  |  | Random Access HE High-tier |  |  |  |  | 
 | Y | U | V | Y | U | V |  |  | 
Class F | -6.9% | -7.2% | -7.4% | -6.0% | -6.4% | -6.4% |  |  | 
Class B | 0.0% | -0.1% | -0.1% | 0.0% | 0.0% | 0.0% |  |  | 
SC RGB 444 | -25.0% | -24.8% | -25.0% | -24.2% | -24.0% | -24.1% |  |  | 
SC YUV 444 | -24.0% | -24.1% | -24.4% | -23.6% | -23.7% | -23.8% |  |  | 
RangeExt | 0.0% | -0.1% | 0.0% | 0.0% | 0.0% | 0.0% |  |  | 
Enc Time[%] | 110% |  |  | 111% |  |  |  |  | 
Dec Time[%] | 106% |  |  | 105% |  |  |  |  | 
 | Low delay B HE Main-tier |  |  | Low delay B HE High-tier |  |  |  |  | 
 | Y | U | V | Y | U | V |  |  | 
Class F | -4.2% | -5.1% | -4.3% | -3.7% | -4.1% | -3.9% |  |  | 
Class B | 0.0% | -0.2% | -0.1% | 0.0% | -0.1% | 0.0% |  |  | 
SC RGB 444 | -19.7% | -18.9% | -18.9% | -19.5% | -18.5% | -18.4% |  |  | 
SC YUV 444 | -19.0% | -18.7% | -18.8% | -19.1% | -18.6% | -18.7% |  |  | 
RangeExt | 0.0% | -0.2% | 0.0% | 0.0% | 0.0% | 0.0% |  |  | 
Enc Time[%] | 107% |  |  | 107% |  |  |  |  | 
Dec Time[%] | 109% |  |  | 109% |  |  |  |  | 

## Slide 14: 1 CTUs vs. Anchor (lossy)
 | All Intra HE Main-tier |  |  | All Intra HE High-tier |  |  | All Intra HE Super-High-tier |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class F | -8.2% | -8.1% | -8.2% | -7.1% | -7.1% | -7.2% | -6.0% | -6.2% | -6.2%
Class B | -0.1% | -0.1% | -0.1% | -0.1% | -0.1% | -0.1% | 0.0% | 0.0% | 0.0%
SC RGB 444 | -28.5% | -28.4% | -28.7% | -28.0% | -28.0% | -28.1% | -27.5% | -27.4% | -27.4%
SC YUV 444 | -25.2% | -25.1% | -25.4% | -24.6% | -24.6% | -24.8% | -24.1% | -24.0% | -24.0%
RangeExt | 0.0% | 0.0% | -0.1% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Enc Time[%] | 128% |  |  | 129% |  |  | 130% |  | 
Dec Time[%] | 87% |  |  | 87% |  |  | 87% |  | 
 | Random Access HE Main-tier |  |  | Random Access HE High-tier |  |  |  |  | 
 | Y | U | V | Y | U | V |  |  | 
Class F | -6.0% | -6.2% | -6.5% | -5.2% | -5.6% | -5.6% |  |  | 
Class B | 0.0% | -0.1% | -0.1% | 0.0% | -0.1% | 0.0% |  |  | 
SC RGB 444 | -22.9% | -22.7% | -22.9% | -22.3% | -22.1% | -22.3% |  |  | 
SC YUV 444 | -21.4% | -21.6% | -21.9% | -21.2% | -21.3% | -21.4% |  |  | 
RangeExt | 0.0% | -0.1% | -0.1% | 0.0% | 0.0% | -0.1% |  |  | 
Enc Time[%] | 114% |  |  | 114% |  |  |  |  | 
Dec Time[%] | 108% |  |  | 109% |  |  |  |  | 
 | Low delay B HE Main-tier |  |  | Low delay B HE High-tier |  |  |  |  | 
 | Y | U | V | Y | U | V |  |  | 
Class F | -3.7% | -4.0% | -3.9% | -3.2% | -3.4% | -3.3% |  |  | 
Class B | 0.0% | -0.2% | -0.4% | 0.0% | 0.0% | -0.1% |  |  | 
SC RGB 444 | -18.1% | -17.2% | -17.2% | -17.6% | -16.7% | -16.6% |  |  | 
SC YUV 444 | -16.6% | -16.2% | -16.3% | -16.8% | -16.1% | -16.2% |  |  | 
RangeExt | 0.0% | -0.2% | 0.0% | 0.0% | -0.1% | 0.0% |  |  | 
Enc Time[%] | 110% |  |  | 110% |  |  |  |  | 
Dec Time[%] | 106% |  |  | 105% |  |  |  |  | 

## Slide 15: 4 columns vs. Anchor (lossy)
 | All Intra HE Main-tier |  |  | All Intra HE High-tier |  |  | All Intra HE Super-High-tier |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class F | -4.4% | -4.3% | -4.4% | -3.7% | -3.8% | -3.8% | -3.2% | -3.3% | -3.3%
Class B | 0.0% | -0.1% | -0.1% | 0.0% | -0.1% | -0.1% | 0.0% | 0.0% | 0.0%
SC RGB 444 | -18.9% | -19.0% | -19.2% | -18.9% | -19.1% | -19.1% | -18.8% | -18.8% | -18.8%
SC YUV 444 | -15.3% | -15.3% | -15.6% | -15.1% | -15.3% | -15.4% | -15.1% | -15.1% | -15.1%
RangeExt | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Enc Time[%] | 122% |  |  | 123% |  |  | 123% |  | 
Dec Time[%] | 105% |  |  | 105% |  |  | 104% |  | 
 | Random Access HE Main-tier |  |  | Random Access HE High-tier |  |  |  |  | 
 | Y | U | V | Y | U | V |  |  | 
Class F | -3.2% | -3.4% | -3.5% | -2.8% | -3.0% | -3.1% |  |  | 
Class B | 0.1% | -0.1% | -0.1% | 0.0% | -0.1% | 0.0% |  |  | 
SC RGB 444 | -15.3% | -15.3% | -15.5% | -15.1% | -15.1% | -15.2% |  |  | 
SC YUV 444 | -12.9% | -13.1% | -13.3% | -13.0% | -13.1% | -13.2% |  |  | 
RangeExt | 0.0% | -0.1% | -0.1% | 0.0% | 0.0% | 0.0% |  |  | 
Enc Time[%] | 111% |  |  | 111% |  |  |  |  | 
Dec Time[%] | 101% |  |  | 106% |  |  |  |  | 
 | Low delay B HE Main-tier |  |  | Low delay B HE High-tier |  |  |  |  | 
 | Y | U | V | Y | U | V |  |  | 
Class F | -2.1% | -2.3% | -2.1% | -1.7% | -1.7% | -1.8% |  |  | 
Class B | 0.0% | -0.1% | -0.1% | 0.0% | -0.1% | 0.0% |  |  | 
SC RGB 444 | -11.7% | -11.2% | -11.2% | -11.8% | -11.1% | -11.1% |  |  | 
SC YUV 444 | -10.1% | -10.0% | -9.9% | -10.5% | -10.2% | -10.1% |  |  | 
RangeExt | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% |  |  | 
Enc Time[%] | 108% |  |  | 108% |  |  |  |  | 
Dec Time[%] | 104% |  |  | 105% |  |  |  |  | 

## Slide 16: Conclusions
Intra Motion Compensation is proposed with
  Search area restriction to left CTU (or left 4 columns) + current CTU
  No interpolation filter
  Exponential-Golomb codes for MV coding
in order to make it more friendly to practical implementations.