## Slide 1: Intra Motion Compensation with 2-D MVs JCTVC-N0256
Chao Pang, Joel Sole, Liwei Guo, Marta Karczewicz, Rajan Joshi

## Slide 2: Introduction
Intra motion compensation (MC)
  JCTVC-N0205 (RCE3) and N0206
Current CU
Prediction
Current CTU
Left CTU
Left Left CTU

## Slide 3: Issues and Proposed
Issues in JCTVC-N0205
  MVs are restricted to be 1-D
    This removes flexibility from the encoder without providing benefits in the pipelining
  A new syntax element is introduced to signal whether the MV is horizontal or vertical
    Departs from the HEVC design
  Binarization is fixed length codes
    Instead of Exponential-Golomb codes in HEVC
Proposal:
  Intra MC with 2-D MV
  Better alignment with HEVC MV coding
  Binarization using Exponential-Golomb codes

## Slide 4: 2-D MV
Usage of 2-D MV for Intra MC
  Both MV components can be non-zero at the same time
  No need for an additional syntax element
Two MV coding methods tested:
  MV predictor + Flag indicating non-zero MVD + Exponential-Golomb of 3rd order + Sign Flag
  No predictor + Exponential-Golomb codes used for MVD coding in HEVC

## Slide 5: Pipeline Aspects
2-D MV tested on the top of the pipeline friendly method in JCTVC-N0254
  No interpolation filters
  MV search area is restricted to current CTU and left CTU/left 4 columns

## Slide 6: Encoder Aspects
To further test the method, in some experiments the following applies:
  Fast encoder for the 2-D MV (instead of full search)
  Restricting the MV to be 1-D (but use 2-D signaling)

## Slide 7: Experimental Results
Provided results to assess the proposed method:
  Performance of 2-D MV vs. 1-D MV
  Fast search vs. full search
  Signaling: 1-D search using 2-D signaling vs. 1-D signaling
  Signaling: MV coding method 1 vs. method 2

## Slide 8: 2-D MV with 1 CTU vs Anchor (lossless)
 | All Intra Main |  |  | Random Access Main |  |  | Low delay B Main |  | 
 | compression ratio |  |  | compression ratio |  |  | compression ratio |  | 
 | Reference | Tested |  | Reference | Tested |  | Reference | Tested | 
Class F | 5.2 | 5.5 | -4.4% | 31.7 | 34.4 | -3.2% | 49.8 | 53.4 | -2.4%
Class B | 2.2 | 2.2 | 0.0% | 2.6 | 2.6 | 0.0% | 2.6 | 2.6 | 0.0%
SC RGB 444 | 10.1 | 15.1 | -26.3% | 100.4 | 152.6 | -21.0% | 381.6 | 581.4 | -18.1%
SC YUV 444 | 11.4 | 18.5 | -23.1% | 128.9 | 207.0 | -20.8% | 325.6 | 558.6 | -19.7%
RangeExt | 2.4 | 2.4 | 0.0% | 2.5 | 2.5 | 0.0% | 2.5 | 2.5 | 0.0%
Enc Time[%] | 282% |  |  | 154% |  |  | 127% |  | 
Dec Time[%] | 92% |  |  | 104% |  |  | 103% |  | 

## Slide 9: 2-D MV with 1 CTU vs Anchor (lossy)
 | All Intra HE Main-tier |  |  | All Intra HE High-tier |  |  | All Intra HE Super-High-tier |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class F | -11.2% | -11.1% | -11.4% | -9.7% | -9.9% | -10.0% | -8.3% | -8.5% | -8.6%
Class B | -0.4% | -0.6% | -0.5% | -0.3% | -0.4% | -0.4% | -0.1% | -0.2% | -0.2%
SC RGB 444 | -35.5% | -35.5% | -35.8% | -34.7% | -34.8% | -35.0% | -33.9% | -33.9% | -33.9%
SC YUV 444 | -29.8% | -29.8% | -30.1% | -29.3% | -29.4% | -29.6% | -28.7% | -28.7% | -28.7%
RangeExt | -0.4% | -0.4% | -0.5% | -0.2% | -0.2% | -0.3% | -0.1% | -0.1% | -0.1%
Enc Time[%] | 221% |  |  | 213% |  |  | 206% |  | 
Dec Time[%] | 81% |  |  | 81% |  |  | 81% |  | 
 | Random Access HE Main-tier |  |  | Random Access HE High-tier |  |  |  |  | 
 | Y | U | V | Y | U | V |  |  | 
Class F | -8.5% | -9.0% | -9.1% | -7.4% | -7.9% | -8.0% |  |  | 
Class B | -0.1% | -0.3% | -0.4% | -0.1% | -0.2% | -0.2% |  |  | 
SC RGB 444 | -29.3% | -29.1% | -29.3% | -28.3% | -28.1% | -28.2% |  |  | 
SC YUV 444 | -25.9% | -26.1% | -26.4% | -25.4% | -25.6% | -25.7% |  |  | 
RangeExt | -0.2% | -0.4% | -0.4% | -0.1% | -0.1% | -0.2% |  |  | 
Enc Time[%] | 151% |  |  | 150% |  |  |  |  | 
Dec Time[%] | 103% |  |  | 103% |  |  |  |  | 
 | Low delay B HE Main-tier |  |  | Low delay B HE High-tier |  |  |  |  | 
 | Y | U | V | Y | U | V |  |  | 
Class F | -5.2% | -5.6% | -5.2% | -4.6% | -4.7% | -4.6% |  |  | 
Class B | 0.0% | 0.0% | -0.4% | 0.0% | 0.0% | -0.1% |  |  | 
SC RGB 444 | -23.5% | -22.6% | -22.7% | -23.2% | -22.2% | -22.2% |  |  | 
SC YUV 444 | -20.1% | -19.7% | -19.8% | -20.6% | -19.9% | -20.0% |  |  | 
RangeExt | 0.0% | -0.2% | -0.2% | 0.0% | 0.0% | -0.1% |  |  | 
Enc Time[%] | 142% |  |  | 141% |  |  |  |  | 
Dec Time[%] | 103% |  |  | 103% |  |  |  |  | 

## Slide 10: 2-D MV with 1 CTU vs 1-D MV with 1 CTU (lossless)
 | All Intra Main |  |  | Random Access Main |  |  | Low delay B Main |  | 
 | compression ratio |  |  | compression ratio |  |  | compression ratio |  | 
 | Reference | Tested |  | Reference | Tested |  | Reference | Tested | 
Class F | 5.4 | 5.5 | -2.1% | 32.8 | 34.4 | -1.8% | 50.6 | 53.4 | -1.8%
Class B | 2.2 | 2.2 | 0.0% | 2.6 | 2.6 | 0.0% | 2.6 | 2.6 | 0.0%
SC RGB 444 | 14.2 | 15.1 | -5.4% | 144.5 | 152.6 | -4.5% | 565.1 | 581.4 | -3.3%
SC YUV 444 | 17.0 | 18.5 | -5.7% | 190.8 | 207.0 | -4.9% | 520.8 | 558.6 | -4.2%
RangeExt | 2.4 | 2.4 | 0.0% | 2.5 | 2.5 | 0.0% | 2.5 | 2.5 | 0.0%
Enc Time[%] | 222% |  |  | 142% |  |  | 126% |  | 
Dec Time[%] | 101% |  |  | 93% |  |  | 96% |  | 

## Slide 11: 2-D MV with 1 CTU vs 1-D MV with 1 CTU (lossy)
 | All Intra HE Main-tier |  |  | All Intra HE High-tier |  |  | All Intra HE Super-High-tier |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class F | -3.5% | -3.5% | -3.7% | -3.0% | -3.2% | -3.3% | -2.6% | -2.7% | -2.8%
Class B | -0.4% | -0.4% | -0.4% | -0.2% | -0.3% | -0.3% | -0.1% | -0.1% | -0.2%
SC RGB 444 | -9.7% | -9.8% | -9.9% | -9.3% | -9.4% | -9.5% | -8.9% | -8.9% | -9.0%
SC YUV 444 | -7.1% | -7.2% | -7.2% | -7.2% | -7.3% | -7.4% | -7.2% | -7.2% | -7.3%
RangeExt | -0.3% | -0.3% | -0.4% | -0.2% | -0.2% | -0.2% | -0.1% | -0.1% | -0.1%
Enc Time[%] | 177% |  |  | 170% |  |  | 164% |  | 
Dec Time[%] | 98% |  |  | 97% |  |  | 98% |  | 
 | Random Access HE Main-tier |  |  | Random Access HE High-tier |  |  |  |  | 
 | Y | U | V | Y | U | V |  |  | 
Class F | -2.9% | -3.1% | -3.0% | -2.5% | -2.7% | -2.7% |  |  | 
Class B | -0.1% | -0.2% | -0.3% | -0.1% | -0.2% | -0.2% |  |  | 
SC RGB 444 | -8.3% | -8.3% | -8.3% | -7.8% | -7.8% | -7.8% |  |  | 
SC YUV 444 | -6.5% | -6.5% | -6.5% | -6.3% | -6.4% | -6.4% |  |  | 
RangeExt | -0.1% | -0.2% | -0.2% | -0.1% | -0.1% | -0.1% |  |  | 
Enc Time[%] | 136% |  |  | 133% |  |  |  |  | 
Dec Time[%] | 97% |  |  | 96% |  |  |  |  | 
 | Low delay B HE Main-tier |  |  | Low delay B HE High-tier |  |  |  |  | 
 | Y | U | V | Y | U | V |  |  | 
Class F | -1.7% | -1.7% | -1.5% | -1.5% | -1.4% | -1.3% |  |  | 
Class B | 0.0% | 0.1% | 0.0% | 0.0% | 0.1% | 0.0% |  |  | 
SC RGB 444 | -6.6% | -6.6% | -6.6% | -6.9% | -6.7% | -6.7% |  |  | 
SC YUV 444 | -4.7% | -4.8% | -4.7% | -5.3% | -5.3% | -5.3% |  |  | 
RangeExt | 0.0% | 0.1% | -0.2% | 0.0% | 0.0% | -0.1% |  |  | 
Enc Time[%] | 129% |  |  | 128% |  |  |  |  | 
Dec Time[%] | 101% |  |  | 102% |  |  |  |  | 

## Slide 12: 2-D MV with 1 CTU vs 1-D MV with 2 CTUs (lossless)
 | All Intra Main |  |  | Random Access Main |  |  | Low delay B Main |  | 
 | compression ratio |  |  | compression ratio |  |  | compression ratio |  | 
 | Reference | Tested |  | Reference | Tested |  | Reference | Tested | 
Class F | 5.4 | 5.5 | -1.6% | 33.1 | 34.4 | -1.5% | 50.8 | 53.4 | -1.7%
Class B | 2.2 | 2.2 | 0.0% | 2.6 | 2.6 | 0.0% | 2.6 | 2.6 | 0.0%
SC RGB 444 | 14.7 | 15.1 | -2.8% | 148.9 | 152.6 | -2.5% | 590.7 | 581.4 | -1.2%
SC YUV 444 | 17.7 | 18.5 | -2.4% | 199.5 | 207.0 | -1.9% | 555.8 | 558.6 | -0.9%
RangeExt | 2.4 | 2.4 | 0.0% | 2.5 | 2.5 | 0.0% | 2.5 | 2.5 | 0.0%
Enc Time[%] | 219% |  |  | 142% |  |  | 128% |  | 
Dec Time[%] | 101% |  |  | 94% |  |  | 98% |  | 

## Slide 13: 2-D MV with 1 CTU vs 1-D MV with 2 CTUs (lossy)
 | All Intra HE Main-tier |  |  | All Intra HE High-tier |  |  | All Intra HE Super-High-tier |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class F | -2.0% | -2.1% | -2.2% | -1.7% | -1.9% | -1.9% | -1.4% | -1.6% | -1.6%
Class B | -0.4% | -0.4% | -0.4% | -0.2% | -0.3% | -0.3% | -0.1% | -0.1% | -0.2%
SC RGB 444 | -6.3% | -6.4% | -6.4% | -6.1% | -6.1% | -6.2% | -5.8% | -5.8% | -5.8%
SC YUV 444 | -2.8% | -2.8% | -2.9% | -2.9% | -3.0% | -3.1% | -3.0% | -3.0% | -3.2%
RangeExt | -0.3% | -0.3% | -0.4% | -0.2% | -0.2% | -0.2% | -0.1% | -0.1% | -0.1%
Enc Time[%] | 179% |  |  | 171% |  |  | 165% |  | 
Dec Time[%] | 97% |  |  | 97% |  |  | 97% |  | 
 | Random Access HE Main-tier |  |  | Random Access HE High-tier |  |  |  |  | 
 | Y | U | V | Y | U | V |  |  | 
Class F | -1.8% | -2.0% | -2.0% | -1.5% | -1.8% | -1.8% |  |  | 
Class B | -0.1% | -0.3% | -0.3% | -0.1% | -0.2% | -0.2% |  |  | 
SC RGB 444 | -5.4% | -5.5% | -5.5% | -5.2% | -5.3% | -5.3% |  |  | 
SC YUV 444 | -2.9% | -3.0% | -3.0% | -2.8% | -2.9% | -3.0% |  |  | 
RangeExt | -0.1% | -0.3% | -0.3% | -0.1% | -0.1% | -0.2% |  |  | 
Enc Time[%] | 140% |  |  | 137% |  |  |  |  | 
Dec Time[%] | 99% |  |  | 99% |  |  |  |  | 
 | Low delay B HE Main-tier |  |  | Low delay B HE High-tier |  |  |  |  | 
 | Y | U | V | Y | U | V |  |  | 
Class F | -1.0% | -0.6% | -0.9% | -0.9% | -0.7% | -0.8% |  |  | 
Class B | 0.0% | 0.2% | -0.3% | 0.0% | 0.1% | -0.1% |  |  | 
SC RGB 444 | -4.5% | -4.4% | -4.4% | -4.5% | -4.4% | -4.4% |  |  | 
SC YUV 444 | -1.6% | -1.5% | -1.6% | -2.2% | -2.0% | -2.1% |  |  | 
RangeExt | 0.0% | 0.0% | -0.2% | 0.0% | 0.0% | -0.2% |  |  | 
Enc Time[%] | 132% |  |  | 131% |  |  |  |  | 
Dec Time[%] | 98% |  |  | 98% |  |  |  |  | 

## Slide 14: 2D MV with 1 CTU: Fast search vs Full search (lossless)
 | All Intra Main |  |  | Random Access Main |  |  | Low delay B Main |  | 
 | compression ratio |  |  | compression ratio |  |  | compression ratio |  | 
 | Reference | Tested |  | Reference | Tested |  | Reference | Tested | 
Class F | 5.2 | 5.5 | -4.4% | 31.7 | 34.4 | -3.2% | 49.8 | 53.3 | -2.4%
Class B | 2.2 | 2.2 | 0.0% | 2.6 | 2.6 | 0.0% | 2.6 | 2.6 | 0.0%
SC RGB 444 | 10.1 | 15.0 | -26.1% | 100.4 | 152.2 | -20.8% | 381.6 | 581.0 | -18.0%
SC YUV 444 | 11.4 | 18.4 | -23.1% | 128.9 | 207.5 | -20.9% | 325.6 | 552.6 | -19.6%
RangeExt | 2.4 | 2.4 | 0.0% | 2.5 | 2.5 | 0.0% | 2.5 | 2.5 | 0.0%
Enc Time[%] | 149% |  |  | 102% |  |  | 100% |  | 
Dec Time[%] | 94% |  |  | 106% |  |  | 105% |  | 
Fast search
 | All Intra Main |  |  | Random Access Main |  |  | Low delay B Main |  | 
 | compression ratio |  |  | compression ratio |  |  | compression ratio |  | 
 | Reference | Tested |  | Reference | Tested |  | Reference | Tested | 
Class F | 5.2 | 5.5 | -4.4% | 31.7 | 34.4 | -3.2% | 49.8 | 53.4 | -2.4%
Class B | 2.2 | 2.2 | 0.0% | 2.6 | 2.6 | 0.0% | 2.6 | 2.6 | 0.0%
SC RGB 444 | 10.1 | 15.1 | -26.3% | 100.4 | 152.6 | -21.0% | 381.6 | 581.4 | -18.1%
SC YUV 444 | 11.4 | 18.5 | -23.1% | 128.9 | 207.0 | -20.8% | 325.6 | 558.6 | -19.7%
RangeExt | 2.4 | 2.4 | 0.0% | 2.5 | 2.5 | 0.0% | 2.5 | 2.5 | 0.0%
Enc Time[%] | 282% |  |  | 154% |  |  | 127% |  | 
Dec Time[%] | 92% |  |  | 104% |  |  | 103% |  | 
Full search

## Slide 15: 2-D MV with 1CTU Fast search (lossy)
 | All Intra HE Main-tier |  |  | All Intra HE High-tier |  |  | All Intra HE Super-High-tier |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class F | -10.9% | -10.8% | -11.1% | -9.5% | -9.8% | -9.8% | -8.2% | -8.5% | -8.5%
Class B | -0.4% | -0.5% | -0.4% | -0.3% | -0.3% | -0.3% | -0.1% | -0.2% | -0.2%
SC RGB 444 | -35.2% | -35.2% | -35.5% | -34.5% | -34.6% | -34.7% | -33.6% | -33.5% | -33.6%
SC YUV 444 | -29.6% | -29.6% | -29.9% | -29.2% | -29.2% | -29.4% | -28.6% | -28.6% | -28.6%
RangeExt | -0.3% | -0.3% | -0.5% | -0.2% | -0.2% | -0.2% | -0.1% | -0.1% | -0.1%
Enc Time[%] | 133% |  |  | 129% |  |  | 127% |  | 
Dec Time[%] | 85% |  |  | 85% |  |  | 85% |  | 
 | Random Access HE Main-tier |  |  | Random Access HE High-tier |  |  |  |  | 
 | Y | U | V | Y | U | V |  |  | 
Class F | -8.2% | -8.6% | -8.6% | -7.2% | -7.7% | -7.6% |  |  | 
Class B | -0.1% | -0.1% | -0.3% | -0.1% | -0.1% | -0.2% |  |  | 
SC RGB 444 | -29.1% | -28.9% | -29.1% | -28.1% | -28.0% | -28.0% |  |  | 
SC YUV 444 | -25.9% | -26.1% | -26.4% | -25.5% | -25.6% | -25.8% |  |  | 
RangeExt | -0.1% | -0.3% | -0.2% | -0.1% | -0.1% | -0.2% |  |  | 
Enc Time[%] | 114% |  |  | 113% |  |  |  |  | 
Dec Time[%] | 104% |  |  | 103% |  |  |  |  | 
 | Low delay B HE Main-tier |  |  | Low delay B HE High-tier |  |  |  |  | 
 | Y | U | V | Y | U | V |  |  | 
Class F | -5.0% | -5.1% | -5.3% | -4.5% | -4.4% | -4.8% |  |  | 
Class B | 0.0% | 0.0% | -0.2% | 0.0% | 0.0% | -0.1% |  |  | 
SC RGB 444 | -23.8% | -22.9% | -22.9% | -23.2% | -22.2% | -22.2% |  |  | 
SC YUV 444 | -19.8% | -19.5% | -19.5% | -20.3% | -19.7% | -19.8% |  |  | 
RangeExt | 0.0% | -0.1% | -0.2% | 0.0% | -0.1% | -0.1% |  |  | 
Enc Time[%] | 110% |  |  | 111% |  |  |  |  | 
Dec Time[%] | 104% |  |  | 104% |  |  |  |  | 

## Slide 16: 2-D MV with 1 CTU Full search (lossy)
 | All Intra HE Main-tier |  |  | All Intra HE High-tier |  |  | All Intra HE Super-High-tier |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class F | -11.2% | -11.1% | -11.4% | -9.7% | -9.9% | -10.0% | -8.3% | -8.5% | -8.6%
Class B | -0.4% | -0.6% | -0.5% | -0.3% | -0.4% | -0.4% | -0.1% | -0.2% | -0.2%
SC RGB 444 | -35.5% | -35.5% | -35.8% | -34.7% | -34.8% | -35.0% | -33.9% | -33.9% | -33.9%
SC YUV 444 | -29.8% | -29.8% | -30.1% | -29.3% | -29.4% | -29.6% | -28.7% | -28.7% | -28.7%
RangeExt | -0.4% | -0.4% | -0.5% | -0.2% | -0.2% | -0.3% | -0.1% | -0.1% | -0.1%
Enc Time[%] | 221% |  |  | 213% |  |  | 206% |  | 
Dec Time[%] | 81% |  |  | 81% |  |  | 81% |  | 
 | Random Access HE Main-tier |  |  | Random Access HE High-tier |  |  |  |  | 
 | Y | U | V | Y | U | V |  |  | 
Class F | -8.5% | -9.0% | -9.1% | -7.4% | -7.9% | -8.0% |  |  | 
Class B | -0.1% | -0.3% | -0.4% | -0.1% | -0.2% | -0.2% |  |  | 
SC RGB 444 | -29.3% | -29.1% | -29.3% | -28.3% | -28.1% | -28.2% |  |  | 
SC YUV 444 | -25.9% | -26.1% | -26.4% | -25.4% | -25.6% | -25.7% |  |  | 
RangeExt | -0.2% | -0.4% | -0.4% | -0.1% | -0.1% | -0.2% |  |  | 
Enc Time[%] | 151% |  |  | 150% |  |  |  |  | 
Dec Time[%] | 103% |  |  | 103% |  |  |  |  | 
 | Low delay B HE Main-tier |  |  | Low delay B HE High-tier |  |  |  |  | 
 | Y | U | V | Y | U | V |  |  | 
Class F | -5.2% | -5.6% | -5.2% | -4.6% | -4.7% | -4.6% |  |  | 
Class B | 0.0% | 0.0% | -0.4% | 0.0% | 0.0% | -0.1% |  |  | 
SC RGB 444 | -23.5% | -22.6% | -22.7% | -23.2% | -22.2% | -22.2% |  |  | 
SC YUV 444 | -20.1% | -19.7% | -19.8% | -20.6% | -19.9% | -20.0% |  |  | 
RangeExt | 0.0% | -0.2% | -0.2% | 0.0% | 0.0% | -0.1% |  |  | 
Enc Time[%] | 142% |  |  | 141% |  |  |  |  | 
Dec Time[%] | 103% |  |  | 103% |  |  |  |  | 

## Slide 17: 1-D search with 2-D signaling vs 1-D signaling (lossless)
 | All Intra Main |  |  | Random Access Main |  |  | Low delay B Main |  | 
 | compression ratio |  |  | compression ratio |  |  | compression ratio |  | 
 | Reference | Tested |  | Reference | Tested |  | Reference | Tested | 
Class F | 5.4 | 5.4 | 0.0% | 32.8 | 32.8 | -0.1% | 50.6 | 50.6 | 0.0%
Class B | 2.2 | 2.2 | 0.0% | 2.6 | 2.6 | 0.0% | 2.6 | 2.6 | 0.0%
SC RGB 444 | 14.2 | 14.3 | 0.0% | 144.5 | 145.0 | -0.2% | 565.1 | 565.2 | 0.0%
SC YUV 444 | 17.0 | 17.0 | -0.1% | 190.8 | 191.3 | -0.2% | 520.8 | 521.9 | -0.1%
RangeExt | 2.4 | 2.4 | 0.0% | 2.5 | 2.5 | 0.0% | 2.5 | 2.5 | 0.0%
Enc Time[%] | 98% |  |  | 98% |  |  | 98% |  | 
Dec Time[%] | 107% |  |  | 97% |  |  | 100% |  | 

## Slide 18: 1-D search with 2-D signaling vs 1-D signaling (lossy)
 | All Intra HE Main-tier |  |  | All Intra HE High-tier |  |  | All Intra HE Super-High-tier |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class F | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Class B | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
SC RGB 444 | -1.1% | -1.3% | -1.4% | -1.1% | -1.3% | -1.4% | -1.1% | -1.3% | -1.3%
SC YUV 444 | -0.1% | -0.3% | -0.2% | -0.1% | -0.2% | -0.2% | -0.2% | -0.2% | -0.2%
RangeExt | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Enc Time[%] | 99% |  |  | 100% |  |  | 99% |  | 
Dec Time[%] | 101% |  |  | 102% |  |  | 102% |  | 
 | Random Access HE Main-tier |  |  | Random Access HE High-tier |  |  |  |  | 
 | Y | U | V | Y | U | V |  |  | 
Class F | 0.0% | -0.1% | -0.1% | 0.0% | 0.0% | 0.0% |  |  | 
Class B | 0.0% | 0.1% | 0.0% | 0.0% | 0.1% | -0.1% |  |  | 
SC RGB 444 | -1.1% | -1.2% | -1.2% | -1.0% | -1.2% | -1.1% |  |  | 
SC YUV 444 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% |  |  | 
RangeExt | 0.0% | 0.1% | 0.1% | 0.0% | 0.0% | 0.1% |  |  | 
Enc Time[%] | 98% |  |  | 98% |  |  |  |  | 
Dec Time[%] | 96% |  |  | 96% |  |  |  |  | 
 | Low delay B HE Main-tier |  |  | Low delay B HE High-tier |  |  |  |  | 
 | Y | U | V | Y | U | V |  |  | 
Class F | -0.1% | -0.2% | 0.4% | -0.1% | 0.0% | 0.0% |  |  | 
Class B | 0.0% | 0.0% | 0.3% | 0.0% | -0.1% | 0.1% |  |  | 
SC RGB 444 | -0.6% | -0.8% | -0.8% | -0.9% | -1.0% | -1.1% |  |  | 
SC YUV 444 | 0.1% | 0.0% | 0.0% | 0.0% | -0.1% | -0.1% |  |  | 
RangeExt | 0.1% | 0.1% | 0.0% | 0.0% | 0.0% | -0.1% |  |  | 
Enc Time[%] | 99% |  |  | 99% |  |  |  |  | 
Dec Time[%] | 100% |  |  | 101% |  |  |  |  | 

## Slide 19: 2-D search MV coding method 1 vs method 2 (lossless)
 | All Intra Main |  |  | Random Access Main |  |  | Low delay B Main |  | 
 | compression ratio |  | Bit-rate saving | compression ratio |  | Bit-rate saving | compression ratio |  | Bit-rate saving
 | Reference | Tested |  | Reference | Tested |  | Reference | Tested | 
Class F | 5.5 | 5.5 | -0.3% | 34.0 | 34.4 | -0.4% | 52.8 | 53.4 | -0.4%
Class B | 2.2 | 2.2 | 0.0% | 2.6 | 2.6 | 0.0% | 2.6 | 2.6 | 0.0%
SC RGB 444 | 15.0 | 15.1 | -0.5% | 151.4 | 152.6 | -0.4% | 577.2 | 581.4 | -0.3%
SC YUV 444 | 18.2 | 18.5 | -0.7% | 205.3 | 207.0 | -0.4% | 545.1 | 558.6 | -0.9%
RangeExt | 2.4 | 2.4 | 0.0% | 2.5 | 2.5 | 0.0% | 2.5 | 2.5 | 0.0%
Enc Time[%] | 92% |  |  | 106% |  |  | 97% |  | 
Dec Time[%] | 96% |  |  | 98% |  |  | 99% |  | 

## Slide 20: 2-D search MV coding method 1 vs method 2 (lossy)
 | All Intra HE Main-tier |  |  | All Intra HE High-tier |  |  | All Intra HE Super-High-tier |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class F | -1.1% | -1.0% | -1.1% | -0.8% | -0.8% | -0.8% | -0.6% | -0.6% | -0.7%
Class B | -0.1% | -0.1% | -0.1% | -0.1% | -0.1% | -0.1% | 0.0% | 0.0% | 0.0%
SC RGB 444 | -2.7% | -2.8% | -2.8% | -2.5% | -2.5% | -2.5% | -2.3% | -2.3% | -2.3%
SC YUV 444 | -2.2% | -2.3% | -2.3% | -1.8% | -1.9% | -1.8% | -1.5% | -1.5% | -1.4%
RangeExt | -0.1% | -0.1% | -0.1% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Enc Time[%] | 99% |  |  | 99% |  |  | 98% |  | 
Dec Time[%] | 93% |  |  | 92% |  |  | 92% |  | 
 | Random Access HE Main-tier |  |  | Random Access HE High-tier |  |  |  |  | 
 | Y | U | V | Y | U | V |  |  | 
Class F | -0.9% | -0.9% | -1.0% | -0.7% | -0.8% | -0.8% |  |  | 
Class B | 0.0% | -0.1% | 0.0% | 0.0% | -0.1% | 0.0% |  |  | 
SC RGB 444 | -2.2% | -2.2% | -2.2% | -1.9% | -1.9% | -1.9% |  |  | 
SC YUV 444 | -2.0% | -2.1% | -2.0% | -1.6% | -1.6% | -1.5% |  |  | 
RangeExt | -0.1% | -0.1% | -0.1% | 0.0% | 0.0% | -0.1% |  |  | 
Enc Time[%] | 98% |  |  | 98% |  |  |  |  | 
Dec Time[%] | 96% |  |  | 97% |  |  |  |  | 
 | Low delay B HE Main-tier |  |  | Low delay B HE High-tier |  |  |  |  | 
 | Y | U | V | Y | U | V |  |  | 
Class F | -0.6% | -0.8% | 0.0% | -0.4% | -0.4% | 0.1% |  |  | 
Class B | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% |  |  | 
SC RGB 444 | -1.7% | -1.6% | -1.6% | -1.8% | -1.6% | -1.6% |  |  | 
SC YUV 444 | -1.6% | -1.6% | -1.5% | -1.2% | -1.1% | -1.0% |  |  | 
RangeExt | 0.0% | 0.0% | -0.1% | 0.0% | 0.0% | -0.1% |  |  | 
Enc Time[%] | 99% |  |  | 101% |  |  |  |  | 
Dec Time[%] | 97% |  |  | 97% |  |  |  |  | 

## Slide 21: Conclusions
Proposed Intra Motion Compensation using 2-D Motion Vectors
  Improved performance vs. 1-D
  Better alignment with HEVC MV coding
  More implementation friendly (no interpolation filter and reduced search area)