## Slide 1: JCTVC-N0261 AhG5: Memory Bandwidth Reduction for HEVC RExt
Woo-Shik Kim, Vadim Seregin, Joel Sole, Marta Karczewicz

## Slide 2: Problem statement
In HEVC version 1, to reduce memory bandwidth bi-prediction is restricted for 4x8 and 8x4 PUs
Bandwidth goes up in 4:4:4 chroma format in HEVC RExt
Bandwidth assessment from JCTVC-L0440 applied to 4:2:0 and 4:4:4:
For consumer applications using 4:4:4, it is desirable to reduce memory bandwidth requirement
Memory configuration | 4:2:0 | 4:4:4 | Ratio
4×2 | 15.0 | 20.5 | 137%
8×2 | 18.0 | 24.0 | 133%

## Slide 3: Current Status
It was proposed in Incheon meeting JCTVC-M0298
It was recommended for adoption in RExt BoG
During plenary discussion, there was a request to have a test with weighted prediction
AhG5 has a mandate to study it

## Slide 4: Solutions: Approach 1
Restrict bi-prediction for 8x8 CU
  For merge mode, bi-directional MV candidate is converted to uni-directional motion vector from RefPicList0
  For AMVP mode, only uni-directional MV can be chosen at encoder side and inter-prediction direction signaling is restricted to uni-direction only
  Can be applied to chroma components only for better coding efficiency
  BW compared to 4:2:0 is reduced from 137% to 108% at the cost of 0.3% loss in Y
Memory configuration | 4:2:0 | 4:4:4 | Test 1/2 | Ratio to 4:2:0 | Ratio to 4:4:4
4×2 | 15.0 | 20.5 | 16.3 | 108% | 79%
8×2 | 18.0 | 24.0 | 21.0 | 117% | 88%

## Slide 5: Solutions: Approach 2
Restrict motion interpolation in vertical direction for 8x8 PU
  No MV coding change
  MV is rounded to the nearest integer at MC stage
  Can be applied to chroma components only for better coding efficiency
Tests
  3-1. For 8x8 PUs, motion interpolation is applied only in the horizontal direction for all color components
  3-2. For 8x8 PUs, motion interpolation is applied only in the horizontal direction for all chroma components
  3-3. For 8x8 PUs, motion interpolation is not applied. For PUs smaller that 16x16, motion interpolation is applied only in the horizontal direction for all components  BW close to 4:2:0
Memory configuration | 4:2:0 | 4:4:4 | Test 3-2 | Ratio to 4:2:0 | Ratio to 4:4:4
4×2 | 15.0 | 20.5 | 16.3 | 113% | 83%
8×2 | 18.0 | 24.0 | 21.0 | 117% | 88%

## Slide 6: Weighted prediction test for Approach 1
Weighted prediction was enabled and tested with methods 1 and 2
It was noticed that weights from RefPicList0 and RefPicList1 can be different and using only uni-L0 conversion may not be optimal
In Test 2a the direction with larger weight can be selected for uni-prediction
 | Random Access HE Main-tier |  |  | Random Access HE High-tier |  |  | Low delay B HE Main-tier |  |  | Low delay B HE High-tier |  | 
 | Y | U | V | Y | U | V | Y | U | V | Y | U | V
Test 1 WP Black | 0.6% | 0.6% | 0.6% | 0.8% | 0.8% | 0.9% | 0.3% | 0.3% | 0.4% | 0.6% | 0.6% | 0.7%
Test 1 WP White | 0.6% | 0.5% | 0.5% | 0.8% | 0.7% | 0.8% | 0.4% | 0.4% | 0.6% | 0.6% | 0.5% | 0.8%
Test 2 WP Black | 0.1% | 0.5% | 0.5% | 0.2% | 0.6% | 0.9% | 0.1% | 0.4% | 0.3% | 0.3% | 0.5% | 0.5%
Test 2 WP White | 0.1% | 0.6% | 0.5% | 0.3% | 0.7% | 0.8% | 0.2% | 0.4% | 0.3% | 0.3% | 0.5% | 0.6%
Test 2a WP Black | 0.1% | 0.6% | 0.5% | 0.3% | 0.7% | 0.8% | 0.1% | 0.6% | 0.3% | 0.2% | 0.7% | 0.5%
Test 2a WP White | 0.1% | 0.5% | 0.5% | 0.3% | 0.7% | 0.8% | 0.1% | 0.6% | 0.4% | 0.2% | 0.6% | 0.6%

## Slide 7: Experimental results
BD-rate using RExt common conditions
Summary results of RA and LB YUV 4:4:4 (+ is loss) (%)
Thanks to Canon for cross-verification (JCTVC-N0310)
 | Random Access HE Main-tier |  |  | Random Access HE High-tier |  |  | Low delay B HE Main-tier |  |  | Low delay B HE High-tier |  | 
 | Y | U | V | Y | U | V | Y | U | V | Y | U | V
Test 1 | 0.7 | 0.8 | 0.8 | 1.0 | 0.9 | 1.2 | 0.6 | 0.6 | 0.5 | 0.9 | 0.7 | 0.8
Test 2 | 0.2 | 0.7 | 0.8 | 0.4 | 0.8 | 1.1 | 0.2 | 0.3 | 0.3 | 0.4 | 0.4 | 0.5
Test 3-2 | 0.1 | 0.2 | 0.3 | 0.2 | 0.2 | 0.5 | 0.2 | 0.2 | 0.4 | 0.3 | 0.2 | 0.5

## Slide 8: Conclusion
Two approaches are presented for bandwidth reduction
  Bi-prediction restriction
  Motion interpolation restriction
Approach 2 has smaller loss
Both achieve about 20% BW reduction at the cost of 0.2-0.3% loss