## Slide 1: JCTVC-N0263 AhG5: Deblocking Filter in 4:4:4 Chroma Format
Woo-Shik Kim, Wei Pu, Joel Sole, Marta Karczewicz

## Slide 2: Problem statement
In HEVC version 1, chroma deblock filter performance is restricted
  Only applied for intra block edges
  Only a weak filter is applied where 1 pixel each side along the edge is modified
In 4:4:4 chroma format chroma can contain more information than in 4:2:0
  Blocking artifact is observed in chroma components which can harm overall visual quality

## Slide 3: Solutions
Method 1
  Apply luma filter to chroma components
Method 2
  Apply luma filter without the strong filter
    When bS is 2, it is set to 1 for chroma filtering
Method 3
  Currently chroma filter is applied when bS is 2, thus only intra-coded block boundaries are filtered
  Propose to apply chroma filter when bS > 0, so that deblocking filter can be applied for inter-coded blocks
A deblock_chroma_as_luma_flag can be added to signal whether to apply above method or not

## Slide 4: Experimental results
Summary results of YUV 4:4:4 Main-tier (+ is gain) (%)
Subjective test (score is number of viewers)
Method 1 | Y | U | V
AI | 0.0 | 1.1 | 1.2
RA | 0.2 | 3.0 | 2.3
LB | 0.2 | 2.7 | 0.9
Method 2 | Y | U | V
AI | 0.0 | 0.7 | 0.7
RA | 0.2 | 2.4 | 1.7
LB | 0.2 | 2.2 | 0.8
Method 3 | Y | U | V
AI | 0.0 | 0.0 | 0.0
RA | 0.1 | 1.0 | 0.8
LB | 0.1 | 1.1 | 0.9
 | Sequence | HM | N0263
RGB | DucksAndLegs | 1 | 4
 | EBULupoCandlelight | 0 | 5
 | EBURainFruits | 1 | 4
YUV | Kimono | 0 | 5
 | EBURainFruits | 2 | 3

## Slide 5: Conclusion
Methods to strengthen chroma deblock filtering is proposed
Subjective quality improvement is achieved for both RGB and YUV 4:4:4 sequences
Coding efficiency improvement is reported