## Slide 1: JCTVC-N0265 AHG13: Complexity reduction of the up-sampling process
K. Andersson, R. Sjöberg
Notes: 2013-07-25
© Ericsson AB 2013
<number>

## Slide 2: Summary
Multi-loop scalable decoding has a significant impact on decoder complexity.
To reduce complexity while maintaining coding efficiency it is proposed to enable use of 4-tap luma up-sampling filters.
For common conditions, the average number of operations (mult/add) for MC and up-sampling is reduced by 20% and the memory access is reduced by 5%, at a luma BDR loss of 0.9%.
It is also shown that the BDR loss can be reduced by having 8-tap up-sampling filter for intra slices and 4-tap up-sampling filter for other slices.
Thanks to Canon for cross-check (JCTVC-N0280).
Notes: 2013-07-25
<number>
© Ericsson AB 2013

## Slide 3: Background
Compared to single layer decoding SHVC requires both motion compensation in the base layer and motion compensation or up-sampling in the enhancement layers. Both MC and up-sampling requires 8-tap filtering for luma and 4-tap filtering for chroma.
To reduce the computations the use of 4-tap up-sampling filter for luma is investigated.

## Slide 4: 4-tap up-SAMPLING FILTEr
Phase shift | SHM-2.0 Luma up-sampling filter | Proposed 4 taps Luma up-sampling filter
0 | { 0, 0, 0, 64, 0, 0, 0, 0}/64 | { 0, 64, 0, 0}/64
1/3 | {-1, 4, -11, 52, 26, -8, 3, -1}/64 | { -8, 52, 26, -6}/64
1/2 | {-1, 4, -11, 40, 40, -11, 4, -1}/64 | {-8, 40, 40, -8}/64
2/3 | {-1, 3, -8, 26, 52, -11, 4, -1}/64 | {-6, 26, 52, -8}/64

## Slide 5: BDR performance compared to SHM-2.0
 | Spatial scalability 2x |  |  | Spatial scalability 1.5x |  | 
 | Y | U | V | Y | U | V
Intra | 1,9% | 1,6% | 1,6% | 1,1% | 1,1% | 1,1%
RA | 1,0% | 0,4% | 0,4% | 0,4% | 0,3% | 0,3%
LD-B | 0,7% | 0,2% | 0,2% | 0,4% | 0,1% | 0,1%
Avg CC | 1,2% | 0,8% | 0,7% | 0,6% | 0,5% | 0,5%
LD-P | 0,9% | 0,3% | 0,2% | 0,6% | 0,2% | 0,2%
Avg | 1,1% | 0,6% | 0,6% | 0,6% | 0,4% | 0,4%

## Slide 6: AVERAGE OPERATIONS PER pixel for MC and up-SAMPLING
 | Spatial scalability 2x |  |  |  | Spatial scalability 1.5x |  |  | 
 | PU SHM-2.0 [Op/pix] | PU 4-tap Reduction [%] | Pic SHM-2.0 [Op/pix] | Pic 4-tap Reduction [%] | PU SHM-2.0 [Op/pix] | PU 4-tap Reduction [%] | Pic SHM-2.0 [Op/pix] | Pic 4-tap Reduction [%]
Intra | 21,7 | -46,9% | 24,0 | -44,8% | 21,7 | -46,9% | 21,4 | -45,5%
RA | 20,4 | -6,5% | 34,2 | -22,4% | 23,1 | -7,9% | 33,8 | -20,1%
LD-B | 18,3 | -7,8% | 31,7 | -24,0% | 21,1 | -10,2% | 31,0 | -21,7%
Avg CC | 20,1 | -20,4% | 30,0 | -30,4% | 22,0 | -21,7% | 28,7 | -29,1%
LD-P | 12,6 | -9,9% | 26,4 | -28,7% | 14,1 | -13,9% | 24,4 | -27,3%
Avg | 18,2 | -17,8% | 29,1 | -30,0% | 20,0 | -19,7% | 27,6 | -28,6%
Complexity module from JCTVC-L0440v6

## Slide 7: AVERAGE MEMORY ACCESS
 | Spatial scalability 2x |  |  |  | Spatial scalability 1.5x |  |  | 
 | PU SHM-2.0 | PU 4-tap Reduction [%] | Pic SHM-2.0 | Pic 4-tap Reduction [%] | PU SHM-2.0 | PU 4-tap Reduction [%] | Pic SHM-2.0 | Pic 4-tap Reduction [%]
Intra | 7235373 | -11,3% | 10432990 | -1,6% | 6511056 | -12,3% | 8773598 | -2,1%
RA | 12560365 | -0,9% | 17861909 | -0,7% | 9674608 | -1,6% | 14181257 | -1,1%
LD-B | 11750775 | -0,9% | 17026889 | -0,6% | 8991556 | -1,8% | 13397979 | -1,1%
Avg CC | 10515504 | -4,4% | 15107263 | -1,0% | 8392407 | -5,2% | 12117611 | -1,4%
LD-P | 9395321 | -1,2% | 14731693 | -0,9% | 7164954 | -2,3% | 11622646 | -1,3%
Avg | 10235459 | -3,6% | 15013370 | -0,9% | 8085543 | -4,5% | 11993870 | -1,4%
Complexity module from JCTVC-M0455v2

## Slide 8: BDR performance with 4-tap only for inter slices
 | Spatial scalability 2x |  |  | Spatial scalability 1.5x |  | 
 | Y | U | V | Y | U | V
Intra | 0,0% | 0,0% | 0,0% | 0,0% | 0,0% | 0,0%
RA | 0,6% | 0,1% | 0,1% | 0,2% | 0,1% | 0,0%
LD-B | 0,7% | 0,1% | 0,2% | 0,3% | 0,1% | 0,2%
Avg CC | 0,4% | 0,1% | 0,1% | 0,2% | 0,1% | 0,1%
LD-P | 0,8% | 0,3% | 0,2% | 0,5% | 0,1% | 0,2%
Avg | 0,5% | 0,1% | 0,1% | 0,3% | 0,1% | 0,1%

## Slide 9: Signalling of filter size for up-sampling
To be able to trade coding efficiency versus complexity we propose:
  one flag in SPS extension that indicates if the filter length for up-sampling is fixed for the whole sequence.
  one flag in SPS extension that selects 4-tap or 8-tap filter for luma up-sampling.
  one flag in slice header that selects 4-tap or 8-tap filter for luma up-sampling.

## Slide 10: Conclusions
It has been shown that the use of 4-tap filters for luma up-sampling for common conditions can reduce the average number of operations for MC and PU based up-sampling by 20% and memory access by 5% with a BDR loss of 0.9%.
The BDR loss is larger for 2x spatial scalability than 1.5x spatial scalability. For all Intra 2x spatial scalability the loss is 1.9%
By enabling the possibility to select the length of the luma up-sampling filter (4 or 8 tap) it is possible to trade complexity versus performance according to the needs of the applications.

## Slide 11
Notes: 2013-07-25
<number>
© Ericsson AB 2013