## Slide 1: RCE2 Test A.1: Rice parameter signaling for transform-skip blocks
Seung-Hwan Kim, Kiran Misra, Andrew Segall
(JCTVC-N0268)

## Slide 2: Organization
Motivation
Problem Statement
Proposed Method
Results
Conclusions

## Slide 3: Motivation & Problem statement
The importance of transform-skip block coding mode
  Important for screen content sequences [JCTVC-L0428]
    BD-Rate change for disabling transform skip 25.9 % (AI), 23.5% (RA), 20.2% (LD)
  Lossless coding
  The different statistics of residual data
Remaining abs_level coding
  Designed for transformed coefficients
  Statistical distribution of absolute level depends on the scanning position
  Rice-parameter is initialized to ‘0’ and increased monotonically based on the previous level information

## Slide 4: Problem Statement
Problems with remaining abs_level Coding for TS blocks
  Statistical distribution of abs_level in transform-skip blocks doesn’t depend on the scanning position
  Rice-parameter initialization causes coding loss
  Monotonical increment of RP causes delay to reach a optimal rice-parameter and it causes coding loss

## Slide 5: Proposed Solution
Rice parameter signaling
  Send ‘rice-parameter’ for each transform-skip block
  Signal rice-parameter from the given set {0, 2, 4}
  Remove rice-parameter update process

## Slide 6: Results (Lossless)
Provide high coding performance for screen content where the optimal rice-parameter is found to be large

## Slide 7: Results (Lossy)
Provide high coding gain for high bitrates coding conditions such SHT, HT
Slight coding loss has been observed at low bitrates coding such as MT

## Slide 8: Results (Lossy with a slice level flag)
A Slice level flag is considered to control the usage of the rice-parameter signaling method
  If the flag is set to one rice-parameter signaling method is used for TS blocks for the given slice.
  Ex: The flag is set to one when slice QP <32

## Slide 9: Conclusions
Send rice-parameter for each transform-skip block
Simulations demonstrate that the proposed rice-parameter signaling method provides high coding efficiency for lossless and high bitrates coding.
Remove the dependency from previous level information