## Slide 1: HLS: Non-significant slice segments with tiles for single layer HEVC extensions
Cheung Auyeung
Sony Electronics Inc.
July 24, 2013

## Slide 2: Introduction to Tiled Streaming
All tiles are independently
decodable
User selects ROI interactively
User selects ROI interactively
Avoid CTU level transcoding
Avoid CTU level transcoding
Need to reduce complexity and bandwidth to serve all users.

## Slide 3: Avoid CTU Level Transcoding
Replaced by non-significant
tiles in black
Extracted
tiles
8K4K@60P at server
HD@60P to client
4K2K@60P to client
Replaced area outside ROI by non-significant tiles

## Slide 4: Conditions for Non-Significant Tiles
Set tiles_enabled_flag in pic_parameter_set_rbsp() to 1.
  Encode every tile so that every tile is independently decodable.
  Each tile is comprised of one or more slice segments.
Set slice_segment_header_extension_present_flag in pic_parameter_set_rbsp() to 1.
Modify slice_segment_header() to enable the functionality of non-significant slice segment with tiles.
Modify slice_segment_layer_rbsp() to enable the functionality of non-significant slice segment with tiles.

## Slide 5: Proposed Syntax
slice_segment_header( ) { | Descriptor
… | 
… | 
if( slice_segment_header_extension_present_flag ) { | 
if( tiles_enabled_flag ) { | 
non_significant_slice_segment_flag | u(1)
if( non_significant_slice_segment_flag ) | 
slice_segment_size_minus1 | ue(v)
} | 
slice_segment_header_extension_flag | u(1)
if (slice_segment_header_extension_flag) { | 
slice_segment_header_extension_length | ue(v)
for( i = 0; i < slice_segment_header_extension_length; i++) | 
slice_segment_header_extension_data_byte[ i ] | u(8)
} | 
} | 
byte_alignment( ) | 
} | 
slice_segment_layer_rbsp( ) { | Descriptor
slice_segment_header( ) | 
if (!non_significant_slice_segment_flag) | 
slice_segment_data( ) | 
rbsp_slice_segment_trailing_bits( ) | 
} | 

## Slide 6: Conclusions
  To support tiled streaming without transcoding at CTU level, proposed the signaling of non-significant slice segments with syntax modifications in
  slice_segment_header and
  slice_segment_rbsp
Propose to be adopted to HEVC extension.