## Slide 1: Color gamut scalable video coding with piecewise linear prediction and shift-offset model
Cheung Auyeung and Kazushi Sato
Sony Electronics Inc. / Sony Corp.
July 27, 2013

## Slide 2: Introduction
JCTVC-K0241 proposed a color gamut scalable system
JCTVC-L0334 presented results using two color space prediction methods in the color gamut scalable coder:
  Gain-Offset
  Bit-increment
This contribution presented results with two additional color space prediction methods:
  Piecewise Linear
  Shift-offset
Input
BT.709
Input
BT.2020
Base Layer
Encoding Loop
Enhancement Layer
Encoding Loop
Base Layer
Reference
Bitstream
Multiplex
Enhancement Layer
Reference
Color Space
Predictor
Upsampling
10 bits
10 bits
8 bits
8 bits
Color Space Scalable Coder

## Slide 3: Color Space Predictors
256
1024
8 bits BT.709 input
10 Bits BT.2020 Output
256
1024
8 bits BT.709 input
10 Bits BT.2020 Output
256
1024
8 bits BT.709 input
10 Bits BT.2020 Output
256
1024
8 bits BT.709 input
10 Bits BT.2020 Output
Shift-Offset
  Bit-increment
  Gain-Offset
  Piecewise Linear
fixed slope = 4
fixed offset = 0
fixed slope = 4
variable offset
variable slope
variable offset
knot
two variable slopes
one variable knot
JCTVC-L0334 Predictors
Proposed
Predictors

## Slide 4: Piecewise Linear Testing Conditions
The Class A and Class B test sequences are converted into BT.2020 test sequences using software provided by JCTVC-L0334 for this experiment.
Luma QPs are from the SHM-2.0 common test conditions but the QPs of Cb and Cr QP are offset by -2 and -6 as in JCTVC-L0334.
Reference is sequence adaptive Gain-Offset (GO-SA) from JCTVC-L0334 based on SMuC-0.1.1.
  GO-SA parameters are sequence adaptive, QP adaptive, and configuration adaptive.
Test is sequence adaptive Piecewise Linear Prediction (PL-SA) implemented on the GO-SA software from JCTVC-L0334.
  The PL-SA is sequence adaptive. But it is independent on QP and configuration.
Single layer is patched HM8.1rc1 from JCTVC-L0334.
Cross-check is to be reported by Sharp in JCTVC-N0339. Thank you.

## Slide 5: Piecewise Linear Results
The overall luma BDRs for AI-2x, RA-2x, and SNR scalability are -0.8%, -0.7%, and -0.9%, respectively.
There were some losses in BDR for SNR scalability for Cb and Cr at 0.5% and 1.1%.
The coding loss in Cb and Cr in piece-wise linear prediction is likely to be caused by lack of QP and configuration adaptation which were implemented in the Gain-Offset prediction
 | AI HEVC 2x |  |  |  |  | 
 | Y | U | V |  |  | 
Class A | -1.0% | -0.4% | 0.0% |  |  | 
Class B | -0.8% | -0.4% | -0.1% |  |  | 
Overall (Test vs Ref) | -0.8% | -0.4% | -0.1% |  |  | 
Overall (Test vs single layer) | 15.4% | 10.7% | 13.2% |  |  | 
Overall (Ref vs single layer) | 16.4% | 11.2% | 13.2% |  |  | 
Overall (Test EL+BL vs single EL+BL) | -20.2% | -23.5% | -21.9% |  |  | 
Overall (Ref EL+BL vs single EL+BL) | -19.6% | -23.2% | -21.8% |  |  | 
EL only (Test vs Ref) | -1.4% | -0.9% | -0.5% |  |  | 
Enc Time[%] | 100.8% |  |  |  |  | 
Dec Time[%] | 99.0% |  |  |  |  | 
 | RA HEVC 2x |  |  | RA HEVC SNR |  | 
 | Y | U | V | Y | U | V
Class A | -0.8% | 0.0% | -3.8% | -1.2% | -0.7% | -1.4%
Class B | -0.7% | 0.0% | 0.2% | -0.8% | 1.0% | 2.1%
Overall (Test vs Ref) | -0.7% | 0.0% | -0.9% | -0.9% | 0.5% | 1.1%
Overall (Test vs single layer) | 23.3% | 29.0% | 32.0% | 20.4% | 26.8% | 31.3%
Overall (Ref vs single layer) | 24.3% | 29.0% | 33.4% | 21.5% | 26.3% | 30.1%
Overall (Test EL+BL vs single EL+BL) | -13.7% | -9.9% | -7.8% | -17.1% | -12.9% | -10.1%
Overall (Ref EL+BL vs single EL+BL) | -13.0% | -9.9% | -6.9% | -16.3% | -13.2% | -10.9%
EL only (Test vs Ref) | -1.3% | -0.5% | -1.4% | -1.5% | 0.0% | 0.6%
Enc Time[%] | 102.0% |  |  | 102.1% |  | 
Dec Time[%] | 104.2% |  |  | 103.2% |  | 

## Slide 6: Shift-Offset Testing Conditions
Reference is single layer BL and single layer EL output of the patched HM8.1rc1 from JCTVC-L0334.
Tests are the followings:
  Bit-increment (BI) from JCTVC-L0334 based on SMuC-0.1.1
  The shift-offset (SO) implemented in the BI software from JCTVC-L0334.
Cross-check is to be reported by Sharp in JCTVC-N0339. Thank you.
Results:
 | BD-rate (BL+EL) BI |  |  | BD-rate (BL+EL) SO |  | 
 | Y | U | V | Y | U | V
Kimono | -43.6% | -41.7% | -41.0% | -43.7% | -41.7% | -41.2%
ParkScene | -45.3% | -46.0% | -43.4% | -45.4% | -46.0% | -43.7%
Cactus | -41.1% | -40.2% | -34.4% | -40.9% | -39.9% | -34.0%
BasketballDrive | -38.7% | -36.8% | -30.1% | -38.8% | -36.7% | -29.3%
BQTerrace | -47.6% | -48.0% | -41.5% | -47.6% | -48.0% | -41.4%
 | BD-rate (EL) BI |  |  | BD-rate (EL) SO |  | 
 | Y | U | V | Y | U | V
Kimono | -88.7% | -87.5% | -87.2% | -88.8% | -87.7% | -87.4%
ParkScene | -91.4% | -91.3% | -90.6% | -91.5% | -91.4% | -90.7%
Cactus | -82.8% | -82.4% | -80.9% | -82.3% | -81.9% | -80.3%
BasketballDrive | -77.5% | -76.6% | -74.3% | -77.7% | -76.8% | -74.2%
BQTerrace | -94.0% | -94.2% | -93.5% | -94.0% | -94.2% | -93.4%

## Slide 7: Conclusions
Provided results to compare Gain-Offset prediction and the Piecewise Linear prediction for color space prediction.
Propose to continuous study in color gamut scalability.