## Slide 1: JCTVC-N0272
Non-SCE1: On handling re-sampling phase offsets with fixed filters
Koohyar Minoo, David Baylon and Ajay Luthra
ARRIS

## Slide 2: Performance of phase offset resolution vs. exact phase
Sources of phase error with fixed filters and signaling one offset:
Phase offset error due to phase resolution:
  Rounding error associated with mapping an EL sample positions to fractional sample position on a fixed grid in the BL (e.g. in the case 1.5x studied in SCE1 is 0.33/16)
Phase offset error due to fixed precision of phase index:
  Rounding error associated with signaling phase offset with limited precision (e.g. in the case of 1.5x studied in SCE1 is 0.33/16 using 1/16 resolution)

## Slide 3: Performance of phase offset resolution vs. exact phase
resolution | index | ¦ offset error * 16 ¦ | % BDR rate
1/16 (SCE1-test1.2) | 2, 8, 13 | 0.667, 0, 0.333 | 0.6%
1/8 | 3, 9, 14 | 0.333, 1, 0.667 | 1.3%
1/4 | 1, 7, 12 | 1.667, 1, 1.333 | 3.3%
1/16 N0272 | 3, 8, 13 | 0.333, 0, 0.333 | 0.2%
Fixed phase offset resolution (Test 1.2) vs. exact phase (Test 2.2) for luma 1.5x scalability
For the case of 1.5x scalability within SCE1 3 sub-pel filters needed are at locations, 1/6, 1/2 and 5/6 pel. Which on a grid of 16 correspond to:
2.67, 8 and 13.33.

## Slide 4: One solution to Elminate phase offset error (with fixed filters)
Syntax for signaling of filter offsets
Re-mapping of phase indices at PPS level

## Slide 5: Benefitsof Mapping phase indices
Simulations for 1.5x indicate improvement of 0.4% (luma) for 1/16 phase resolution case
No need for rounding to closest 1/16th location (Truncation will do it)