## Slide 1: Non-RCE2 Rice parameter extension for transform-skip blocks
Seung-Hwan Kim, Kiran Misra, Andrew Segall
(JCTVC-N0281)

## Slide 2: Organization
Motivation
Proposed Method
Results
Conclusions

## Slide 3: Motivation
Remaining abs_level Coding for TS blocks
  Maximum RP is limited by 4
  Lossless coding
  High bit-depth coding (bit depth >8)
  High bitrates coding

## Slide 4: Proposed Solution
Rice parameter signaling
  Send ‘rice-parameter’ for each transform-skip block
  Maximum RP is extended to ‘6’
  Signal rice-parameter from the given set {0, 2, 4, 6}
  Remove rice-parameter update process

## Slide 5: Results (Lossless)
Provide high coding performance for screen content where the optimal rice-parameter is found to be large

## Slide 6: Results (Lossy with a slice level flag)
A Slice level flag is considered to control the usage of the rice-parameter signaling method
  If the flag is set to one rice-parameter signaling method is used for TS blocks for the given slice.
  Ex: The flag is set to one when slice QP <32

## Slide 7: Conclusions
Send rice-parameter for each transform-skip block
Simulations demonstrate that the proposed rice-parameter signaling method provides high coding efficiency for lossless and high bitrates coding.
Remove the dependency from previous level information