## Slide 1
JCTVC-N0285
Non-RCE3: Intra motion compensation for screen contents
Junghye Min, Min Woo Park, Sunil Lee, Chanyul Kim

## Slide 2: Summary
A motion compensation method for intra coding of screen contents is proposed.
    The proposed method uses only 4 positions in the decoded area for motion compensation candidates.
Performance (AI )
 | Lossless | Lossy (Y,U,V)
Class F | -0.4% | -1.7%/-1.9%/-1.8%
Class D | 0.0% | 0.0%/-0.1%/-0.1%
SC RGB 444 | -10.2% | -12.2%/-12.4%/-12.7%
SC YUV 444 | -7.6% | -9.5%/-9.5%/-9.7%
RangeExt | 0.0% | 0.0%/0.0%/-0.1%

## Slide 3: Introductions
Screen contents have strong correlations along horizontal and vertical directions
  Intra motion compensation along these two directions is effective for intra coding of screen contents
Real time encoding/decoding is critical issue for screen contents coding.
  Simplified design is required.

## Slide 4: Proposed method
4 candidate positions in the decoded area along horizontal and vertical directions are used for candidate positions for motion compensation
Position index is signalled using unary code.

## Slide 5: Experimental results
 | All Intra Main |  |  | Random Access Main |  |  | Low delay B Main |  | 
 | compression ratio |  | Bit-rate saving | compression ratio |  | Bit-rate saving | compression ratio |  | Bit-rate saving
 | Reference | Tested |  | Reference | Tested |  | Reference | Tested | 
Class F | 5.2 | 5.3 | -0.4% | 31.7 | 31.8 | -0.2% | 49.8 | 49.9 | -0.1%
Class B | 2.2 | 2.2 | 0.0% | 2.6 | 2.6 | 0.0% | 2.6 | 2.6 | 0.0%
SC RGB 444 | 10.1 | 11.9 | -10.2% | 100.4 | 120.0 | -8.7% | 381.6 | 436.4 | -6.3%
SC YUV 444 | 11.4 | 13.4 | -7.6% | 128.9 | 150.3 | -6.8% | 325.6 | 369.9 | -5.7%
RangeExt | 2.4 | 2.4 | 0.0% | 2.5 | 2.5 | 0.0% | 2.5 | 2.5 | 0.0%
Enc Time[%] | 133% |  |  | 109% |  |  | 107% |  | 
Dec Time[%] | 96% |  |  | 102% |  |  | 104% |  | 
 | All Intra HE Main-tier |  |  | All Intra HE High-tier |  |  | All Intra HE Super-High-tier |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class F | -1.7% | -1.9% | -1.8% | -1.5% | -1.6% | -1.6% | -1.3% | -1.4% | -1.4%
Class B | 0.0% | -0.1% | -0.1% | 0.0% | -0.1% | -0.1% | 0.0% | 0.0% | 0.0%
SC RGB 444 | -12.2% | -12.4% | -12.7% | -12.2% | -12.5% | -12.6% | -12.3% | -12.4% | -12.5%
SC YUV 444 | -9.5% | -9.5% | -9.7% | -9.2% | -9.4% | -9.5% | -9.1% | -9.2% | -9.2%
RangeExt | 0.0% | 0.0% | -0.1% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Enc Time[%] | 126% |  |  | 127% |  |  | 128% |  | 
Dec Time[%] | 87% |  |  | 87% |  |  | 87% |  | 
 | Random Access HE Main-tier |  |  | Random Access HE High-tier |  |  |  |  | 
 | Y | U | V | Y | U | V |  |  | 
Class F | -1.4% | -1.6% | -1.6% | -1.2% | -1.4% | -1.3% |  |  | 
Class B | 0.0% | 0.0% | -0.1% | 0.0% | 0.0% | 0.0% |  |  | 
SC RGB 444 | -9.8% | -9.6% | -9.8% | -9.6% | -9.5% | -9.6% |  |  | 
SC YUV 444 | -7.9% | -7.9% | -8.1% | -7.7% | -7.6% | -7.7% |  |  | 
RangeExt | -0.1% | -0.1% | -0.1% | 0.0% | 0.0% | 0.0% |  |  | 
Enc Time[%] | 111% |  |  | 112% |  |  |  |  | 
Dec Time[%] | 110% |  |  | 109% |  |  |  |  | 
 | Low delay B HE Main-tier |  |  | Low delay B HE High-tier |  |  |  |  | 
 | Y | U | V | Y | U | V |  |  | 
Class F | -1.1% | -1.8% | -1.4% | -0.9% | -1.2% | -1.1% |  |  | 
Class B | 0.0% | -0.2% | -0.1% | 0.0% | 0.0% | 0.0% |  |  | 
SC RGB 444 | -4.8% | -4.1% | -4.2% | -5.0% | -4.2% | -4.2% |  |  | 
SC YUV 444 | -5.0% | -4.7% | -4.9% | -5.0% | -4.6% | -4.7% |  |  | 
RangeExt | 0.0% | -0.1% | -0.1% | 0.0% | 0.0% | 0.0% |  |  | 
Enc Time[%] | 108% |  |  | 109% |  |  |  |  | 
Dec Time[%] | 114% |  |  | 114% |  |  |  |  | 
Lossless
Max : pcb-layout (AI, 37%)
Lossy
Max: pcp-layout
(AI,-35.7% -36.1% -37.4%)
Encoder complexity optimization has not been applied yet.

## Slide 6: Conclusions
Simplified design of intra motion compensation was proposed.
The proposed method provides -10.2% and -12.2% luma gains for lossless and lossy AI conditions.
We would like to thank qualcomm for the crosscheck of this proposal.

## Slide 7
Thank you !