## Slide 1
MV-HEVC/SHVC HLS: Ultra-low delay with SHVC, MV-HEVC and 3D-HEVC
JCTVC-N0290/JCT3V-E0098
Robert Skupin, Karsten Sühring, Yago Sanchez, Thomas Schierl

## Slide 2: Problem Statement
Ultra-low delay (ULD) operation of base HEVC based on spatial segmentation and DU based HRD operation.
Current HEVC extension drafts disallow ULD operation: all DUs of layer n precede all DUs of layer (n+1)
Exemplary order of DUs within a 3 layer AU:

## Slide 3: Proposal
ULD operation with HEVC extensions requires appropriate
    NAL unit bitstream order
    HRD operation
    Control ULD mode through VPS extension flag: du_interleaving_enabled_flag

## Slide 4: Proposal – NALU bitstream order
Complement current extension drafts
A coded picture with nuh_layer_id equal to nuhLayerIdA shall precede in decoding order all coded pictures with nuh_layer_id greater than nuhLayerIdA in the same access unit.
with highlighted text:
If du_interleaving_enabled_flag is equal to 0, all VCL NAL units of a A coded picture with nuh_layer_id equal to nuhLayerIdA shall precede in decoding order the VCL NAL units of all coded pictures with nuh_layer_id greater than nuhLayerIdA in the same access unit.
Otherwise (du_interleaving_enabled_flag is equal to 1), all VCL NAL units of decoding unit m with nuh_layer_id equal to nuhLayerIdA shall precede in decoding order all VCL NAL units of decoding unit n with nuh_layer_id greater than nuhLayerIdA in the same access unit for which the decoding process depends on syntax elements or decoded sample values that belong to the decoding unit m.

## Slide 5: Proposal – HRD operation
    In ULD mode:
    Decoding unit information SEI conveys DU CPB removal timings (du_interleaving_enabled_flag equal to 1)
Incapable devices fall back to AU based operation.
AU recombination with nuh_layer_id and NALU order as ordering constraint:
    Single CPB: Non-consecutive memory access
    Per-layer CPB: Consecutive layer-wise recombination

## Slide 6: CPB layouts
Multiple CPBs
Single CPB

## Slide 7: Summary
Current HEVC extension drafts disallow ULD operation
Proposed modifications:
    Add ULD control flag du_interleaving_enabled_flag
    Adjust bitstream order of DUs in ULD mode
    AU based HRD operation as fall back
    AU recombination based on nuh_layer_id and NALU order