## Slide 1: JCTVC-N0354 Non-RCE2: Results for combination of mirroring of non-transformed residual blocks (Test B.3) with other methods
R&D
© BBC MMXIII
Rajitha Weerakkody, Matteo Naccari and Marta Mrak
BBC Research and Development

## Slide 2: Combination of proposals from RCE2 and 8x8 TS
Mirroring of non-transformed residual blocks
  For non-transformed blocks of size 4×4 only
  For non-transformed blocks of size up to 8×8
Replacement of Intra DC mode (JCTVC-N0053)
Extension of RDPCM to inter and lossy (JCTVC-N0083)
Rice Parameter update and initialization (JCTVC-N0222)
  Setting: Applied to transform and transform skip & max Rice equal to 5 with fast update
Extension of transform skip to 8×8 (JCTVC-N0288)
  Setting: Fast encoder method

## Slide 3: Results Lossless coding (mirroring on 4x4 blocks only)
 | All Intra Main | Random Access Main | Low delay B Main
Class F | -5.6% | -6.3% | -7.2%
Class B | -2.1% | -0.8% | -0.7%
SC RGB 444 | -16.0% | -15.8% | -16.4%
SC YUV 444 | -11.8% | -12.1% | -13.2%
RangeExt | -4.1% | -3.0% | -3.0%
Enc Time[%] | 94% | 103% | 102%
Dec Time[%] | 97% | 99% | 97%

## Slide 4: Results Mirroring for 4x4 blocks
 | All Intra HE Main-tier |  |  | All Intra HE High-tier |  |  | All Intra HE Super-High-tier |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class F | -6.1% | -6.5% | -6.8% | -6.5% | -6.9% | -7.1% | -6.7% | -7.1% | -7.2%
Class B | -0.1% | 0.0% | 0.0% | -0.1% | 0.0% | 0.0% | -0.1% | 0.0% | 0.0%
SC RGB 444 | -13.3% | -13.2% | -13.0% | -15.5% | -15.4% | -15.2% | -17.3% | -17.3% | -17.1%
SC YUV 444 | -8.5% | -8.6% | -8.7% | -9.4% | -9.9% | -9.9% | -10.6% | -11.1% | -11.2%
RangeExt | -0.3% | -0.1% | -0.3% | -0.3% | -0.1% | -0.2% | -0.2% | -0.1% | -0.2%
Enc Time[%] | 115% |  |  | 115% |  |  | 114% |  | 
Dec Time[%] | 101% |  |  | 101% |  |  | 101% |  | 
 | Random Access HE Main-tier |  |  | Random Access HE High-tier |  |  |  |  | 
 | Y | U | V | Y | U | V |  |  | 
Class F | -4.2% | -4.3% | -4.7% | -4.3% | -4.3% | -4.6% |  |  | 
Class B | 0.0% | 0.0% | 0.1% | -0.1% | 0.1% | 0.0% |  |  | 
SC RGB 444 | -10.5% | -10.5% | -10.4% | -12.5% | -12.4% | -12.3% |  |  | 
SC YUV 444 | -6.8% | -7.0% | -7.0% | -7.4% | -7.9% | -7.8% |  |  | 
RangeExt | -0.2% | 0.0% | 0.0% | -0.2% | 0.1% | 0.0% |  |  | 
Enc Time[%] | 111% |  |  | 111% |  |  |  |  | 
Dec Time[%] | 102% |  |  | 102% |  |  |  |  | 
 | Low delay B HE Main-tier |  |  | Low delay B HE High-tier |  |  |  |  | 
 | Y | U | V | Y | U | V |  |  | 
Class F | -2.9% | -2.3% | -2.6% | -2.9% | -2.7% | -2.9% |  |  | 
Class B | 0.0% | 0.1% | 0.1% | 0.0% | 0.2% | 0.1% |  |  | 
SC RGB 444 | -11.1% | -11.1% | -11.1% | -13.0% | -12.8% | -12.8% |  |  | 
SC YUV 444 | -5.4% | -5.3% | -5.5% | -6.1% | -6.3% | -6.3% |  |  | 
RangeExt | -0.1% | 0.1% | 0.3% | 0.1% | 0.3% | 0.5% |  |  | 
Enc Time[%] | 109% |  |  | 110% |  |  |  |  | 
Dec Time[%] | 102% |  |  | 103% |  |  |  |  | 

## Slide 5: Results Mirroring for 4x4 and 8x8 blocks
 | All Intra HE Main-tier |  |  | All Intra HE High-tier |  |  | All Intra HE Super-High-tier |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class F | -6.2% | -6.6% | -6.9% | -6.6% | -7.0% | -7.2% | -6.8% | -7.2% | -7.3%
Class B | -0.1% | 0.0% | 0.0% | -0.1% | 0.0% | 0.0% | -0.1% | 0.0% | 0.0%
SC RGB 444 | -13.4% | -13.3% | -13.2% | -15.6% | -15.5% | -15.4% | -17.3% | -17.4% | -17.2%
SC YUV 444 | -8.7% | -8.8% | -8.9% | -9.5% | -10.1% | -10.1% | -10.7% | -11.3% | -11.3%
RangeExt | -0.3% | -0.1% | -0.3% | -0.3% | -0.1% | -0.2% | -0.2% | -0.1% | -0.2%
Enc Time[%] | 115% |  |  | 115% |  |  | 114% |  | 
Dec Time[%] | 100% |  |  | 100% |  |  | 100% |  | 
 | Random Access HE Main-tier |  |  | Random Access HE High-tier |  |  |  |  | 
 | Y | U | V | Y | U | V |  |  | 
Class F | -4.3% | -4.5% | -4.7% | -4.3% | -4.4% | -4.6% |  |  | 
Class B | 0.0% | 0.1% | 0.1% | 0.0% | 0.1% | 0.0% |  |  | 
SC RGB 444 | -10.5% | -10.6% | -10.5% | -12.4% | -12.5% | -12.4% |  |  | 
SC YUV 444 | -6.7% | -6.9% | -6.9% | -7.2% | -7.7% | -7.7% |  |  | 
RangeExt | -0.2% | -0.1% | 0.0% | -0.1% | 0.1% | 0.0% |  |  | 
Enc Time[%] | 111% |  |  | 111% |  |  |  |  | 
Dec Time[%] | 102% |  |  | 102% |  |  |  |  | 
 | Low delay B HE Main-tier |  |  | Low delay B HE High-tier |  |  |  |  | 
 | Y | U | V | Y | U | V |  |  | 
Class F | -3.0% | -2.7% | -3.1% | -2.9% | -2.8% | -3.2% |  |  | 
Class B | 0.0% | 0.2% | 0.1% | 0.0% | 0.1% | 0.0% |  |  | 
SC RGB 444 | -10.9% | -11.0% | -11.0% | -12.9% | -12.8% | -12.7% |  |  | 
SC YUV 444 | -5.6% | -5.2% | -5.6% | -5.9% | -6.0% | -6.2% |  |  | 
RangeExt | 0.0% | 0.0% | 0.1% | 0.1% | 0.2% | 0.4% |  |  | 
Enc Time[%] | 109% |  |  | 110% |  |  |  |  | 
Dec Time[%] | 102% |  |  | 103% |  |  |  |  |