## Slide 1: JCTVC-O0035: RCE1: Summary Report of HEVC Range Extensions Core Experiment 1 on Inter-Component Decorrelation Methods
15th JCT-VC Meeting: Geneva, CH, 23 Oct. – 1 Nov. 2013
Woo-Shik Kim and T. Nguyen

## Slide 2: Introduction
HEVC RExt covers RGB and YCbCr 4:4:4 coding to provide better color fidelity
  There are both professional and consumer applications requiring high color fidelity
YCbCr 4:4:4 coding works better in low bitrate range, but there is limit in quality*
RGB coding usually consumes more bits due to correlation between color components
RCE1 studies inter-color-component decorrelation methods
  Better coding efficiency than YCbCr 4:4:4 coding
  High color fidelity as RGB coding
* A. Minezawa et al, “AHG5/AHG8: On RGB to YCbCr conversion for screen contents,” ITU-T SG16 WP3 and ISO/IEC JTC1/SC29/WG11, Document JCTVC-N0115, Jul. 2013.

## Slide 3: Experiments Description
Adaptive inter-color-component residual prediction in JCTVC-N0266
  Chroma residual signal is predicted from the reconstructed luma residual signal scaled by alpha
  Alpha is selected among {-8, -4, -2, -1, 0, 1, 2, 4, 8}
  Alpha is signaled for each TU if luma cbf is not zero
  In case of intra coding, it is applied only for DM mode
Encoder:
Decoder:

## Slide 4: Experiments Description
Use of non-reconstructed luma residue
  Chroma residual signal is predicted from the non-reconstructed luma residual signal scaled by alpha
  Encoder only modification
  Implementation complexity reduction by facilitating parallel processing
Encoder:
Decoder:
luma coeff parsing
chroma coeff parsing
IQ/IT
IQ/IT
residual prediction
luma prediction
chroma preciction
T/Q
residual prediction
T/Q
<encoding>
<decoding>
…
…
…
…
luma coding
chroma coding

## Slide 5: Experiments Description
PU based signaling for inter coding
Combination of 3 and 2

## Slide 6: Experimental Results
RGB coding
YUV 4:4:4 coding
 | AI |  |  | RA |  |  | LB |  | 
 | G | B | R | G | B | R | G | B | R
Exp1 | -18.1% | -16.6% | -17.3% | -14.5% | -11.9% | -13.7% | -13.6% | -9.2% | -10.8%
Exp2 | -18.1% | -16.6% | -17.3% | -14.1% | -11.7% | -13.5% | -12.6% | -8.7% | -10.1%
Exp3 | -18.1% | -16.6% | -17.3% | -14.2% | -11.8% | -13.6% | -13.0% | -9.1% | -10.5%
Exp4 | -18.1% | -16.6% | -17.3% | -13.9% | -11.8% | -13.4% | -12.3% | -8.8% | -10.0%
 | AI |  |  | RA |  |  | LB |  | 
 | G | B | R | G | B | R | G | B | R
Exp1 | -1.4% | -6.5% | -6.7% | -0.5% | -8.5% | -7.3% | -0.2% | -6.1% | -5.8%
Exp2 | -1.4% | -6.6% | -6.9% | -0.5% | -8.2% | -7.2% | -0.2% | -5.8% | -5.4%
Exp3 | -1.4% | -6.5% | -6.7% | -0.5% | -8.3% | -7.2% | -0.1% | -6.2% | -5.6%
Exp4 | -1.4% | -6.6% | -6.9% | -0.5% | -8.3% | -7.1% | -0.1% | -5.9% | -5.3%

## Slide 7: Experimental Results
Performance on SCC
 | All Intra HE Main-tier |  | 
 | Y | U | V
SC RGB 444 | -26.0% | -25.7% | -26.0%
Animation RGB 444 | -25.9% | -25.7% | -24.5%
SC YUV 444 | -4.5% | -8.0% | -7.9%
Animation YUV 444 | -2.6% | -11.5% | -7.2%
RangeExt | -1.7% | -5.6% | -11.1%
SC(444) GBR Optional | -24.2% | -24.5% | -24.8%
SC(444) YUV Optional | -7.2% | -8.3% | -7.3%
Enc Time[%] | 113% |  | 
Dec Time[%] | 100% |  | 
 | Random Access HE Main-tier |  | 
 | Y | U | V
SC RGB 444 | -23.2% | -23.1% | -23.5%
Animation RGB 444 | -20.0% | -19.9% | -18.4%
SC YUV 444 | -3.5% | -7.8% | -7.8%
Animation YUV 444 | -1.0% | -11.1% | -6.3%
RangeExt | -0.8% | -8.5% | -11.2%
SC(444) GBR Optional | -23.4% | -23.5% | -23.7%
SC(444) YUV Optional | -6.0% | -7.9% | -6.4%
Enc Time[%] | 109% |  | 
Dec Time[%] | 102% |  | 
 | Low delay B HE Main-tier |  | 
 | Y | U | V
SC RGB 444 | -20.9% | -20.3% | -20.8%
Animation RGB 444 | -18.9% | -16.9% | -15.6%
SC YUV 444 | -2.7% | -6.8% | -7.1%
Animation YUV 444 | -0.4% | -9.3% | -4.1%
RangeExt | -0.4% | -5.2% | -7.5%
SC(444) GBR Optional | -21.1% | -21.1% | -21.5%
SC(444) YUV Optional | -8.6% | -10.2% | -9.1%
Enc Time[%] | 107% |  | 
Dec Time[%] | 102% |  | 

## Slide 8: Comparison to RGB/YCbCr 4:4:4
Theoretical performance limit of YCbCr 4:4:4
  Distortion due to forward transform: 1/12
  Distortion from backward transform: a2/12
BT 709:
 | 8 bit | 10 bit
R | 52.41 | 64.48
G | 55.39 | 67.46
B | 51.56 | 63.63
average | 53.48 | 65.55
< achievable PSNR (dB) >

## Slide 9: Comparison to RGB/YCbCr 4:4:4

## Slide 10: Interpretation of Chroma Gain
Larger gain in chroma components in YCbCr 4:4:4
Applied 1.5xlambda_chroma to measure overall performance
 | All Intra HE Main-tier |  | 
 | Y | U | V
YCbCr 4:4:4 | -5.4% | -0.2% | -1.3%
 | Random Access HE Main-tier |  | 
 | Y | U | V
YCbCr 4:4:4 | -4.4% | -3.8% | -2.3%
 | Low delay B HE Main-tier |  | 
 | Y | U | V
YCbCr 4:4:4 | -6.3% | -0.6% | -0.2%

## Slide 11: Complexity
Complexity for prediction
  Additional complexity to access luma residue
  Simple calculation with a few shift/addition operations
Complexity reduction
  Use of non-reconstructed luma residue at encoder
  No need for parameter calculation at decoder
  Chroma DM only for intra coding
HM run time
  19% intra, 12% inter increment at encoder
  0% increment at decoder

## Slide 12: Conclusion
Coding efficiency improvement
  Large gain in RGB coding
    17/13/11 % in AI/RA/LB
  Large gain in chroma in YCbCr 4:4:4 coding
    7/7/6 % in AI/RA/LB, which can be more than 5% luma gain
  More gain in screen contents
    21/26/19 % in AI/RA/LB in RGB
    4/2/2 % luma and 9/8/7 % chroma in AI/RA/LB in YCbCr 4:4:4
High color fidelity
  Similar PSNR to RGB coding
  Better PSNR than YCbCr 4:4:4 coding

## Slide 13: Related Non-RCE1 Documents
A. Khairat, T. Nguyen, M. Siekmann, and D. Marpe, “Non-RCE1: Extended adaptive inter-component prediction,” JCTVC-O0150, Oct. 2013.
K. Kawamura and S. Naito, “Non-RCE1: Inter colour-component residual coefficients prediction,” JCTVC-O0263, Oct. 2013.