## Slide 1: AHG 5 and 18: Entropy Coding Throughput for High Bit Depths
JCTVC-O0046
Broadcast & Professional Research Labs
Sony Europe Ltd.
Karl Sharman
Sony Corp.

## Slide 2: Background (from JCTVC-M0178)
Many of the bits at QP<0 will be equi-probable (EP) bins.
EP bins require a subtraction to decode.
  The subtractions to decode multiple EP bins require sequential processing.
To decode N EP bins,
  The process can be thought of as a N-stage long division by ivlCurrRange1
An example of EP decoding is as follows:
      Note 1: ivlCurrRange is equivalent to m_uiRange in HM.

## Slide 3: Worked Example: ivlCurrRange = 458
bit-stream
ivlOffset = 303
1
0
0
1
0
1
1
1
1
1
1
1
0
1
0
DecodeBypass
ivlOffset = ivlOffset<<1 ivlOffset = ivlOffset | read_bits(1)
ivlOffset >= ivlCurrRange ?
ivlOffset = ivlOffset – ivlCurrRange
binVal = 1
binVal = 0
Done
?
Decoded bins:
No
Yes

## Slide 4: Worked Example: ivlCurrRange = 458
bit-stream
ivlOffset = 607
1
0
0
1
0
1
1
1
1
1
1
1
0
1
0
DecodeBypass
ivlOffset = ivlOffset<<1 ivlOffset = ivlOffset | read_bits(1)
ivlOffset >= ivlCurrRange ?
ivlOffset = ivlOffset – ivlCurrRange
binVal = 1
binVal = 0
Done
?
Decoded bins:
No
Yes

## Slide 5: Worked Example: ivlCurrRange = 458
bit-stream
ivlOffset = 607
1
0
0
1
0
1
1
1
1
1
1
1
0
1
0
DecodeBypass
ivlOffset = ivlOffset<<1 ivlOffset = ivlOffset | read_bits(1)
ivlOffset >= ivlCurrRange ?
ivlOffset = ivlOffset – ivlCurrRange
binVal = 1
binVal = 0
Done
?
Decoded bins:
No
Yes

## Slide 6: Worked Example: ivlCurrRange = 458
bit-stream
ivlOffset = 149
0
0
1
0
0
1
0
1
0
1
1
1
0
1
0
DecodeBypass
ivlOffset = ivlOffset<<1 ivlOffset = ivlOffset | read_bits(1)
ivlOffset >= ivlCurrRange ?
binVal = 0
Done
1
?
Decoded bins:
No
Yes
ivlOffset = ivlOffset – ivlCurrRange
binVal = 1

## Slide 7: Worked Example: ivlCurrRange = 458
bit-stream
ivlOffset = 149
0
1
0
0
1
0
1
0
1
1
1
0
1
0
0
DecodeBypass
ivlOffset = ivlOffset<<1 ivlOffset = ivlOffset | read_bits(1)
ivlOffset >= ivlCurrRange ?
ivlOffset = ivlOffset – ivlCurrRange
binVal = 1
binVal = 0
Done
1
Decoded bins:
No
Yes
?

## Slide 8: Worked Example: ivlCurrRange = 458
bit-stream
ivlOffset = 299
0
1
0
0
1
0
1
0
1
1
1
0
1
0
0
DecodeBypass
ivlOffset = ivlOffset<<1 ivlOffset = ivlOffset | read_bits(1)
ivlOffset >= ivlCurrRange ?
ivlOffset = ivlOffset – ivlCurrRange
binVal = 1
binVal = 0
Done
1
Decoded bins:
No
Yes
?

## Slide 9: Worked Example: ivlCurrRange = 458
bit-stream
ivlOffset = 299
0
1
0
0
1
0
1
0
1
1
1
0
1
0
0
DecodeBypass
ivlOffset = ivlOffset<<1 ivlOffset = ivlOffset | read_bits(1)
ivlOffset >= ivlCurrRange ?
ivlOffset = ivlOffset – ivlCurrRange
binVal = 1
binVal = 0
Done
1
Decoded bins:
No
Yes
?

## Slide 10: Worked Example: ivlCurrRange = 458
bit-stream
ivlOffset = 299
0
1
0
0
1
0
1
0
1
1
1
0
1
0
0
DecodeBypass
ivlOffset = ivlOffset<<1 ivlOffset = ivlOffset | read_bits(1)
ivlOffset >= ivlCurrRange ?
ivlOffset = ivlOffset – ivlCurrRange
binVal = 1
binVal = 0
Done
1
Decoded bins:
No
Yes
0

## Slide 11: Worked Example: ivlCurrRange = 458
bit-stream
ivlOffset = 299
1
0
0
1
0
1
0
1
1
1
0
1
0
0
1
DecodeBypass
ivlOffset = ivlOffset<<1 ivlOffset = ivlOffset | read_bits(1)
ivlOffset >= ivlCurrRange ?
ivlOffset = ivlOffset – ivlCurrRange
binVal = 1
binVal = 0
Done
1
Decoded bins:
No
Yes
0

## Slide 12: Background (continued)
However, when ivlCurrRange=256, the process can be significantly simplified:

## Slide 13: Worked Example: ivlCurrRange=256
bit-stream
ivlOffset = 189
0
1
0
1
1
1
1
0
1
1
1
0
1
0
1
DecodeBypass
ivlOffset = ivlOffset<<1 ivlOffset = ivlOffset | read_bits(1)
ivlOffset >= ivlCurrRange ?
ivlOffset = ivlOffset – ivlCurrRange
binVal = 1
binVal = 0
Done
?
Decoded bins:
No
Yes
8
7
6
5
4
3
2
1
0
Bit

## Slide 14: Worked Example: ivlCurrRange=256
bit-stream
ivlOffset = 189
0
1
0
1
1
1
1
0
1
1
1
0
1
0
1
DecodeBypass
ivlOffset = ivlOffset<<1 ivlOffset = ivlOffset | read_bits(1)
ivlOffset >= ivlCurrRange ?
ivlOffset = ivlOffset – ivlCurrRange
binVal = 1
binVal = 0
Done
?
Decoded bins:
No
Yes
Always 0
8
7
6
5
4
3
2
1
0
Bit

## Slide 15: Worked Example: ivlCurrRange=256
bit-stream
ivlOffset = 189
0
1
0
1
1
1
1
0
1
1
1
0
1
0
1
DecodeBypass
ivlOffset = ivlOffset<<1 ivlOffset = ivlOffset | read_bits(1)
Test bit 8 of ivlOffset
ivlOffset = ivlOffset – ivlCurrRange
binVal = 1
binVal = 0
Done
?
Decoded bins:
0
1
Always 0
8
7
6
5
4
3
2
1
0
Bit
NOTE: Since ivlOffset has been left-shifted by 1, the test/clear on bit 8 is equivalent to a test/clear on bit 7 in the above diagram.

## Slide 16: Worked Example: ivlCurrRange=256
bit-stream
ivlOffset = 189
0
1
0
1
1
1
1
0
1
1
1
0
1
0
1
DecodeBypass
ivlOffset = ivlOffset<<1 ivlOffset = ivlOffset | read_bits(1)
Test bit 8 of ivlOffset
Clear bit 8 of ivlOffset
binVal = 1
binVal = 0
Done
?
Decoded bins:
0
1
Always 0
8
7
6
5
4
3
2
1
0
Bit
NOTE: Since ivlOffset has been left-shifted by 1, the test/clear on bit 8 is equivalent to a test/clear on bit 7 in the above diagram.

## Slide 17: Worked Example: ivlCurrRange=256
bit-stream
ivlOffset = 189
0
1
0
1
1
1
1
0
1
1
1
0
1
0
1
DecodeBypass
ivlOffset = ivlOffset<<1 ivlOffset = ivlOffset | read_bits(1)
Test bit 8 of ivlOffset
binVal = ivlOffset bit 8
Clear bit 8 of ivlOffset
binVal = ivlOffset bit 8 Clear bit 8 of ivlOffset
Done
?
Decoded bins:
0
1
Always 0
8
7
6
5
4
3
2
1
0
Bit
NOTE: Since ivlOffset has been left-shifted by 1, the test/clear on bit 8 is equivalent to a test/clear on bit 7 in the above diagram.

## Slide 18: Worked Example: ivlCurrRange=256
bit-stream
ivlOffset = 189
0
1
0
1
1
1
1
0
1
1
1
0
1
0
1
DecodeBypass
ivlOffset = ivlOffset<<1 ivlOffset = ivlOffset | read_bits(1)
binVal = ivlOffset bit 8
Clear bit 8 of ivlOffset
Done
1
Decoded bins:
Always 0
8
7
6
5
4
3
2
1
0
Bit

## Slide 19: Worked Example: ivlCurrRange=256
bit-stream
ivlOffset = 189
0
1
0
1
1
1
1
0
1
1
1
0
1
0
1
DecodeBypass
binVal = ivlOffset bit 7
Clear bit 7 of ivlOffset
ivlOffset = ivlOffset<<1 ivlOffset = ivlOffset | read_bits(1)
Done
1
Decoded bins:
Always 0
8
7
6
5
4
3
2
1
0
Bit

## Slide 20: Worked Example: ivlCurrRange=256
bit-stream
ivlOffset = 189
0
1
0
1
1
1
1
0
1
1
1
0
1
0
1
DecodeBypass
Done
1
Decoded bins:
0
1
1
1
1
0
binVal = ivlOffset bit 7
Clear bit 7 of ivlOffset
ivlOffset = ivlOffset<<1 ivlOffset = ivlOffset | read_bits(1)

## Slide 21: Benefits When ivlCurrRange = 256
When ivlCurrRange = 256,
  The EP bins are directly visible in ivlOffset.
  N EP bins can be decoded just by looking at the N most-significant-but-one bits of ivlOffset concatenated with the bit-stream.
  Therefore, in this “aligned” case, decoding of EP bins is trivial.
  Throughput is now limited by bandwidth of buffer.
  Decoding of the worst case of a coefficient’s EP data should be possible within one stream operation.
    Decoding Exponential-Golomb bins just requires some simple logic to determine a shift on a shift register.
How best to achieve this state all of the time?

## Slide 22: Increase CABAC Throughput
Method 1
  The simple method to achieve this high throughput system is:
    Prior to EP bins (e.g. sign bits).
      Set ivlCurrRange = 256 (in encoder and decoder).
  This will waste (on average) 0.55 bits per alignment.
    When there is a large amount of bypass data, this loss is insignificant.

## Slide 23: Increase CABAC Throughput
Method 2
  To reduce the cost to ~0.30 bits per alignment, to align in the decoder:
    if (ivlCurrRange >= 384)
      if (ivlOffset < 256) nextEPBitIsZero = true
      else ivlOffset -= 128
    ivlCurrRange = 256
  This concept is developed further in the main document to reduce the loss, although this reduction is at the expense of implementation complexity.
    Method 2 is believed to be a reasonable trade-off.

## Slide 24: Refining the system
The alignment algorithm has been further refined over JCTVC-M0178 so that it can be used at higher QPs without a significant loss in coding efficiency.
The alignment algorithm is only employed if, for a given coefficient group, there are some non-sign bits that are bypass coded.
This means that for each group of 16 coefficients, the number of CABAC encoded bins is constrained:
  When alignment is used,
    16 (significant map) + 8 (>1 map) + 1 (>2 map) CABAC bins (Total of 25)
    + raw bypass bins
  When alignment is not used,
    16 (significant map) + 8 (>1 map) + 1 (>2 map) CABAC bins (Total of 25)
    + 16 CABAC EP bins (sign bits)

## Slide 25: Proposed System
The proposed system:
  Applies (Method 2) alignment prior to sign bit coding if there are some non sign bit bypass values to code
  The use of alignment is configured by a flag in the Sequence Parameter Set.
    This flag is not present for the Main profiles, and is inferred to be 0 (disabled) when not present.
  The alignment scheme could instead be selected by high bit-rate profiles/levels.

## Slide 26: Results
The conditional alignment has been analysed using the AHG18 high bit depth operating points (as defined in RCE2).
Although the proposal is not targeted at the standard RExt operating points, the results are shown below.
  Intra results are presented here. Inter results are similar.

## Slide 27: Conclusion
Throughput of CABAC at high bit depths and bit rates is a concern.
  There is significantly more data (CABAC EP bins) than at 8-bit operating points.
A method has been proposed to increase throughput.
  This causes the CABAC stream to be bit-aligned, allowing EP bins to be seen in ivlOffset as raw data.
  The alignment is only applied on a condition, which limits each group of 16-coefficients to:
    Up to 25 CABAC-encoded bins, and
    either 16 EP sign bits, or raw escape data.
At the standard RExt AHG5 intra conditions, 0.5%-0.6% losses are observed.
At the high bit depth operating points, the overhead is less than 0.2%, and a decrease in decoding time of 7%-8% is observed.