## Slide 1: MV-HEVC/SHVC HLS: On conversion to ROI-oriented multi-layer bitstream (JCTVC-O0056, JCT3V-F0033)
JCT-VC 15th Meeting in Geneva, CH, 23 Oct. - 2 Nov. 2013
JCT-3V 6th Meeting in Geneva, CH, 23 Oct. - 2 Nov. 2013
Tomoyuki Yamamoto, Tomohiro Ikai, Takeshi Tsukuba
SHARP Corporation

## Slide 2: Summary
This contribution introduces
  ROI-capable scalable video application
  Rewriting process by disposal of non-significant VCL NALU and changing EL picture size.
  Proposed modification to keep alignment between EL and BL pixel correspondence between before and after rewriting.
Proposed modifications:
  Option 1: In SPS, signal pixel position where EL pixel position corresponds to BL integer pixel position.
  Option 2: In SPS, signal phase offset between top-left EL pixel and corresponding BL pixel.

## Slide 3: ROI application using SHVC
BL
EL 00
S. Ha QB Field 3/9
EL: Enhancement Layer
BL: Base Layer
EL00
SHVC encoder
Intelligent network element
BL
EL 21
EL 22
BL
EL 30
EL 20
EL 31
EL 21
EL 10
EL 00
EL 11
EL 01
EL 32
EL 22
EL 33
EL 23
EL 12
EL 02
EL 13
EL 03
BL
EL 21
BL
EL 11
BL
EL 22
BL
EL 30
EL 20
EL 31
EL 21
EL 10
EL 00
EL 11
EL 01
EL 32
EL 22
EL 33
EL 23
EL 12
EL 02
EL 13
EL 03
SHVC bitstream

## Slide 4: System components and data requirements
SHVC encoder / SHVC bitstream
  Part of EL bitstream need to be decoded independent of rest parts of EL. When encoding such EL tile, non-collocated part of BL region could be referenced via inter-layer prediction.
Intelligent Network Element (INE)
  INE receives ROI requests from a user.
  INE extracts the sub bitstream corresponding to the requested ROI from the whole bitstreams.
    Extraction process should be easy. INE could discard NAL units based on NAL unit header, VPS, and SPSs. INE overwrite syntax values in VPS, SPS and PPS parameters. INE might overwrite some slice header syntax corresponding to the ROI but should not modify slice data corresponding to the non-ROI. INE should not use information acquired by decoding slice data (e.g. decoded picture, syntax elements below slice data, etc.).
Client terminal
  Client terminal shall have SHVC decoder to decode sub bitstream corresponding to ROI.

## Slide 5: Codec support
There are several ways to support ROI-capable scalable video application with SHVC in combination with “constrained tile set”.
Method 1: Drop VCL NALU containing non-significant slice and change EL picture sizes.
Method 2: Change non-significant slice to skipped slice and remove associated slice data.
Method 3: Remove coefficients data in non-significant slice.
In this contribution, changes relating to Method 1 is introduced.

## Slide 6: Rewriting process
Method 1: Drop VCL NALU containing non-significant slice and change EL picture sizes.
(1) Drop VCL NALU of non-significant tile region
(2) Rewrite picture information
(3) Rewrite tile information
(4) Add BL ROI region information (modify scaled ref. layer offset)
(5) Add EL-to-BL phase shift information
Following slides explain modification regarding step 5.

## Slide 7: Phase shift problem caused by extraction
extraction
A
B
EL
BL
C
D
EL
BL
Phase shift between A and B could be different from that of C & D.
 Need ways to keep phase shift before and after cropping.
cropped regions

## Slide 8: Proposed changes
  Option 1: In SPS, signal pixel position where EL pixel position corresponds to BL integer pixel position.
num_cropped_ref_layer_offsets specifies the number of sets of cropped reference layer offset parameters that are present in the SPS.
cropped_ref_layer_left_offset[ i ] specifies the horizontal offset, in units of two luma samples, between the upper-left luma sample of the resampled i-th direct reference layer picture used for inter-layer prediction and the luma sample of the resampled picture whose corresponding position on the reference picture is integer position. When not present, the value of seq_cropped_ref_layer_left_offset[ i ] is inferred to be equal to 0.
sps_extension( ) { | Descriptor
… | 
num_scaled_ref_layer_offsets | ue(v)
for( i = 0; i < num_scaled_ref_layer_offsets; i++) { | 
scaled_ref_layer_left_offset[ i ] | se(v)
scaled_ref_layer_top_offset[ i ] | se(v)
scaled_ref_layer_right_offset[ i ] | se(v)
scaled_ref_layer_bottom_offset[ i ] | se(v)
} | 
num_cropped_ref_layer_offsets | ue(v)
for( i = 0; i < num_cropped_ref_layer_offsets; i++) { | 
cropped_ref_layer_left_offset[ i ] | ue(v)
cropped_ref_layer_top_offset[ i ] | ue(v)
} | 
} | 
C
cropped_ref_layer_left/top_offset

## Slide 9: Proposed changes
  Option 2: In SPS, signal phase offset between top-left EL pixel and corresponding BL pixel.
num_ ref_layer_phase_offsets specifies the number of sets of reference layer phase offset parameters that are present in the SPS.
cropped_ref_layer_left_phase_offset[ i ] specifies the horizontal phase offset in unit of 1/16 between the upper-left luma sample of the current picture and the upper-left luma sample of the resampled i-th direct reference layer picture used for inter-layer prediction.
sps_extension( ) { | Descriptor
… | 
num_scaled_ref_layer_offsets | ue(v)
for( i = 0; i < num_scaled_ref_layer_offsets; i++) { | 
scaled_ref_layer_left_offset[ i ] | se(v)
scaled_ref_layer_top_offset[ i ] | se(v)
scaled_ref_layer_right_offset[ i ] | se(v)
scaled_ref_layer_bottom_offset[ i ] | se(v)
} | 
num_ref_layer_phase_offsets | ue(v)
for( i = 0; i < num_ref_layer_phase_offsets; i++) { | 
cropped_ref_layer_left_phase_offset[ i ] | u(4)
cropped_ref_layer_top_phase_offset[ i ] | u(4)
} | 
} | 
C
D
EL
BL
cropped_ref_layer_left/top_phase_offset

## Slide 10: Conclusion
This contribution introduces:
  ROI-capable scalable video application
  rewriting process by disposing non-significant VCL NALU and changing EL picture size.
This contribution proposes modifications to keep EL and BL phase alignment before and after rewriting.
  Option 1: In SPS, signal pixel position where EL pixel position corresponds to BL integer pixel position.
  Option 2: In SPS, signal phase offset between top-left EL pixel and corresponding BL pixel.
It is recommended to agree on supporting ROI-capable scalable video application in SHVC, and adopt proposed modification.