## Slide 1: MV-HEVC/SHVC HLS: On sharing parameter sets across layers (JCTVC-O0059, JCT3V-F0036)
JCT-VC 15th Meeting in Geneva, CH, 23 Oct. - 2 Nov. 2013
JCT-3V 6th Meeting in Geneva, CH, 25 Oct. - 2 Nov. 2013
Takeshi Tsukuba, Tomoyuki Yamamoto, Tomohiro Ikai
SHARP Corporation

## Slide 2: Summary
Motivation
  In bitstrem extraction, sharing SPS/PPS could be removed since SPS/PPS can also be shared in case of no dependency between the layers of shared SPS/PPS and the referring layer.
  Scaled reference layer offsets for only one layer with nuh_layer_id equal to the nuh_layer_id value of SPS are signalled so that when scaled reference layer offsets are present in SPS, different layers cannot refer the SPS.
  Proposal
      For issue 1, restrict that sharing parameter sets (SPS/PPS) shall be direct or indirect reference layer of the referring layer.
      For issue 1, add a new direct_dependency_type to show sharing parameter set dependency.
      For issue 2, signal scaled reference layer offsets for multiple layers which refer the same SPS or move scaled reference layer offsets into VPS like JCTVC-N0089.
  Benefits
      Avoid the improper removal of sharing parameter set in bitstream extraction.
      Enable parameter sharing in case of pixel, motion or any other dependency is not utilized.
      Enhance SPS sharing capability for Extended Spatial Scalability.
Notes:   Avoid the improper removal of sharing parameter set in bitstream extraction.
  Enable parameter sharing in case of pixel, motion or any other dependency is not utilized.
  Enhance SPS sharing capability for Extended Spatial Scalability.

## Slide 3: Issue 1
In sub bitstrem extraction, sharing SPS or PPS could be removed since SPS or PPS can also be shared in case of no dependency between the layers of shared SPS and the referring layer.
The situation can be illustrated in Fig.1.
  Layer0 is direct reference layer of Layer2
  Parameter sets of Layer1 are shared among Layer1 and Layer2
  When extracting layer2, parameter sets of Layer1 could be discarded

## Slide 4: Solution 1 for issue 1
    Restrict that sharing parameter sets (SPS/PPS) shall be direct or indirect reference layer of the referring layer.
Text changes
      Solution 1 can solve the improper removal of sharing parameter set
      in bitstream extraction.
Notes: The proposal adds the following restriction.
F.7.4.2.4 Order of VPS, SPS and PPS RBSPs and their activation
It is a requirement of bitstream conformance that, when an SPS with nuh_layer_id equal to nuhLayerIdA is active for a layer with nuh_layer_id equal to nuhLayerIdB, the layer with nuh_layer_id equal to nuhLayerIdA shall be a direct or indirect reference layer of the layer with nuh_layer_id equal to nuhLayerIdB.
It is a requirement of bitstream conformance that, when a PPS with nuh_layer_id equal to nuhLayerIdA is active for a layer with nuh_layer_id equal to nuhLayerIdB, the layer with nuh_layer_id equal to nuhLayerIdA shall be a direct or indirect reference layer of the layer with nuh_layer_id equal to nuhLayerIdB.

## Slide 5: Solution 2 for issue 1
    Add a new direct_dependency_type to show sharing parameter sets dependency (NonVCLDepEanbledFlag)
    Restrict that sharing parameter sets (SPS/PPS) shall be direct reference layer of the referring layer and NonVCLDepEnabledFlag between the two layers shall be equal to 1.
      Solution 2 can give the functionality to enable parameter sharing in case of pixel, motion or any other dependency is not utilized.
      See next page on text changes
Notes: The proposal adds the following restriction.
F.7.4.2.4 Order of VPS, SPS and PPS RBSPs and their activation
It is a requirement of bitstream conformance that, when an SPS with nuh_layer_id equal to nuhLayerIdA is active for a layer with nuh_layer_id equal to nuhLayerIdB, the layer with nuh_layer_id equal to nuhLayerIdA shall be a direct or indirect reference layer of the layer with nuh_layer_id equal to nuhLayerIdB.
It is a requirement of bitstream conformance that, when a PPS with nuh_layer_id equal to nuhLayerIdA is active for a layer with nuh_layer_id equal to nuhLayerIdB, the layer with nuh_layer_id equal to nuhLayerIdA shall be a direct or indirect reference layer of the layer with nuh_layer_id equal to nuhLayerIdB.

## Slide 6: Text changes on Solution 2
vps_extension( ) { | Descriptor
…snipped… // signal dependency type indicating that SPS/PPS having nuh_layer_id equal to layer_id_nuh[j] for the layer with layer_id_nuh[j] is directly referred by the layer with nuh_layer_id equal to layer_id_nuh[i] | 
direct_dep_type_len_minus3 | ue(v)
for( i = 1; i <= vps_max_layers_minus1; i++ ) | 
for( j = 0; j < i; j++ ) | 
if( direct_dependency_flag[ i ][ j ] ) | 
direct_dependency_type[ i ][ j ] | u(v)
…snipped… | 
} | 
It is a requirement of bitstream conformance that, when an SPS with nuh_layer_id equal to nuhLayerIdA is active for a layer with nuh_layer_id equal to nuhLayerIdB, the layer with nuh_layer_id equal to nuhLayerIdA shall be a direct reference layer of the layer with nuh_layer_id equal to nuhLayerIdB and the direct dependency type between the two layers indicates non-VCL dependency.
It is a requirement of bitstream conformance that, when a PPS with nuh_layer_id equal to nuhLayerIdA is active for a layer with nuh_layer_id equal to nuhLayerIdB, the layer with nuh_layer_id equal to nuhLayerIdA shall be a direct reference layer of the layer with nuh_layer_id equal to nuhLayerIdB and the direct dependency type between the two layers indicates non-VCL dependency type.
Let the layer with nuh_layer_id equal to nuhLayerIdA have an index j. The direct dependency type between the two layers NonVCLDepEnabledFlag[ nuhLayerIdB ][ j ] shall be equal to 1.

## Slide 7: Text changes on Solution 2

## Slide 8: Solution 3 for issue 3
Signal scaled reference layer offsets for multiple layers which refer the same SPS
      Solution 3 can enhance SPS sharing capability for Extended Spatial Scalability.
      See next page on text changes on Solution 3.

## Slide 9: Text changes on Solution 3
sps_extension( ) { | Descriptor
… | 
num_layer_id_refering_sps_minus1 | ue(v)
for( k = 0; k < num_layer_id_refering_sps_minus1; k++) { | 
if( k > 0 ){ | se(v)
layer_id_refering_sps[ k ] | u(6)
LIdtoIdx[ layer_id_refering_sps[ k ] ] = k | 
else{ | 
layer_id_refering_sps[ 0 ] = nuh_layer_id | 
LIdtoIdx[ layer_id_refering_sps[ k ] ] = 0 | 
} | 
num_scaled_ref_layer_offsets[ k ] | ue(v)
for( i = 0; i < num_scaled_ref_layer_offsets[ k ]; i++) { | 
scaled_ref_layer_left_offset[ k ][ i ] | se(v)
scaled_ref_layer_top_offset[ k ][ i ] | se(v)
scaled_ref_layer_right_offset[ k ][ i ] | se(v)
scaled_ref_layer_bottom_offset[ k ][ i ] | se(v)
} | 
} | 
} | 

## Slide 10: Text changes on Solution 3

## Slide 11: Conclusion
  Proposal
      Restrict that sharing parameter sets (SPS/PPS) shall be direct or indirect reference layer of the referring layer.
      Add a new direct_dependency_type to show sharing parameter set dependency.
      Signal scaled reference layer offsets for multiple layers which refer the same SPS or move scaled reference layer offsets into VPS like JCTVC-N0089.
  Benefits
      Proposal 1 can avoid the improper removal of sharing parameter set in bitstream extraction.
      Proposal 2 can enable parameter sharing in case of pixel, motion or any other dependency is not utilized.
      Proposal 3 can enhance SPS sharing capability for Extended Spatial Scalability.
      It is recommended to adopt to next SHVC/MV-HEVC.
      - either of proposal 1 or 2
      - proposal 3
Notes:   Avoid the improper removal of sharing parameter set in bitstream extraction.
  Enable parameter sharing in case of pixel, motion or any other dependency is not utilized.
  Enhance SPS sharing capability for Extended Spatial Scalability.

## Slide 12
Thank you!