## Slide 1: RCE2 – C2: Entropy Coding Compression Efficiency for High Bit Depths
JCTVC-O0065
Broadcast & Professional Research Labs
Sony Europe Ltd.
Karl Sharman
Sony Corp.

## Slide 2: Background (from N0189)
Coding higher bit-depth data gradually becomes more costly.
For the sequences tested:
  For 16-bit data,
    Without lossless coding tools, the sequences are actually inflated at their useful operating range: (MSE <= 1, SNR >= 96.3, i.e. QP <= -32)
    The base-band video rate is 1920x1080x16x3x50 = ~ 5 Gbps.
    Lossless coding tools (PCM mode) are generally used.
  For 14-bit data,
    Without lossless coding tools, the sequences are inflated for a substantial part of their operating range: (MSE <= 0.5, SNR >= 81.3, i.e. at QP <= -26)
    The 14-bit base-band video rate is ~4.4 Gbps.
    In simple terms, 13-bit video data would be compressible; 14-bit video data would be better coded as raw / PCM.
    This occurs for AVC as well.

## Slide 3: Increase CABAC Efficiency (from N0189)
The addition of a “fixed bits” scheme to the entropy coding was proposed in M0178:
  Conceptually, the algorithm is (for a number of fixed bits BF):
  For each significant coefficient, C,
    split the value C into CMSB and CLSB, where CLSB comprises the BF least-significant bits of C.
    Code CMSB as for normal coefficients in a group.
    After the sign bits are coded, code the bits for CLSB using EP bins.
      (Sign bit hiding is based upon the entire coefficient C.)

## Slide 4: M0178 Fixed Bits results (from N0189)
From the studies at higher bit-depths, with
  MAX_TR_DYNAMIC_RANGE = bitDepth+6
  ENTROPY_CODING_DYNAMIC_RANGE = bitDepth+6
  Transform matrix precision = 14
  Transform skip enabled; TransQuant-Bypass, RDOQ and PCM disabled

## Slide 5: Extension of Fixed Bits (from N0189)
  The fixed bits scheme has been rolled into the Golomb Rice escape parameter scheme.
    This results in slightly reduced gains from the original scheme, but does not require additional stages in the entropy process.
    The reduction in gains is because the fixed bits applied to all non-zero coefficients, where as this scheme only applies to all escape coded coefficients.
  When BF fixed bits would have been used, now the Golomb Rice parameter cRiceParam is increased by BF at the start of the TU, and clipped to 4+BF during the processing.
  The question then remains on how to select BF.
    In M0178, BF was chosen by the encoder, with BF =max(0,-QP/6) being a reasonable estimate.
    However, an algorithm to adapt BF is now presented.

## Slide 6: Auto-adaptation (from N0189)
Auto-adaptation requires the value BF to be treated as a slice-scoped (cf context-variable) parameter.
  BF is initialised to 0 at the start of the slice.
  For each TU encoded/decoded:
    The variables undershootCount, overshootCount and totalCount are each initialised to 0.
    For each coefficient that requires an escape code, escapeCode, do: totalCount++ if (escapeCode > (3 << cRiceParam)) undershootCount++ else if ((escapeCode * 3) < (1 << cRiceParam)) overshootCount++
    At the end of encoding/decoding the TU, BF is adjusted according to the following pseudo-code: if ((undershootCount * 4) > totalCount) BF++ else if (((overshootCount * 2) > totalCount) && (BF > 0)) BF--
    (BF is naturally limited to ENTROPY_CODING_DYNAMIC_RANGE (as defined in JCTVC-N0188))

## Slide 7: Results:
AHG8 – lossy test conditions

## Slide 8: Results:
AHG8 – lossless test conditions
(Positive values show an improvement over anchor)

## Slide 9: Results:
AHG18 test conditions

## Slide 10: Conclusion
The Golomb-Rice Parameter modification with auto-adaptation gives significant BD-rate efficiency improvements for:
  high operating points,
  lossy and lossless coding non-video sequences
  whilst not being detrimental to standard video and CTC operating points.
For the 16-bit operating point,
  In the anchor:
    there is practically no compression, and TUs would be best encoded using lossless and PCM only.
  But in this test,
    30 to 40% compression is achieved (i.e. relative to baseband).