## Slide 1: JCTVC-O0088 AhG5: Memory Bandwidth Reduction for HEVC RExt
Woo-Shik Kim, Vadim Seregin, Joel Sole, Marta Karczewicz

## Slide 2: Problem statement
In HEVC version 1, to reduce memory bandwidth, bi-prediction is restricted for 4x8 and 8x4 PUs
Bandwidth goes up for 4:4:4 chroma format in HEVC RExt
Bandwidth assessment from JCTVC-L0440 applied to 4:2:0 and 4:4:4
For consumer applications using 4:4:4, it is desirable to reduce memory bandwidth requirement
Memory configuration | 4:2:0 | 4:4:4 | Ratio
4×2 | 15.0 | 20.5 | 137%
8×2 | 18.0 | 24.0 | 133%

## Slide 3: Problem statement
AhG5 mandate
  Perform memory bandwidth analysis of the range extensions technical design and its proposed modifications
Previous contributions
  M0298, N0261
Notes from last meeting
  It was suggested to simply keep in mind the potential to use the bipred block size constraint approach when finalizing RExt, but not to act now since the 4:4:4 design is not yet final.

## Slide 4: Proposed Method
Restrict bi-prediction for 8x8 CU
  For merge mode, bi-directional MV candidate is converted to uni-directional motion vector from RefPicList0
  For AMVP mode, only uni-directional MV can be chosen at encoder side and inter direction signaling is restricted to uni-direction only
  BW compared to 4:2:0 is reduced from 137% to 108% at the cost of 0.2% loss in Y
Memory configuration | 4:2:0 | 4:4:4 | Test 1/2 | Ratio to 4:2:0 | Ratio to 4:4:4
4×2 | 15.0 | 20.5 | 16.3 | 108% | 79%
8×2 | 18.0 | 24.0 | 21.0 | 117% | 88%

## Slide 5: Experimental results
BD-rate using RExt common conditions (JCTVC-N1006)
Thanks to Canon for cross-check
Summary results of RA and LB YUV 4:4:4
 | Random Access HE Main-tier |  |  | Random Access HE High-tier |  | 
 | Y | U | V | Y | U | V
RGB 4:4:4 | 1.5% | 0.9% | 1.4% | 1.6% | 0.8% | 1.4%
YCbCr 4:4:4 | 0.8% | 0.8% | 0.8% | 1.0% | 0.9% | 1.2%
YCbCr 4:2:2 | 0.6% | 0.6% | 0.6% | 0.9% | 0.7% | 1.0%
Overall | 1.0% | 0.8% | 0.9% | 1.2% | 0.8% | 1.2%
 | 1.0% | 0.6% | 1.0% | 1.2% | 0.6% | 1.2%
Enc Time[%] | 97% |  |  | 97% |  | 
Dec Time[%] | 100% |  |  | 100% |  | 
 | Low delay B HE Main-tier |  |  | Low delay B HE High-tier |  | 
 | Y | U | V | Y | U | V
RGB 4:4:4 | 1.3% | 0.9% | 1.2% | 1.4% | 0.8% | 1.3%
YCbCr 4:4:4 | 0.6% | 0.6% | 0.6% | 0.9% | 0.7% | 0.9%
YCbCr 4:2:2 | 0.7% | 0.4% | 0.4% | 0.9% | 0.5% | 0.8%
Overall | 0.9% | 0.6% | 0.8% | 1.1% | 0.7% | 1.0%
 | 0.9% | 0.8% | 0.8% | 1.0% | 0.6% | 1.0%
Enc Time[%] | 96% |  |  | 96% |  | 
Dec Time[%] | 102% |  |  | 101% |  | 

## Slide 6: Conclusion
Proposed a method d to reduce memory bandwidth for 4:4:4
Achieves about 20% BW reduction at the cost of 0.9% loss