## Slide 1: Transcoding-friendly Scalable video coding (JCTVC-O0127)
Kenneth Andersson, Thomas Rusert, Rickard Sjöberg, Jonatan Samuelsson
Notes: 2013-10-17
<number>

## Slide 2: Summary
Additional functionality to SHVC is proposed to provide better flexibility in controlling bitrate in uplink and downlink:
  In difference to traditional scalable coding:
    Encode the highest fidelity in the base layer
    Encode lower fidelities in higher layers
    Generate transform coefficients in low fidelity layers with dependency to the highest fidelity
    Low fidelity streams can be obtained by guided transcoding
  The use of this functionality is signalled as a new dependency type in VPS, parallel to other dependency types
Notes: 2013-10-17
<number>

## Slide 3: SUMMARY Cont’
Advantage:
  The highest fidelity is decodable by an HEVC version 1 decoder.
  Extraction of the highest fidelity comes at no bitrate cost while using SHVC typically would render a bitrate cost of 14-24% for SNR scalability.
  Significant reduction of traditional transcoding complexity to derive a coding efficient low fidelity HEVC version 1 bitstream.
  BD rate reduction compared to simulcast by 12.1% (RA/LDB/LDP) for SNR scalability
  Thanks to Nokia for cross-checking (JCTVC-O0322)

## Slide 4: BACKGROUND
IP based video delivery where the end-points are HEVC version 1 decoders featuring:
  Coding efficient representation from the encoder(s) to a network node (uplink)
  Coding efficient representation from the network node to the end-users (downlink)
Optimally the coding efficiency of both the uplink and the downlink should have same coding efficiency as for coding for a single representation
Encoder
Network node
HEVC v1 decoder
Uplink
Downlink

## Slide 5: Current possibilities
Simulcast:
  Encode several fidelities in the uplink and select the appropriate one for downlink to the end-point.
Scalable coding:
  Encode several fidelities dependently in the uplink and extract appropriate NALs for the downlink to the end-point.
Transcoding:
  Encode the highest fidelity in the uplink and decode and re-encode to lower fidelity if that is needed for downlink.
HEVC high fidelity
Network node
HEVC v1 decoder
Uplink
Downlink
HEVC low fidelity
HEVC high fidelity
Network node
HEVC v1 decoder
Uplink
Downlink
Layer 0: low fidelity
Network node
Uplink
Downlink
Layer 1: high fidelity
HEVC v1 decoder
for low fidelity

## Slide 6: SUITABILITY of current possibilites
Simulcast:
  No overhead in the downlink but will give significant overhead for independent coding of fidelities in the uplink.
Scalable coding:
  Reduces overhead in the uplink compared to simulcast but only the low fidelity can be decoded by a HEVC version 1 decoder so transcoding is needed for other fidelities. The highest fidelity of the scalable bitstream has already before transcoding a significant overhead compared to single layer coding. Do not fit the use case.
Transcoding:
  The uplink can be coded very efficiently also the downlink if the highest fidelity is selected. To derive a coding efficient low fidelity bitstream requires significant computations in the network node.
HEVC high fidelity
Network node
HEVC v1 decoder
Uplink
Downlink
HEVC low fidelity
HEVC high fidelity
Network node
HEVC v1 decoder
Uplink
Downlink
Layer 0: low fidelity
Network node
Uplink
Downlink
Layer 1: high fidelity
HEVC v1 decoder
for low fidelity

## Slide 7: Proposal
Encode the high fidelity in the base layer of SHVC
Encode the low fidelity in a higher layer of SHVC
Generate transform coefficients in low fidelity layers with dependency to the highest fidelity:
  When a new dependency type is signalled in VPS apply transformation and quantization before the normal decoding process of transform coefficients in a low fidelity layer.
Layer 1: low fidelity
Network node
HEVC v1 decoder
Uplink
Downlink
Layer 0: high fidelity

## Slide 8: Overview of Decoding process

## Slide 9: Benefits of the proposal
  In difference to traditional transcoding:
    Coding parameters for the low fidelity is estimated before sent to the transcoder and provided as a layer of a scalable bitstream.
    Mode and motion estimation can be performed using the original.
    The coding efficiency of the low fidelity can be controlled before transcoding.
  When bitstream reach the network node instead of traditional transcoding a transcoder:
    Decode the low fidelity layer with reference to the highest fidelity layer
    Encode a low fidelity single layer bitstream re-using coding parameters of the decoded low fidelity layer.

## Slide 10: Benefits of the proposal cont’
  In difference to traditional scalable coding:
    The most important part of a scalable bitstream, the highest fidelity, is decodable by a HEVC version 1 decoder and without loss in coding efficiency compared to single layer coding
    Encoding decisions of the layers can be performed similar to single layer coding

## Slide 11: Benefits of the proposal cont’
In difference to simulcasting several fidelities:
  Overhead of independently encoded fidelities can be reduced.
  Both a simulcast bitstream and a bitstream according to the proposal can be produced simultaneously.
  Pending on bandwidth in uplink and capabilities in the network an appropriate stream can be selected.
  The proposed functionality can also be used to reduce overhead for already encoded HEVC version 1 bitstreams while keeping the coding efficiency of the highest fidelity.

## Slide 12: Results for SNR scalability
The proposal is compared with simulcast. Simulcast is coded with SHM-3.0.1 with no dependency between the two layers. QPs in the common conditions are switched for base and enhancement layer.
The proposal is also coded with the low fidelity in layer 1 and without inter-layer sample and motion prediction.

## Slide 13: PROPOSAL vs SIMULCAST
 | RA HEVC SNR |  |  | LD-B HEVC SNR |  | 
 | Y | U | V | Y | U | V
Class A | -12,2% | -12,3% | -12,2% | -10,4% | -10,5% | -10,5%
Class B | -13,6% | -13,7% | -13,8% | -12,3% | -12,5% | -12,6%
Overall (Test vs Ref) | -13,2% | -13,3% | -13,4% | -11,8% | -11,9% | -12,0%
Overall (Test vs single layer) | 0,0% | 0,0% | 0,0% | 0,0% | 0,0% | 0,0%
Enc Time[%] | 97,8% |  |  | 101,5% |  | 
Dec Time[%] | 111,9% |  |  | 116,4% |  | 

## Slide 14: CONCLUSION
We have shown how SHVC can provide a high fidelity bitstream with same performance as single layer HEVC.
A low fidelity stream can be derived from a scalable bitstream in the network with significant reduction of complexity compared to traditional transcoding.
Compared to simulcast average BD rate reductions of 12.1% have been shown for SNR scalability.
We propose that this functionality is adopted to the SHVC draft to provide better flexibility for controlling bitrate in uplink and downlink.

## Slide 15
Notes: 2013-10-17
<number>

## Slide 16: BACKUP slides

## Slide 17: Comparison witH SHVC for SNR scalability
SHVC vs Simulcast and Single layer:
Proposal vs Simulcast and Single layer:
 | RA HEVC SNR |  |  | LD-B HEVC SNR |  | 
 | Y | U | V | Y | U | V
Overall (Test vs Ref) | -20,9% | -8,9% | -7,6% | -12,5% | -5,3% | -2,0%
Overall (Test vs single layer) | 14,4% | 32,1% | 34,2% | 24,3% | 34,7% | 39,5%
 | RA HEVC SNR |  |  | LD-B HEVC SNR |  | 
 | Y | U | V | Y | U | V
Overall (Test vs Ref) | -13,2% | -13,3% | -13,4% | -11,8% | -11,9% | -12,0%
Overall (Test vs single layer) | 0,0% | 0,0% | 0,0% | 0,0% | 0,0% | 0,0%