## Slide 1: On residual DPCM design unification for lossy coding in HEVC-RExt JCTVC-O0134
R&D
© BBC MMXIII
Matteo Naccari and Marta Mrak
BBC Research and Development

## Slide 2: Introduction
For lossy coding, Inverse RDPCM at the decoder is performed differently for intra and inter in Draft 4 of the HEVC-RExt text:
Intra
Inter
Different reconstruction paths may be problematic for some implementations
Inverse quantisation
Residual levels
Inverse TS
Inverse RDPCM
Reconstructed residuals
Inverse quantisation
Residual levels
Inverse RDPCM
Inverse TS
Reconstructed residuals

## Slide 3: Proposal
Unify the design towards the inter RDPCM design
Intra
Inter
Inverse quantisation
Residual levels
Inverse TS
Inverse RDPCM
Reconstructed residuals
Inverse quantisation
Residual levels
Inverse RDPCM
Inverse TS
Reconstructed residuals
Inverse TS
Inverse RDPCM

## Slide 4: Results over RCE3 CTC and lossy coding
 | AI-MT | AI-HT | AI-SHT | RA-MT | RA-HT | LD-MT | LD-HT
Class F | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Class B | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
SC RGB 444 | 0.0% | -0.1% | -0.1% | -0.1% | 0.0% | 0.1% | 0.0%
Animation RGB 444 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
SC YUV 444 | -0.1% | -0.1% | -0.1% | 0.0% | 0.0% | -0.1% | -0.1%
Animation YUV 444 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
RangeExt | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
SC(444) GBR Optional | 0.0% | -0.1% | -0.4% | -0.1% | -0.1% | -0.3% | -0.5%
SC(444) YUV Optional | 0.0% | 0.0% | -0.1% | -0.2% | -0.1% | -0.7% | -0.3%
Average Y-BD rates
Almost no losses are recorded
Shorter feedback path at the encoder