## Slide 1
Signalling decoded picture buffer size (JCTVC-O0136/JCT3V-F0049)
Byeongdoo Choi
Samsung Electronics Co., Ltd
Oct., 2013
Notes: <number>

## Slide 2: Discussion on DPB operation
How do DPBs operate?
  Outputs of the decoded picture in AU will be aligned.
  An unused reference picture can be independently removed from DPB for each layer. (already supported)
A DPB can be split into several sub-DPBs, e.g. for each layer or group of layers. Each sub-DPB may contain the decoded pictures having the same representation format.
  Benefits: The buffers can be allocated more precisely in decoders.
  No other clear benefit is expected.
Shall sub-DPB or other partition of DPBs be specified?
  If the only benefit of DPB partitioning is saving memories, signalling information helpful for DPB allocation is enough without a specific text regarding sub-DPB operations.
  In practical implementations, DPB can be intelligently designed with the provided information over the specified DPB operation.
<number>

## Slide 3: Proposal on DPB signalling
Three alternative syntax to indicate the maximum decoded buffer sizes are proposed.
  DPB signalling for each operation point and for each representation format.
  DPB signaling for each operation point and additionally for each layer.
  Explicitly selecting the level of DPB signaling (hybrid of options 1&2).
We assert that those syntax are helpful for session negotiation and decoder set-up.
The selective signalling of DPB sizes (option-3) is preferable, due to the degree of freedom of DPB in practical implementations.
<number>

## Slide 4: Option-1: DPB signalling for each operation point and representation format
Maximum DBP sizes for each operation points (layer set + temporal sub-layer) are signalled.
To assist the exact allocation of DPB according to representation formats, maximum DPB size for each representation format can be optionally signalled.
max_dpb_size_for_ layer_set_minus1[ i ][ j ] plus 1 specifies the maximum required size of the decoded picture buffer of the ith layer set for the CVS in units of picture storage buffers when HighestTid is equal to j.
max_dpb_size_for_rep_format_idx_present_flag[ i ][ j ] equal to 1 indicates whether max_dpb_size_for_ rep_format_idx _minus1[ i ][ j ][ k ] is present.
max_dpb_size_for_ rep_format_idx_minus1[ i ][ j ][ k ] plus 1 specifies the maximum required size of the decoded picture buffer of the i-th layer set associated with the k-th representation format for the CVS in units of picture storage buffers when HighestTid is equal to j.
<number>

## Slide 5: Option-2: DPB signalling for each operation point and for each layer of the operation point.
If the DPB operates in layer-wise, maximum DPB size for each layer of each operation point can be signalled optionally.
max_dpb_size_for_ layer_set_minus1[ i ][ j ] plus 1 specifies the maximum required size of the decoded picture buffer of the ith layer set for the CVS in units of picture storage buffers when HighestTid is equal to j.
max_dpb_size_for_layer_present_flag[ i ][ j ] equal to 1 indicates that max_dpb_size_for_layer_minus1[ i ][ j ][ k ] is present.
max_dpb_size_for_layer_minus1[ i ][ j ][ k ] plus 1 specifies the maximum required size of the decoded picture buffer of the k-th layer associated with the i-th layer set for the CVS in units of picture storage buffers when HighestTid is equal to j.
<number>

## Slide 6: Option-3: Selecting the type of DPB signalling
By DPB behaving models, a desired DBP size information can be selectively delivered.
vps_dpb_signal_present_flag equal to 1indicates that max DPB size for each layer set and sub-layer is signaled. vps_dpb_signal_present_flag equal to 0 indicates that max DPB size for each layer set and sub-layer is not signaled.
dpb_signal_type specifies whether max_dpb_size_for_ rep_format_idx _minus1[ i ][ j ][ k ] or max_dpb_size_for_ layer_minus1 [ i ][ j ][ k ] is signaled or not.
<number>

## Slide 7
Thank you !
<number>