## Slide 1
On inter-layer dependency signalling (JCTVC-O0138/JCT3V-F0051)
Byeongdoo Choi
Samsung Electronics Co., Ltd
Oct., 2013
Notes: <number>

## Slide 2: Outline
Some clean-ups or improvements of syntax related to inter-layer RPS or other layer dependency indication are proposed.
On inter-layer reference picture set
  Removal of the inter-layer RPS
  Or, improvements of the inter-layer RPS ( inter-layer DPB status instead of direct inter-layer references)
On all_ref_layers_active_flag and max_one_active_ref_layer_flag
  Signalling those syntax for each layer
  Optional signalling of max_one_active_ref_layer_flag depending on the value of all_ref_layers_active_flag
A new flag high_ref_layers_active_flag
  Indication whether closer dependent layers are used for inter-layer prediction
<number>

## Slide 3: On inter-layer reference picture set
Motivation
The inter-layer RPS in SH indicates the active inter-layer references for each picture, even if the layer dependency is indicated by direct_dependency_flag[ i ][ j ] in VPS.
The roles of the inter-layer RPS:
  Fine controls of inter-layer references for each picture
  Q: How often shall the inter-layer references be changed within a CVS?
  Picture loss detection within an access unit
  Q: Even if the RPS can detect the loss of the previous pictures, is it really useful to detect the loss of the pictures within an access unit?
  If necessary, is the current design of the inter-layer RPS suitable to detect the loss of pictures?
Removal of the inter-layer RPS or its improvement can be considered.
<number>

## Slide 4: Proposed improvements of inter-layer RPS
Current design:
  The inter-layer reference pictures to be used for decoding the current layer are indexed.
Proposed design:
  The inter-layer reference pictures to be used for decoding the current layer and the layers with nuh_layer_id greater than that of the current layer are indexed.
  Aligned with the RPS design, the picture buffers in DPB are signalled with the flags indicating whether decoded pictures are used for the current picture or used for the pictures of higher layers.
  Picture loss detection: When the current picture with nuh_layer_id equal to i is decoded, if the decoded picture of nuh_layer_id less than i, which is indicated by the inter-layer RPS of the current picture and included in TargetDecLayerIdList, is not present in a DPB, that picture turns out to be a lost picture.
Benefits:
  More exact detection of loss pictures within an access unit.
  Early marking of unused reference pictures
    If a decoded picture with TemporalId equal to HighestTid is not included in the inter-layer RPS, that picture can be immediately marked as “unused for reference”.
  Explicit indication of decoded picture buffer status.
<number>

## Slide 5: Specification text of the proposed inter-layer RPS
<number>
inter_layer_dep_layer_idc[ i ] specifies the variable, RefPicLayerIdInDPB[ i ], representing the nuh_layer_id of the i-th picture that may be used by the current picture and the pictures with nuh_layer_id greater than nuh_layer_id of the current picture for inter-layer prediction. The length of the syntax element inter_layer_dep_layer_idc[ i ] is Ceil( Log2( nuh_layer_id ) ) bits. The value of inter_layer_dep_layer_idc[ i ] shall be in the range of 0 to nuh_layer_id − 1, inclusive. When not present, the value of inter_layer_dep_layer_idc[ i ] is inferred to be equal to i.
used_by_curr_layer_flag [ i ] specifies the variable, RefPicLayerId [ i ], representing the nuh_layer_id of the i-th picture that may be used by the current picture for inter-layer prediction. When not present, the value of used_by_curr_layer_flag [ i ] is inferred to be equal to 0.
The variables RefPicLayerId[ i ] for all values of i in the range of 0 to NumActiveRefLayerPics − 1, inclusive, are derived as follows:
for( i = 0; i < num_dependent_layer; i++) if(used_by_curr_layer_flag[ i ]) { RefPicLayerId[ i ] = DepLayerId [ nuh_layer_id ][ inter_layer_dep_layer_idc[ i ] ]

## Slide 6: On all_ref_layers_active_flag and max_one_active_ref_layer_flag
Motivation 1
all_ref_layers_active_flag equal to 1 indicates that the decoded pictures of all directly dependent layers of each layer are included in the inter-layer reference picture set of the picture of each layer
max_one_active_ref_layer_flag equal to 1 specifies that at most one picture is used for inter-layer prediction for each picture in the CVS.
  The flag max_one_active_ref_layer_flag is applicable for SHVC, while all_ref_layers_active_flag[ i ] seems to be mainly used for MV-HEVC. Both flags may reduce redundant syntax by avoiding fully signalling of the inter-layer RPS syntaxes in slice headers.
In some cases, all reference layers are active for some layers, while only one reference is active in other layers, especially for multiple scalability dimensions.
Signaling both syntax elements for each layer is more bit-efficient, especially to cope with bitstreams having multiple scalability dimensions.
<number>

## Slide 7: On all_ref_layers_active_flag and max_one_active_ref_layer_flag
Motivation 2
Both flags shall not be equal to 1 together at the same time
  Except for the case that each layer has only one directly dependent layer.
  However, when all_ref_layers_active_flag is equal to 1 and each layer has only one directly dependent layer, signaling max_one_active_ref_layer_flag does not affect any decoding process.
Therefore, if all_ref_layers_active_flag is equal to 1, max_one_active_ref_layer_flag can be inferred to be equal to 0 without signaling.
<number>

## Slide 8: Proposals on all_ref_layers_active_flag and max_one_active_ref_layer_flag
On all_ref_layers_active_flag and max_one_active_ref_layer_flag
  Signalling those syntax for each layer
  Optional signalling of max_one_active_ref_layer_flag depending on the value of all_ref_layers_active_flag
all_ref_layers_active_flag[ i ] equal to 1 specifies that for each picture of the i-th layer, the reference layer pictures of all direct reference layers of the i-th layer are present in the same access unit as the decoded picture and are included in the inter-layer reference picture set of the picture. all_ref_layers_active_flag equal to 0 specifies that the above restriction may or may not apply.
max_one_active_ref_layer_flag [ i ] equal to 1 specifies that at most one picture is used for inter-layer prediction for each picture of the i-th layer in the CVS. max_one_active_ref_layer_flag equal to 0 specifies that more than one picture may be used for inter-layer prediction for each picture of the i-th layer in the CVS. When not present, max_one_active_ref_layer_flag [ i ] is inferred to be equal to 0.
<number>

## Slide 9: A new flag high_ref_layers_active_flag
In most cases, inter-layer reference pictures with closer nuh_layer_id values to that of the current picture tend to be more correlated.
The proposed flag, high_ref_layers_active_flag, indicates that higher dependent layers are active reference layers for the current picture, without signaling inter-layer RPS.
high_ref_layers_active_flag equal to 1 specifies that inter_layer_pred_layer_idc[ i ] is inferred to equal to NumDirectRefLayers[ nuh_layer_id ] – 1 – I, when i is in the range of 0 to NumActiveRefLayerPics – 1. high_ref_layers_active_flag equal to 0 specifies that inter_layer_pred_layer_idc[ i ] is explicitly signaled.
<number>

## Slide 10
Thank you !
<number>