## Slide 1
Layer-wise initialization and parameter set activation (JCTVC-O0139/JCT3V-F0052)
Byeongdoo Choi
Samsung Electronics Co., Ltd
Oct., 2013
Notes: <number>

## Slide 2: Motivation
A layer-wise start-up and its related process were adopted at the last Vienna meeting.
In this contribution, the improvements of the process related to the layer-wise start-up and the conditions of the parameter set activation are proposed.
<number>

## Slide 3: On video parameter set activation
We summarize the above description as follows:
  A VPS remains active until a new VPS is activated or until the end of the bitstream.
  A new VPS is activated at an access unit in which all pictures are IDRs.
  A new VPS is activated at an access unit in which a picture with nuh_layer_id equal to 0 is a BLA picture.
<number>

## Slide 4: On video parameter set activation
An minor improvement on VPS activation is proposed.
  A VPS remains active until a new VPS is activated or until the end of the bitstream.
  A new VPS is activated at an access unit in which all pictures are IDRs.
  A new VPS is activated at an access unit in which a picture with nuh_layer_id equal to 0 is a BLA picture or a CRA with HandleCraAsBlaFlag equal to 1.
<number>

## Slide 5: On sequence parameter set activation
A condition for changing the SPS syntax elements related to the representation format is proposed.
  If layers have different IRAP periods, a non-IRAP picture with nuh_layer_id greater than 0 can be an LIP in an initial IRAP access unit. Then, the pictures with the same nuh_layer_id following the LIP in decoding order may or may not refer to the decoded picture belonging to the previous CVS as references.
  If the picture size or the bit-depth is changed by activating a new SPS in the following CVS, the pictures in the following CVS may refer to the decoded picture with different formats. That is not allowed in the current SHVC and MV-HEVC.
The following condition for changing the SPS syntax elements related to the representation format is proposed.
<number>
The SPS syntax elements pic_width_in_luma_samples, pic_height_in_luma_samples, bit_depth_luma_minus8, bit_depth_chroma_minus8, and chroma_format_idc shall remain unchanged within a sequence of activated SPS RBSPs, in their activation order, from any activated SPS RBSP until the end of the bitstream or up to but excluding an SPS RBSP that is activated within the next access unit in which at least one of the following conditions is true: - The access unit includes a picture for each nuh_layer_id value in TargetDecLayerIdList and each picture in the access unit is an IDR picture. - The access unit includes an IRAP picture with nuh_layer_id equal to 0 for which NoClrasOutputFlag is equal to 1.

## Slide 6: On LayerInitialisedFlag
In the current specification text, when a layer with nuh_layer_id greater than 0 starts up at an IRAP picture, the RASL pictures associated with the IRAP picture of the layer cannot be correctly decoded.
Therefore, we believe that each layer can be initialized when the current picture is an IRAP picture with NoRaslOutputFlag equal to 1.
Adding the phrase highlighted in yellow is proposed in the below specification text
<number>

## Slide 7: On definition of layer initialisation picture
Each layer can be initialized when the current picture of the layer is an LIP picture. The LIP picture may activate a new SPS for each layer.
Current definition of LIP:
Based on the above definition of LIP, however, a layer cannot be correctly initialized and all the following pictures from the LIP cannot be correctly decoded in cases that the LayerInitialisedFlag[i] of a directly dependent layer of the LIP is not equal to 1.
The successful decoding of an LIP of the current layer is possible when all dependent layers of the current layer are initialized.
Proposed definition of LIP:
<number>
layer initialisation picture (LIP): A picture that is an IRAP picture with NoRaslOutputFlag equal to 1 or that is contained in an initial IRAP access unit.

## Slide 8: On cross_layer_irap_aligned_flag
If two pictures in an access unit have no dependency to each other when cross_layer_irap_aligned_flag is equal to 1, two pictures may have different nal_unit_type values. If poc_reset_flag is not set equal to 1, the POC values of pictures may or may not be the same across layers.
However, it is a requirement of bitstream conformance that the value of poc_reset_flag shall be equal to 0, when cross_layer_irap_aligned_flag is equal to 1.
In conclusion, if cross_layer_irap_aligned_flag is equal to 1, two pictures having no dependency to each other in an access unit can have different nal_unit_type values and different POC values.
<number>

## Slide 9: On cross_layer_irap_aligned_flag
In order to resolve this conflict, we propose to change the semantics of cross_layer_irap_aligned_flag, as follows:
->
Or alternatively, we propose to change the semantics of poc_reset_flag, as follows:
<number>
cross_layer_irap_aligned_flag equal to 1 specifies that IRAP pictures in the CVS are cross-layer aligned, i.e. when a picture pictureA of a layer layerA in an access unit is an IRAP picture, each picture pictureB in the same access unit that belongs to a direct reference layer of layerA or that belongs to a layer for which layerA is a direct reference layer of that layer is an IRAP picture and the VCL NAL units of pictureB have the same value of nal_unit_type as that of pictureA. cross_layer_irap_aligned_flag equal to 0 specifies that the above restriction may or may not apply.

## Slide 10
Thank you !
<number>