## Slide 1
AHG5 and AHG8: Recommended profiling of range extension coding tools
Samsung Electronics
JCTVC-O0144
Sunil Lee, Elena Alshina, Chanyul Kim, Ken McCann
Samsung Electronics and Zetacast

## Slide 2
Contents
Inspire the World, Create the Future
Samsung Electronics
Ⅰ
Ⅱ
Ⅲ
Ⅳ
Introduction
Test Results
Recommended Profiles
Conclusion

## Slide 3
Introduction
  At the last meeting in Vienna, five profiles for HEVC range extensions were defined – Main 12, Main 4:2:2 10/12, and Main 4:4:4 10/12.
  However, it was not determined which range extension coding tools were to be included in each profile.
  In this contribution, five coding tools which have been adopted into HEVC range extensions are evaluated under common test condition (CTC).
  The increased bit-depth and extended color format, which are primary goals of HEVC range extensions, are now considered for consumer electronics such as ultra high-definition (UHD) TV which is already available in the market.
  Based on the test results and the requirement from the market, the mapping between the profiles and coding tools is recommended in this contribution.
Samsung Electronics

## Slide 4
Test Results (1/5)
Anchor: HM12.0-RExt4.1, intra RDPCM disabled
Tested results: HM12.0-RExt4.1 (CTC, lossy coding anchor)
Almost no gain for camera-captured test sequences in CTC
Samsung Electronics
BD-rate Y | AI-MT | AI-HT | AI-SHT | RA-MT | RA-HT | LB-MT | LB-HT
RGB 4:4:4 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
YCbCr 4:4:4 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | -0.1% | -0.1%
YCbCr 4:2:2 | -0.1% | -0.1% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Overall | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Enc Time[%] | 101% | 101% | 100% | 101% | 101% | 101% | 100%
Dec Time[%] | 100% | 100% | 100% | 100% | 100% | 99% | 98%

## Slide 5
Test Results (2/5)
Anchor: HM12.0-RExt4.1, inter RDPCM disabled
Tested results: HM12.0-RExt4.1 (CTC, lossy coding anchor)
Almost no gain for camera-captured test sequences in CTC
Samsung Electronics
BD-rate Y | AI-MT | AI-HT | AI-SHT | RA-MT | RA-HT | LB-MT | LB-HT
RGB 4:4:4 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
YCbCr 4:4:4 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | -0.1% | -0.1%
YCbCr 4:2:2 | 0.0% | 0.0% | 0.0% | -0.1% | -0.1% | -0.1% | -0.1%
Overall | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | -0.1% | -0.1%
Enc Time[%] | 100% | 101% | 100% | 103% | 103% | 102% | 102%
Dec Time[%] | 101% | 101% | 101% | 98% | 97% | 96% | 97%

## Slide 6
Test Results (3/5)
Anchor: HM12.0-RExt4.1, residual rotation disabled
Tested results: HM12.0-RExt4.1 (CTC, lossy coding anchor)
Better than intra/inter RDPCM, but still the coding gain for camera-captured test sequences in CTC is marginal (up to -0.1%)
Samsung Electronics
BD-rate Y | AI-MT | AI-HT | AI-SHT | RA-MT | RA-HT | LB-MT | LB-HT
RGB 4:4:4 | -0.1% | -0.1% | 0.0% | -0.1% | 0.0% | 0.0% | 0.0%
YCbCr 4:4:4 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | -0.1% | 0.0%
YCbCr 4:2:2 | -0.1% | -0.1% | 0.0% | -0.1% | -0.1% | -0.1% | -0.1%
Overall | -0.1% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Enc Time[%] | 101% | 101% | 101% | 100% | 100% | 100% | 100%
Dec Time[%] | 99% | 100% | 100% | 96% | 97% | 96% | 97%

## Slide 7
Test Results (4/5)
Anchor: HM12.0-RExt4.1, “single context model for significance map coding in transform skip block” disabled
Tested results: HM12.0-RExt4.1 (CTC, lossy coding anchor)
Surprisingly, this simplest change is better than previous 3 coding tools, but still the coding gain for camera-captured test sequences in CTC is marginal (up to -0.2%)
Samsung Electronics
BD-rate Y | AI-MT | AI-HT | AI-SHT | RA-MT | RA-HT | LB-MT | LB-HT
RGB 4:4:4 | -0.1% | -0.1% | 0.0% | -0.1% | -0.1% | 0.0% | -0.1%
YCbCr 4:4:4 | 0.0% | -0.1% | 0.0% | -0.1% | -0.1% | -0.1% | -0.1%
YCbCr 4:2:2 | -0.1% | -0.1% | -0.1% | -0.1% | -0.2% | -0.1% | -0.2%
Overall | -0.1% | -0.1% | -0.1% | -0.1% | -0.1% | -0.1% | -0.1%
Enc Time[%] | 100% | 100% | 100% | 100% | 100% | 100% | 100%
Dec Time[%] | 100% | 100% | 100% | 99% | 99% | 99% | 100%

## Slide 8
Test Results (5/5)
Anchor: HM12.0-RExt4.1, intra block copy disabled
Tested results: HM12.0-RExt4.1 (CTC, lossy coding anchor)
The best coding gain among 5 coding tools under consideration in this contribution (up to -0.7% for RGB 4:4:4 in AI), but still the coding gain for camera-captured test sequences in CTC is marginal.
Furthermore, intra block copy introduces unacceptably high encoder complexity (up to 158% in AI) and increase the implementation cost, e.g. additional memory to keep the reference samples in intra should be added.
Samsung Electronics
BD-rate Y | AI-MT | AI-HT | AI-SHT | RA-MT | RA-HT | LB-MT | LB-HT
RGB 4:4:4 | -0.7% | -0.3% | -0.2% | -0.4% | -0.1% | -0.2% | -0.1%
YCbCr 4:4:4 | -0.3% | -0.3% | -0.2% | -0.1% | -0.1% | 0.0% | 0.0%
YCbCr 4:2:2 | -0.3% | -0.2% | -0.1% | -0.1% | -0.1% | 0.0% | 0.0%
Overall | -0.4% | -0.3% | -0.1% | -0.2% | -0.1% | -0.1% | 0.0%
Enc Time[%] | 158% | 155% | 152% | 119% | 117% | 114% | 112%
Dec Time[%] | 99% | 99% | 100% | 99% | 98% | 98% | 99%

## Slide 9
Conclusion
  The profiling of range extension coding tools should use a similar evidence-based decision process to that used for HEVC v1, based on testing under the range extension common test conditions.
  Test results show that all five of the coding tools evaluated in this contribution give near-zero benefit when evaluated under these conditions.
  At the same time, there is an immediate market requirement for HEVC range extensions which fulfill the stated purpose of Amd 1: to support high fidelity video signals in the high end consumer and professional environment.
  It is recommended that range extension profiles in Amd 1 should provide generic support for increased bit depth and extended colour formats, without adding coding tools that are beneficial only for screen content.
  It is also recommended to develop separate 4:4:4 profiles focused on screen content, in coordination with the call for proposals for coding of screen content and medical visual content planned for January 2014.
  It may be appropriate to consider including the five additional coding tools analyzed in this proposal in the initial test model for this new activity.
Samsung Electronics

## Slide 10
References
M. Zhou, M. Budagavi, “RCE2: Experimental results on Test 3 and Test 4,” Document of Joint Collaborative Team on Video Coding, JCTVC-M0056, Apr. 2013.
R. Joshi, J. Sole, M. Karczewicz, “RCE2 subtest C.2: Extension of residual DPCM to lossy coding,” Document of Joint Collaborative Team on Video Coding, JCTVC-N0052, Jul. 2013.
M. Naccari, M. Mrak, “RCE2: Experimental results for Test C.1,” Document of Joint Collaborative Team on Video Coding, JCTVC-N0074, Jul. 2013.
D. He, J. Wang, G. Martin-Cocher, “Rotation of Residual Block for Transform Skipping,” Document of Joint Collaborative Team on Video Coding, JCTVC-J0093, Jun. 2012.
T. Tsukuba, T. Yamamoto, “Constant coefficient context for intra transform skipping,” Document of Joint Collaborative Team on Video Coding, JCTVC-J0069, Jun. 2012.
C. Pang, J. Sole, L. Guo, M. Karczewicz, R. Joshi, “Non-RCE3: Intra Motion Compensation with 2-D MVs,” Document of Joint Collaborative Team on Video Coding, JCTVC-N0256, Jul. 2013.
D. Flynn, K. Sharman, C. Rosewarne, “Common test conditions and software reference configurations for HEVC range extensions,” Document of Joint Collaborative Team on Video Coding, JCTVC-N1006, Aug. 2013.
MPEG Video and JCT-VC, “Request for ISO/IEC 23008-2:201X/Amd.1”, ISO/IEC JTC1/SC29/WG11/N13344, Jan. 2013
Samsung Electronics

## Slide 11
THANK YOU
Inspire the World, Create the Future

## Slide 12
Appendix – List of test sequences
Samsung Electronics
RGB 4:4:4 | YCbCr 4:4:4 | YCbCr 4:2:2
Traffic_2560x1600_30_12bit_444_crop.rgb | Traffic_2560x1600_30_10bit_444_crop.yuv | Traffic_2560x1600_30_10bit_422_crop.yuv
Kimono1_1920x1080_24_10bit_444.rgb | Kimono1_1920x1080_24_10bit_444.yuv | Kimono1_1920x1080_24_10bit_422.yuv
EBULupoCandlelight_1920x1080_50_10bit_444.rgb | EBULupoCandlelight_1920x1080_50_10bit_444.yuv | EBUHorse_1920x1080_50_10bit_422.yuv
EBURainFruits_1920x1080_50_10bit_444.rgb | EBURainFruits_1920x1080_50_10bit_444.yuv | EBUGraphics_1920x1080_50_10bit_422.yuv
VenueVu_1920x1080_30_8bit_444.rgb | VenueVu_1920x1080_30_10bit_444.yuv | EBUWaterRocksClose_1920x1080_50_10bit_422.yuv
DucksAndLegs_1920x1080_30_10bit_444.rgb | BirdsInCage_1920x1080_60_10bit_444.yuv | EBUKidsSoccer_1920x1080_50_10bit_422.yuv
OldTownCross_1920x1080_50_10bit_444.rgb | CrowdRun_1920x1080_50_10bit_444.yuv | Seeking_1920x1080_50_10bit_422.yuv
ParkScene_1920x1080_24_10bit_444.rgb |  |