## Slide 1: [AHG16] JCTVC-O0145 - Key picture concept and single loop decoding
Christian Feldmann, Mathias Wien
Notes: n: die Conclusions könnten noch knackiger werden. - Mach am besten bei den results auf einem einführungsslide noch klar, dass Du CTC für die Referenz hast, und was die mods für das Proposal sind (8:10:47 PM) mathias.wien: und die frage, wie man das signalisiert, sollten wir zumindest auf dem letzten Slide noch aufwerfen, vielleicht als TBD...

## Slide 2: 1 – Key picture concept
Key picture concept in SHM3.0.1
  1 Key picture per GOP (POC 0,8,…)
  BL key pictures:
    Use only other BL key pictures for inter prediction (POC -8,-16)
  BL non key pictures:
    Use EL reconstruction for inter prediction
    TMVP: Use BL or deactivate
  Requires Multi-loop decoding

## Slide 3: 1 - Conventional prediction
GOP size 8
SHM 3.0.1 random access

## Slide 4: 1 - Key picture concept
Periodic key pictures (0, 8, 16 …)
Non key pictures predict from EL

## Slide 5: 1 - Key picture concept - Drift
Decoding BL only
In BL: Use BL for prediction
No drift for key pictures

## Slide 6: 1 – Results (vs. SHM2.0 CTC) (JCTVC-N0202)
RA HEVC SNR |  |  | 
 | Y | U | V
Class A | -3,5% | -10,2% | -10,4%
Class B | -2,9% | -8,4% | -10,1%
Overall (Test vs Ref) | -3,1% | -8,9% | -10,2%
BL Drift |  |  | 
 | Y | U | V
Class A | 4,0% | 2,0% | 1,8%
Class B | 4,7% | 2,4% | 2,4%
Overall (Test vs Ref) | 4,5% | 2,3% | 2,2%
Class A | -0,17 dB | -0,04 dB | -0,03 dB
Class B | -0,12 dB | -0,03 dB | -0,04 dB
Overall (Test vs Ref) | -0,13 dB | -0,04 dB | -0,04 dB
Notes: Similar idea as JCTVC-O0227

## Slide 7: 2 – Single Loop Decoding
Changes to support single loop decoding:
  Use unfiltered BL reference in EL
  Use constrained intra prediction in BL
  Only zero MV for BL prediction
Single loop decoding:
  Base layer Intra has to be decoded
  Base layer key pictures need to be decoded
Stream can be decoded by single- and multi loop decoder implementations

## Slide 8: 2 – Results (vs. SHM3.0.1 CTC)
 | BD-Rate |  |  |  |  |  | 
 | RA HEVC SNR |  |  |  | RA HEVC SNR BL ONLY |  | 
 | Y | U | V |  | Y | U | V
Class A | 1,6% | -7,0% | -7,1% |  | 6,7% | 3,5% | 3,6%
Class B | 1,1% | -5,4% | -7,7% |  | 6,7% | 4,7% | 4,6%
Overall (Test vs Ref) | 1,2% | -5,9% | -7,5% |  | 6,7% | 4,4% | 4,3%
 | RA HEVC SNR BL ONLY (BD-PRSN) |  | 
 | Y | U | V
Class A | -0,2839 | -0,0748 | -0,0674
Class B | -0,1672 | -0,0630 | -0,0841
Overall (Test vs Ref) | -0,2006 | -0,0664 | -0,0794

## Slide 9: 2 – Complexity Results (vs. SHM3.0.1 CTC)
 | RA HEVC SNR |  |  |  |  | LD-B HEVC SNR |  |  | 
 | Pure | DDR2 | DDR3 | Mults |  | Pure | DDR2 | DDR3 | Mults
Class A | 61% | 63% | 66% | 68% |  | 65% | 67% | 71% | 77%
Class B | 61% | 64% | 68% | 67% |  | 66% | 70% | 75% | 75%
Overall | 61% | 64% | 67% | 68% |  | 66% | 68% | 73% | 76%
 | RA | LDB
Pix Inter | 82,09% | 85,27%
Pix Intra | 84,62% | 78,42%
Pix MV Full Sum | 51,10% | 56,19%
Pix MV Half | 64,42% | 78,53%
Pix MV Quarter | 65,75% | 74,84%
Pix MV Full BL | 5,17% | 2,15%
Pix Inv Transf Y | 98,41% | 94,95%
Pix Deblocking Y | 65,66% | 67,30%
Pix SAO Y | 102,21% | 99,02%

## Slide 10: 3 – Modified scheme
Original scheme:
  Use unfiltered BL reconstruction for inter layer prediction
Modified scheme:
  Use filtered BL reconstruction for inter layer prediction in key pictures

## Slide 11: 3 – Results (vs. SHM3.0.1 CTC)
 | BD-Rate |  |  |  |  |  | 
 | RA HEVC SNR |  |  |  | RA HEVC SNR BL ONLY |  | 
 | Y | U | V |  | Y | U | V
Class A | -0,7% | -8,2% | -8,1% |  | 6,5% | 3,3% | 3,5%
Class B | -0,7% | -6,3% | -8,1% |  | 6,5% | 4,6% | 4,5%
Overall (Test vs Ref) | -0,7% | -6,8% | -8,1% |  | 6,5% | 4,2% | 4,2%
 | RA HEVC SNR BL ONLY (BD-PRSN) |  | 
 | Y | U | V
Class A | -0,2748 | -0,0723 | -0,0658
Class B | -0,1632 | -0,0613 | -0,0816
Overall (Test vs Ref) | -0,1951 | -0,0644 | -0,0771

## Slide 12: 3 – Complexity Results (vs. SHM3.0.1 CTC)
 | RA HEVC SNR |  |  |  |  | LD-B HEVC SNR |  |  | 
 | Pure | DDR2 | DDR3 | Mults |  | Pure | DDR2 | DDR3 | Mults
Class A | 61% | 63% | 66% | 68% |  | 65% | 66% | 70% | 76%
Class B | 61% | 64% | 68% | 67% |  | 66% | 70% | 74% | 75%
Overall | 61% | 63% | 67% | 68% |  | 65% | 68% | 72% | 75%
 | RA | LDB
Pix Inter | 79,11% | 85,33%
Pix Intra | 83,25% | 76,53%
Pix MV Full Sum | 47,70% | 55,84%
Pix MV Half | 60,60% | 77,87%
Pix MV Quarter | 61,30% | 74,22%
Pix MV Full BL | 5,25% | 2,11%
Pix Inv Transf Y | 98,28% | 94,67%
Pix Deblocking Y | 63,33% | 66,86%
Pix SAO Y | 101,60% | 95,60%

## Slide 13: Conclusion
Using key picture concept increases overall performance
Drift when decoding only BL
No low level changes
Single loop decoding:
  Performance 1.2%, modified scheme -0.7%
  Significant complexity reduction
  Specification change:
    Prediction structure (see JCTVC-O0227)
    Constrained Intra
    Only 0 mv for inter layer prediction
    no filtering in BL for non key pictures

## Slide 14: Conclusion
Proposal:
  Consider inclusion of single loop SNR decoding in the design
  Continue CE with updated schemes
Thanks to InterDigital for cross checking