## Slide 1: Displacement Vector Signaling for Intra Block Copying JCTVC-N0154
Chao Pang, Joel Sole, Liwei Guo, Rajan Joshi, Marta Karczewicz

## Slide 2: Introduction
  Intra block copying (JCTVC-N0256)
  Two methods are proposed to improve the coding efficiency of DV
left CTU
current CTU
CU
DV
DV (displacement vector)

## Slide 3: Method 1
The left or above DV is selected as predictor, and the resulting displacement vector difference (DVD) is encoded;
  A flag indicates whether the difference is zero
  If the DVD is not zero, expo-Golomb code with order 3 encodes the remaining absolute level of the DVD and a flag encodes the sign
To avoid extra line buffer to store the above MV, only the above MV inside current CTU is allowed to be used as the predictor

## Slide 4: Method 2
No DV predictor used
  A flag indicates whether the DV is zero
  If the DV is not zero, exponential-Golomb codes of order 4 encodes the DV remaining absolute level and a flag encodes the sign

## Slide 5: Experimental results
Lossy and lossless RCE2/RCE3 test conditions
Comparing the anchor, we test
  Method 1: DV coding with predictor
  Method 2: DV coding without predictor

## Slide 6: MV with predictor (lossless)
 | AI Main |  |  |  | RA Main |  |  |  | LB Main |  |  | 
Bit-rate saving | Total | Average | Min | Max | Total | Average | Min | Max | Total | Average | Min | Max
Class F | 0.4% | 0.6% | 0.0% | 2.0% | 0.0% | 0.5% | 0.0% | 2.0% | 0.0% | 0.5% | 0.0% | 2.0%
Class B | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
SC RGB 444 | 0.4% | 0.5% | 0.1% | 0.9% | 0.2% | 0.4% | 0.0% | 0.7% | 0.1% | 0.4% | -0.4% | 1.6%
Animation RGB 444 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
SC YUV 444 | 0.5% | 0.6% | 0.1% | 1.1% | 0.2% | 0.4% | 0.1% | 0.9% | 0.2% | 0.5% | 0.0% | 1.4%
Animation YUV 444 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
RangeExt | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
SC GBR 444 Optional | 0.8% | 1.0% | 0.4% | 1.5% | 0.4% | 0.9% | 0.3% | 1.5% | 0.3% | 1.1% | 0.3% | 1.5%
SC YUV 444 Optional | 1.7% | 1.9% | 0.8% | 3.3% | 1.0% | 1.6% | 0.8% | 2.6% | 0.8% | 0.7% | -1.5% | 2.7%
Enc Time[%] | 98% |  |  |  | 98% |  |  |  | 97% |  |  | 
Dec Time[%] | 98% |  |  |  | 99% |  |  |  | 98% |  |  | 

## Slide 7: MV with predictor (lossy)
 | All Intra HE Main-tier |  |  | All Intra HE High-tier |  |  | All Intra HE Super-High-tier |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class F | -1.3% | -1.2% | -1.2% | -0.9% | -1.0% | -0.9% | -0.7% | -0.7% | -0.7%
Class B | -0.1% | -0.1% | -0.1% | -0.1% | -0.1% | -0.1% | 0.0% | 0.0% | 0.0%
SC RGB 444 | -1.8% | -1.8% | -1.9% | -1.4% | -1.5% | -1.5% | -1.2% | -1.2% | -1.1%
Animation RGB 444 | -0.2% | -0.2% | -0.2% | -0.1% | -0.1% | -0.1% | 0.0% | -0.1% | -0.1%
SC YUV 444 | -2.8% | -2.8% | -2.9% | -2.2% | -2.2% | -2.3% | -1.7% | -1.6% | -1.7%
Animation YUV 444 | -0.3% | -0.3% | -0.3% | -0.2% | -0.2% | -0.2% | -0.1% | -0.1% | -0.1%
RangeExt | 0.0% | 0.0% | -0.1% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
SC(444) GBR Optional | -5.4% | -5.6% | -5.6% | -5.1% | -5.1% | -5.1% | -4.5% | -4.2% | -4.2%
SC(444) YUV Optional | -4.8% | -4.9% | -4.9% | -4.0% | -4.1% | -4.2% | -3.3% | -3.4% | -3.3%
Enc Time[%] | 98% |  |  | 99% |  |  | 98% |  | 
Dec Time[%] | 96% |  |  | 96% |  |  | 97% |  | 
 | Random Access HE Main-tier |  |  | Random Access HE High-tier |  | 
 | Y | U | V | Y | U | V
Class F | -1.0% | -1.1% | -1.0% | -0.8% | -0.8% | -0.7%
Class B | -0.1% | -0.1% | 0.0% | 0.0% | 0.0% | 0.0%
SC RGB 444 | -1.4% | -1.4% | -1.5% | -1.1% | -1.1% | -1.1%
Animation RGB 444 | -0.2% | -0.2% | -0.2% | -0.1% | -0.1% | -0.1%
SC YUV 444 | -2.4% | -2.4% | -2.3% | -1.7% | -1.7% | -1.7%
Animation YUV 444 | -0.1% | -0.2% | 0.0% | -0.1% | -0.2% | 0.0%
RangeExt | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
SC(444) GBR Optional | -5.1% | -5.1% | -5.2% | -4.6% | -4.7% | -4.6%
SC(444) YUV Optional | -4.8% | -4.8% | -5.0% | -4.1% | -4.0% | -4.2%
Enc Time[%] | 100% |  |  | 100% |  | 
Dec Time[%] | 99% |  |  | 99% |  | 
 | Low delay B HE Main-tier |  |  | Low delay B HE High-tier |  | 
 | Y | U | V | Y | U | V
Class F | -0.8% | -1.4% | -1.2% | -0.6% | -0.8% | -0.8%
Class B | 0.0% | 0.0% | -0.3% | 0.0% | 0.0% | 0.0%
SC RGB 444 | -0.8% | -0.7% | -0.7% | -0.6% | -0.4% | -0.4%
Animation RGB 444 | -0.1% | -0.2% | -0.1% | 0.0% | -0.1% | -0.1%
SC YUV 444 | -2.4% | -2.3% | -2.5% | -1.8% | -1.6% | -1.8%
Animation YUV 444 | -0.1% | -0.2% | -0.1% | 0.0% | -0.1% | -0.1%
RangeExt | 0.0% | 0.1% | -0.1% | 0.0% | 0.0% | -0.1%
SC(444) GBR Optional | -3.6% | -3.3% | -3.4% | -3.6% | -3.3% | -3.3%
SC(444) YUV Optional | -4.7% | -4.3% | -4.7% | -3.2% | -2.7% | -3.1%
Enc Time[%] | 99% |  |  | 99% |  | 
Dec Time[%] | 98% |  |  | 98% |  | 

## Slide 8
 | AI Main |  |  |  | RA Main |  |  |  | LB Main |  |  | 
Bit-rate saving | Total | Average | Min | Max | Total | Average | Min | Max | Total | Average | Min | Max
Class F | 0.1% | 0.2% | 0.0% | 0.6% | 0.0% | 0.2% | 0.0% | 0.4% | 0.0% | 0.1% | 0.0% | 0.4%
Class B | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
SC RGB 444 | 0.2% | 0.3% | 0.0% | 0.4% | 0.1% | 0.2% | 0.1% | 0.4% | 0.1% | 0.2% | 0.0% | 0.5%
Animation RGB 444 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
SC YUV 444 | 0.3% | 0.3% | 0.1% | 0.5% | 0.1% | 0.3% | 0.1% | 0.5% | 0.0% | 0.2% | -0.3% | 0.6%
Animation YUV 444 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
RangeExt | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
SC GBR 444 Optional | 0.4% | 0.5% | 0.2% | 0.8% | 0.2% | 0.3% | -0.1% | 0.8% | 0.2% | 1.4% | 0.1% | 3.7%
SC YUV 444 Optional | 0.8% | 0.8% | 0.4% | 1.2% | 0.6% | 0.8% | 0.5% | 1.3% | 0.4% | -0.6% | -3.5% | 1.1%
Enc Time[%] | 103% |  |  |  | 103% |  |  |  | 102% |  |  | 
Dec Time[%] | 99% |  |  |  | 101% |  |  |  | 100% |  |  | 
MV without predictor (lossless)

## Slide 9
MV without predictor (lossy)
 | All Intra HE Main-tier |  |  | All Intra HE High-tier |  |  | All Intra HE Super-High-tier |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class F | -0.7% | -0.8% | -0.6% | -0.5% | -0.6% | -0.5% | -0.4% | -0.4% | -0.4%
Class B | -0.1% | 0.0% | -0.1% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
SC RGB 444 | -0.8% | -0.8% | -0.8% | -0.6% | -0.6% | -0.6% | -0.5% | -0.5% | -0.5%
Animation RGB 444 | -0.1% | -0.1% | -0.1% | 0.0% | -0.1% | 0.0% | 0.0% | 0.0% | 0.0%
SC YUV 444 | -1.3% | -1.2% | -1.3% | -1.0% | -0.9% | -0.9% | -0.7% | -0.7% | -0.6%
Animation YUV 444 | -0.1% | -0.1% | -0.1% | 0.0% | -0.1% | -0.1% | 0.0% | 0.0% | 0.0%
RangeExt | 0.0% | 0.0% | -0.1% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
SC(444) GBR Optional | -0.9% | -1.1% | -1.0% | -0.7% | -1.0% | -0.9% | -0.7% | -0.8% | -0.7%
SC(444) YUV Optional | -1.8% | -1.8% | -1.8% | -1.5% | -1.5% | -1.5% | -1.3% | -1.4% | -1.3%
Enc Time[%] | 101% |  |  | 102% |  |  | 101% |  | 
Dec Time[%] | 99% |  |  | 99% |  |  | 99% |  | 
 | Random Access HE Main-tier |  |  | Random Access HE High-tier |  | 
 | Y | U | V | Y | U | V
Class F | -0.5% | -0.6% | -0.5% | -0.4% | -0.4% | -0.3%
Class B | -0.1% | 0.0% | -0.1% | 0.0% | 0.0% | -0.1%
SC RGB 444 | -0.7% | -0.7% | -0.7% | -0.7% | -0.6% | -0.7%
Animation RGB 444 | -0.1% | -0.1% | -0.1% | 0.0% | 0.0% | 0.0%
SC YUV 444 | -0.9% | -1.0% | -1.0% | -0.6% | -0.7% | -0.7%
Animation YUV 444 | 0.0% | -0.1% | 0.0% | 0.0% | -0.1% | 0.0%
RangeExt | 0.0% | 0.0% | 0.1% | 0.0% | 0.0% | 0.0%
SC(444) GBR Optional | -0.8% | -0.8% | -0.8% | -0.6% | -0.5% | -0.5%
SC(444) YUV Optional | -2.0% | -2.0% | -2.0% | -1.6% | -1.5% | -1.6%
Enc Time[%] | 95% |  |  | 96% |  | 
Dec Time[%] | 100% |  |  | 99% |  | 
 | Low delay B HE Main-tier |  |  | Low delay B HE High-tier |  | 
 | Y | U | V | Y | U | V
Class F | -0.3% | -0.7% | 0.0% | -0.2% | -0.3% | -0.2%
Class B | 0.0% | 0.0% | -0.3% | 0.0% | 0.0% | 0.0%
SC RGB 444 | -0.7% | -0.4% | -0.5% | -0.5% | -0.3% | -0.4%
Animation RGB 444 | -0.1% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
SC YUV 444 | -1.4% | -1.2% | -1.5% | -0.8% | -0.6% | -0.9%
Animation YUV 444 | 0.0% | 0.0% | -0.1% | 0.0% | 0.0% | -0.1%
RangeExt | 0.0% | 0.0% | -0.1% | 0.0% | 0.0% | -0.1%
SC(444) GBR Optional | -0.4% | -0.3% | -0.2% | 0.2% | 0.4% | 0.3%
SC(444) YUV Optional | -2.6% | -2.4% | -2.4% | -1.6% | -1.4% | -1.6%
Enc Time[%] | 99% |  |  | 98% |  | 
Dec Time[%] | 99% |  |  | 99% |  | 

## Slide 10: Displacement Vector Signaling for Intra Block Copying JCTVC-N0154
Chao Pang, Joel Sole, Liwei Guo, Rajan Joshi, Marta Karczewicz