## Slide 1: Intra block copying with padding JCTVC-O0157
Chao Pang, Joel Sole, Liwei Guo , Rajan Joshi, Marta Karczewicz (Qualcomm)
Tao Lin, Shuhui Wang (Tongji University)

## Slide 2: Introduction
Intra block copying (Intra BC), JCTVC-N0256
left CTU
current CTU
CU
DV
DV (displacement vector)

## Slide 3: Intra BC
The reference block must be completely reconstructed
There is no overlap between the current block and the reference block
Issues:
  Many “good” partially reconstructed reference blocks cannot be used
  Many “good” DVs are wasted

## Slide 4: Proposal: Intra BC with padding
When (DVx <= 0) && (DVx + W > 0) && (DVy <= 0) && (DVy + W > 0), the unavailable part is padded using horizontal copying

## Slide 5: Experimental results
RCE2/RCE3 test conditions
BD-rates for two cases
  Intra BC with padding
  Intra BC with padding with search region being current CTU + left 4 columns
  Intra BC with padding + DV coding method 1 in JCTVC-O0154

## Slide 6: Intra BC with padding (lossless)
 | AI Main |  |  |  | RA Main |  |  |  | LB Main |  |  | 
Bit-rate saving | Total | Average | Min | Max | Total | Average | Min | Max | Total | Average | Min | Max
Class F | 0.1% | 0.1% | 0.0% | 0.3% | 0.0% | 0.0% | -0.1% | 0.2% | 0.0% | 0.0% | 0.0% | 0.1%
Class B | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
SC RGB 444 | 0.4% | 0.6% | 0.2% | 1.6% | 0.2% | 0.4% | 0.1% | 1.5% | 0.1% | 0.4% | 0.0% | 1.3%
Animation RGB 444 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
SC YUV 444 | 0.4% | 0.5% | 0.1% | 1.2% | 0.2% | 0.5% | 0.0% | 1.2% | 0.1% | 0.3% | 0.0% | 1.0%
Animation YUV 444 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
RangeExt | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
SC GBR 444 Optional | 1.5% | 1.5% | 1.0% | 2.0% | 1.1% | 1.3% | 0.7% | 2.0% | 1.1% | 2.0% | 0.8% | 3.9%
SC YUV 444 Optional | 1.6% | 1.6% | 1.3% | 1.7% | 1.2% | 1.3% | 1.1% | 1.8% | 1.1% | 0.2% | -2.9% | 2.3%
Enc Time[%] | 103% |  |  |  | 102% |  |  |  | 100% |  |  | 
Dec Time[%] | 99% |  |  |  | 101% |  |  |  | 98% |  |  | 

## Slide 7: Intra BC with padding(lossy)
 | All Intra HE Main-tier |  |  | All Intra HE High-tier |  |  | All Intra HE Super-High-tier |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class F | -0.5% | -0.5% | -0.5% | -0.5% | -0.4% | -0.4% | -0.4% | -0.3% | -0.3%
Class B | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
SC RGB 444 | -0.8% | -0.8% | -0.9% | -0.9% | -0.8% | -0.8% | -0.8% | -0.7% | -0.7%
Animation RGB 444 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
SC YUV 444 | -0.9% | -0.8% | -0.9% | -0.8% | -0.8% | -0.7% | -0.8% | -0.7% | -0.6%
Animation YUV 444 | 0.0% | -0.1% | -0.1% | 0.0% | -0.1% | -0.1% | 0.0% | 0.0% | 0.0%
RangeExt | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
SC(444) GBR Optional | -3.2% | -3.3% | -3.6% | -3.4% | -3.6% | -4.0% | -3.4% | -3.4% | -3.6%
SC(444) YUV Optional | -1.9% | -1.6% | -1.6% | -1.9% | -1.7% | -1.6% | -1.9% | -1.8% | -1.8%
Enc Time[%] | 102% |  |  | 102% |  |  | 100% |  | 
Dec Time[%] | 95% |  |  | 95% |  |  | 95% |  | 
 | Random Access HE Main-tier |  |  |  | Random Access HE High-tier |  | 
 | Y |  | U | V | Y | U | V
Class F | -0.5% | -0.5% |  | -0.4% | -0.4% | -0.3% | -0.2%
Class B | 0.0% | 0.0% |  | 0.0% | 0.0% | 0.0% | 0.0%
SC RGB 444 | -0.6% | -0.5% |  | -0.6% | -0.7% | -0.6% | -0.7%
Animation RGB 444 | 0.0% | 0.0% |  | 0.0% | 0.0% | 0.0% | 0.0%
SC YUV 444 | -0.5% | -0.5% |  | -0.4% | -0.4% | -0.4% | -0.3%
Animation YUV 444 | 0.0% | -0.1% |  | 0.0% | 0.0% | -0.1% | 0.0%
RangeExt | -0.1% | -0.1% |  | 0.0% | 0.0% | 0.0% | -0.1%
SC(444) GBR Optional | -2.3% | -2.4% |  | -2.6% | -2.4% | -2.5% | -3.0%
SC(444) YUV Optional | -2.0% | -1.8% |  | -2.0% | -1.9% | -1.8% | -1.9%
Enc Time[%] | 101% |  |  |  | 101% |  | 
Dec Time[%] | 99% |  |  |  | 99% |  | 
 | Low delay B HE Main-tier |  |  | Low delay B HE High-tier |  | 
 | Y | U | V | Y | U | V
Class F | -0.4% | -0.7% | -0.6% | -0.3% | -0.3% | -0.3%
Class B | 0.0% | -0.2% | -0.1% | 0.0% | -0.1% | 0.0%
SC RGB 444 | -0.3% | -0.2% | -0.3% | -0.4% | -0.3% | -0.4%
Animation RGB 444 | 0.0% | -0.1% | -0.1% | 0.0% | 0.0% | -0.1%
SC YUV 444 | -1.0% | -1.0% | -1.2% | -0.8% | -0.7% | -0.9%
Animation YUV 444 | 0.0% | -0.1% | 0.0% | 0.0% | -0.1% | 0.0%
RangeExt | 0.0% | 0.1% | -0.1% | 0.0% | 0.0% | -0.1%
SC(444) GBR Optional | -0.9% | -0.8% | -1.0% | -1.3% | -1.2% | -1.3%
SC(444) YUV Optional | -2.5% | -2.2% | -2.2% | -1.7% | -1.3% | -1.7%
Enc Time[%] | 100% |  |  | 100% |  | 
Dec Time[%] | 99% |  |  | 99% |  | 

## Slide 8
Intra BC with padding in current CTU + 4 col(lossless)
 | AI Main |  |  |  | RA Main |  |  |  | LB Main |  |  | 
Bit-rate saving | Total | Average | Min | Max | Total | Average | Min | Max | Total | Average | Min | Max
Class F | 0.1% | 0.2% | 0.0% | 0.4% | 0.0% | 0.0% | -0.2% | 0.2% | 0.0% | 0.0% | 0.0% | 0.1%
Class B | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
SC RGB 444 | 0.7% | 1.0% | 0.2% | 2.9% | 0.3% | 0.7% | -0.1% | 2.8% | 0.1% | 0.5% | -0.3% | 2.1%
Animation RGB 444 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
SC YUV 444 | 0.6% | 0.8% | 0.1% | 2.4% | 0.4% | 0.9% | 0.0% | 2.4% | 0.0% | 0.4% | -0.8% | 2.0%
Animation YUV 444 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
RangeExt | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
SC GBR 444 Optional | 2.0% | 2.1% | 1.4% | 3.1% | 1.3% | 1.7% | 0.8% | 3.1% | 1.2% | 2.4% | 1.2% | 4.8%
SC YUV 444 Optional | 2.2% | 2.1% | 1.4% | 2.7% | 1.5% | 2.2% | 1.2% | 2.7% | 1.2% | 0.7% | -2.2% | 3.0%
Enc Time[%] | 101% |  |  |  | 103% |  |  |  | 100% |  |  | 
Dec Time[%] | 103% |  |  |  | 98% |  |  |  | 104% |  |  | 
Notes: <number>

## Slide 9
Intra BC with padding in current CTU + 4 col (lossy)
 | All Intra HE Main-tier |  |  | All Intra HE High-tier |  |  | All Intra HE Super-High-tier |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class F | -0.7% | -0.7% | -0.7% | -0.6% | -0.5% | -0.5% | -0.5% | -0.4% | -0.4%
Class B | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
SC RGB 444 | -1.5% | -1.4% | -1.5% | -1.5% | -1.3% | -1.4% | -1.4% | -1.3% | -1.3%
Animation RGB 444 | 0.0% | -0.1% | -0.1% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
SC YUV 444 | -1.5% | -1.3% | -1.4% | -1.4% | -1.2% | -1.3% | -1.4% | -1.2% | -1.2%
Animation YUV 444 | 0.0% | -0.1% | -0.1% | 0.0% | -0.1% | 0.0% | 0.0% | 0.0% | 0.0%
RangeExt | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
SC(444) GBR Optional | -4.5% | -4.5% | -4.9% | -4.7% | -4.9% | -5.5% | -4.5% | -4.6% | -4.9%
SC(444) YUV Optional | -2.9% | -2.4% | -2.6% | -2.7% | -2.4% | -2.5% | -2.7% | -2.5% | -2.6%
Enc Time[%] | 104% |  |  | 103% |  |  | 104% |  | 
Dec Time[%] | 96% |  |  | 96% |  |  | 96% |  | 
 | Random Access HE Main-tier |  |  | Random Access HE High-tier |  | 
 | Y | U | V | Y | U | V
Class F | -0.6% | -0.5% | -0.5% | -0.5% | -0.4% | -0.4%
Class B | 0.0% | -0.1% | 0.0% | 0.0% | -0.1% | 0.0%
SC RGB 444 | -1.2% | -1.1% | -1.2% | -1.2% | -1.1% | -1.1%
Animation RGB 444 | 0.0% | -0.1% | -0.1% | 0.0% | 0.0% | 0.0%
SC YUV 444 | -1.3% | -1.1% | -1.2% | -1.3% | -1.1% | -1.1%
Animation YUV 444 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
RangeExt | -0.1% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
SC(444) GBR Optional | -3.5% | -3.5% | -3.8% | -3.6% | -3.6% | -4.2%
SC(444) YUV Optional | -2.8% | -2.5% | -2.5% | -2.7% | -2.4% | -2.4%
Enc Time[%] | 99% |  |  | 99% |  | 
Dec Time[%] | 99% |  |  | 99% |  | 
 | Low delay B HE Main-tier |  |  | Low delay B HE High-tier |  | 
 | Y | U | V | Y | U | V
Class F | -0.6% | -0.4% | -0.3% | -0.4% | -0.2% | -0.3%
Class B | 0.0% | 0.0% | -0.2% | 0.0% | 0.0% | 0.0%
SC RGB 444 | -0.6% | -0.6% | -0.7% | -0.6% | -0.6% | -0.6%
Animation RGB 444 | -0.1% | -0.1% | -0.1% | 0.0% | 0.0% | 0.0%
SC YUV 444 | -1.1% | -0.9% | -1.1% | -0.7% | -0.5% | -0.5%
Animation YUV 444 | -0.1% | -0.2% | 0.0% | -0.1% | -0.1% | 0.0%
RangeExt | -0.1% | 0.1% | 0.0% | 0.0% | 0.0% | 0.0%
SC(444) GBR Optional | -2.4% | -2.1% | -2.3% | -3.0% | -2.8% | -2.9%
SC(444) YUV Optional | -2.3% | -2.2% | -2.5% | -1.8% | -1.4% | -1.7%
Enc Time[%] | 100% |  |  | 100% |  | 
Dec Time[%] | 99% |  |  | 100% |  | 

## Slide 10: Intra BC with padding + DV coding (lossless)
 | AI Main |  |  |  | RA Main |  |  |  | LB Main |  |  | 
 | Bit-rate saving |  |  |  | Bit-rate saving |  |  |  | Bit-rate saving |  |  | 
 | Total | Average | Min | Max | Total | Average | Min | Max | Total | Average | Min | Max
Class F | 0.5% | 0.7% | 0.1% | 2.3% | 0.1% | 0.6% | 0.0% | 2.1% | 0.0% | 0.6% | 0.0% | 2.1%
Class B | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
SC RGB 444 | 0.8% | 1.0% | 0.2% | 2.3% | 0.4% | 0.8% | 0.2% | 2.2% | 0.2% | 0.7% | -0.3% | 2.2%
Animation RGB 444 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
SC YUV 444 | 0.9% | 1.1% | 0.2% | 2.2% | 0.4% | 0.8% | 0.1% | 2.1% | 0.2% | 0.6% | -0.3% | 2.2%
Animation YUV 444 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
RangeExt | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
SC GBR 444 Optional | 2.3% | 2.5% | 1.8% | 3.6% | 1.5% | 2.1% | 1.4% | 3.3% | 1.4% | 2.0% | 1.4% | 2.7%
SC YUV 444 Optional | 3.2% | 3.4% | 1.9% | 5.0% | 2.3% | 3.3% | 1.9% | 4.3% | 1.9% | 2.1% | 0.0% | 4.4%
Enc Time[%] | 103% |  |  |  | 97% |  |  |  | 99% |  |  | 
Dec Time[%] | 93% |  |  |  | 96% |  |  |  | 94% |  |  | 

## Slide 11: Intra BC with padding + DV coding (lossy)
 | All Intra HE Main-tier |  |  | All Intra HE High-tier |  |  | All Intra HE Super-High-tier |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class F | -1.7% | -1.7% | -1.7% | -1.3% | -1.4% | -1.3% | -1.0% | -1.0% | -1.0%
Class B | -0.1% | -0.1% | -0.1% | -0.1% | -0.1% | -0.1% | 0.0% | 0.0% | -0.1%
SC RGB 444 | -2.5% | -2.6% | -2.7% | -2.2% | -2.3% | -2.2% | -1.9% | -1.9% | -1.8%
Animation RGB 444 | -0.2% | -0.3% | -0.3% | -0.1% | -0.2% | -0.1% | -0.1% | -0.1% | -0.1%
SC YUV 444 | -3.5% | -3.5% | -3.6% | -2.9% | -2.9% | -2.9% | -2.4% | -2.3% | -2.3%
Animation YUV 444 | -0.3% | -0.3% | -0.4% | -0.2% | -0.2% | -0.2% | -0.1% | -0.2% | -0.1%
RangeExt | 0.0% | 0.0% | -0.1% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
SC(444) GBR Optional | -7.5% | -7.6% | -7.8% | -7.2% | -7.3% | -7.5% | -6.9% | -6.5% | -6.7%
SC(444) YUV Optional | -6.5% | -6.5% | -6.5% | -5.8% | -5.8% | -5.8% | -5.2% | -5.1% | -5.1%
Enc Time[%] | 104% |  |  | 104% |  |  | 102% |  | 
Dec Time[%] | 94% |  |  | 94% |  |  | 95% |  | 
 | Random Access HE Main-tier |  |  | Random Access HE High-tier |  | 
 | Y | U | V | Y | U | V
Class F | -1.4% | -1.4% | -1.4% | -1.1% | -1.1% | -1.0%
Class B | -0.1% | -0.1% | -0.1% | 0.0% | 0.0% | -0.1%
SC RGB 444 | -2.0% | -2.0% | -2.0% | -1.9% | -1.8% | -1.8%
Animation RGB 444 | -0.1% | -0.1% | -0.1% | -0.1% | -0.1% | -0.1%
SC YUV 444 | -2.7% | -2.8% | -2.6% | -2.2% | -2.3% | -2.2%
Animation YUV 444 | -0.1% | -0.2% | -0.2% | -0.1% | -0.2% | -0.1%
RangeExt | -0.1% | 0.0% | -0.1% | -0.1% | 0.0% | -0.1%
SC(444) GBR Optional | -6.2% | -6.3% | -6.5% | -5.9% | -6.0% | -6.2%
SC(444) YUV Optional | -6.4% | -6.3% | -6.5% | -5.5% | -5.3% | -5.5%
Enc Time[%] | 104% |  |  | 103% |  | 
Dec Time[%] | 100% |  |  | 99% |  | 
 | Low delay B HE Main-tier |  |  | Low delay B HE High-tier |  | 
 | Y | U | V | Y | U | V
Class F | -1.2% | -1.7% | -1.5% | -0.9% | -1.0% | -1.2%
Class B | 0.0% | 0.1% | 0.1% | 0.0% | 0.0% | 0.2%
SC RGB 444 | -1.2% | -1.2% | -1.2% | -1.1% | -1.0% | -1.0%
Animation RGB 444 | -0.1% | -0.2% | -0.2% | -0.1% | -0.1% | -0.1%
SC YUV 444 | -3.0% | -3.0% | -3.1% | -2.3% | -2.2% | -2.5%
Animation YUV 444 | -0.1% | -0.2% | -0.1% | -0.1% | -0.2% | -0.1%
RangeExt | 0.0% | 0.0% | -0.2% | 0.0% | -0.1% | -0.2%
SC(444) GBR Optional | -4.0% | -3.8% | -3.9% | -4.0% | -3.9% | -3.8%
SC(444) YUV Optional | -7.5% | -7.2% | -7.4% | -5.8% | -5.4% | -5.7%
Enc Time[%] | 103% |  |  | 102% |  | 
Dec Time[%] | 100% |  |  | 100% |  | 

## Slide 12: Conclusions
Intra BC with padding is proposed
  Improvement with 0.7~6% BD-rate reduction for most SC sequences and configurations tested
  Minor change to the semantics and decoding process
  Marginal impact on the encoder and decoder implementation complexity
  Independent of other DV coding methods for Intra BC, such as JCTVC-O0154

## Slide 13: Intra block copying with padding JCTVC-O0157
Chao Pang, Joel Sole, Liwei Guo , Rajan Joshi, Marta Karczewicz (Qualcomm)
Tao Lin, Shuhui Wang (Tongji University)