## Slide 1: Context Derivation Method for intra_bc_flag Coding JCTVC-N0158
Chao Pang, Joel Sole, Liwei Guo, Rajan Joshi, Marta Karczewicz

## Slide 2: Introduction
Intra block copying:
Currently, the context for intra_bc_flag is derived as follows
context value = (above intra_bc_flag == 0) ? 0: 1 + (left intra_bc_flag == 0) ? 0: 1
  Therefore, an extra line buffer is needed to store the above intra_bc_flag values.
Two methods are proposed to remove the line buffer
left CTU
current CTU
CU
DV

## Slide 3: Technical Description
Method 1
  Only the above flags inside the current CTU are used
  The number of context is kept being 3
Method 2
  Use a single context for intra_bc_flag coding
  The number of context is reduced to 1

## Slide 4: Experimental results
Methods integrated in HM12.0_RExt4.1
RCE2/RCE3 test conditions
The proposed methods are compared to the anchor in terms of BD-rate and bit-savings

## Slide 5: No line buffer + 3 contexts (lossless)
 | AI Main |  |  |  | RA Main |  |  |  | LB Main |  |  | 
 | Bit-rate saving |  |  |  | Bit-rate saving |  |  |  | Bit-rate saving |  |  | 
 | Total | Average | Min | Max | Total | Average | Min | Max | Total | Average | Min | Max
Class F | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.1% | 0.0% | 0.2% | 0.0% | 0.0% | 0.0% | 0.0%
Class B | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
SC RGB 444 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.1% | 0.0% | 0.0% | 0.0% | 0.0%
Animation RGB 444 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
SC YUV 444 | 0.0% | 0.0% | 0.0% | 0.0% | 0.1% | 0.1% | -0.1% | 0.7% | 0.0% | 0.0% | 0.0% | 0.0%
Animation YUV 444 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
RangeExt | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
SC GBR 444 Optional | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.1% | 0.0% | 0.1% | 0.0% | 0.8% | -0.5% | 3.1%
SC YUV 444 Optional | 0.0% | 0.0% | 0.0% | 0.0% | 0.1% | 0.2% | 0.0% | 0.6% | 0.0% | -0.1% | -0.3% | 0.0%
Enc Time[%] | 100% |  |  |  | 99% |  |  |  | 99% |  |  | 
Dec Time[%] | 100% |  |  |  | 100% |  |  |  | 100% |  |  | 

## Slide 6: No line buffer + 1 context (lossless)
 | AI Main |  |  |  | RA Main |  |  |  | LB Main |  |  | 
 | Bit-rate saving |  |  |  | Bit-rate saving |  |  |  | Bit-rate saving |  |  | 
 | Total | Average | Min | Max | Total | Average | Min | Max | Total | Average | Min | Max
Class F | 0.0% | 0.0% | -0.1% | 0.0% | 0.0% | 0.0% | -0.1% | 0.1% | 0.0% | 0.0% | -0.1% | 0.0%
Class B | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
SC RGB 444 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | -0.1% | -0.3% | 0.0% | 0.0% | 0.0% | -0.2% | 0.0%
Animation RGB 444 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
SC YUV 444 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | -0.1% | 0.0% | 0.0% | 0.0% | -0.1% | 0.0%
Animation YUV 444 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
RangeExt | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
SC GBR 444 Optional | 0.0% | -0.1% | -0.1% | 0.0% | 0.0% | 0.0% | -0.1% | 0.0% | 0.0% | -0.2% | -0.4% | 0.0%
SC YUV 444 Optional | -0.1% | -0.1% | -0.1% | 0.0% | 0.0% | 0.0% | -0.1% | 0.0% | 0.0% | -0.1% | -0.1% | 0.0%
Enc Time[%] | 101% |  |  |  | 101% |  |  |  | 99% |  |  | 
Dec Time[%] | 99% |  |  |  | 105% |  |  |  | 100% |  |  | 

## Slide 7
No line buffer + 3 contexts (lossy)
 | All Intra HE Main-tier |  |  | All Intra HE High-tier |  |  | All Intra HE Super-High-tier |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class F | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Class B | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
SC RGB 444 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Animation RGB 444 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
SC YUV 444 | 0.0% | 0.1% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Animation YUV 444 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
RangeExt | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
SC(444) GBR Optional | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
SC(444) YUV Optional | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Enc Time[%] | 99% |  |  | 99% |  |  | 99% |  | 
Dec Time[%] | 100% |  |  | 100% |  |  | 100% |  | 
 | Low delay B HE Main-tier |  |  | Low delay B HE High-tier |  | 
 | Y | U | V | Y | U | V
Class F | 0.0% | -0.5% | -0.2% | 0.0% | -0.2% | -0.2%
Class B | 0.0% | 0.0% | -0.2% | 0.0% | 0.0% | 0.0%
SC RGB 444 | 0.4% | 0.4% | 0.3% | 0.3% | 0.3% | 0.2%
Animation RGB 444 | 0.1% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
SC YUV 444 | -0.2% | -0.2% | -0.3% | -0.3% | -0.3% | -0.4%
Animation YUV 444 | 0.0% | -0.1% | 0.0% | 0.0% | -0.1% | 0.0%
RangeExt | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | -0.2%
SC(444) GBR Optional | -0.2% | -0.4% | -0.2% | 0.2% | 0.1% | 0.2%
SC(444) YUV Optional | -0.4% | -0.2% | -0.3% | 0.1% | 0.1% | 0.0%
Enc Time[%] | 100% |  |  | 100% |  | 
Dec Time[%] | 100% |  |  | 100% |  | 
 | Random Access HE Main-tier |  |  | Random Access HE High-tier |  | 
 | Y | U | V | Y | U | V
Class F | 0.0% | 0.0% | -0.1% | 0.0% | 0.0% | 0.0%
Class B | 0.0% | 0.1% | 0.0% | 0.0% | 0.0% | 0.0%
SC RGB 444 | 0.0% | 0.0% | 0.0% | -0.1% | -0.2% | -0.2%
Animation RGB 444 | -0.1% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
SC YUV 444 | -0.1% | -0.1% | -0.1% | 0.0% | 0.0% | 0.0%
Animation YUV 444 | 0.0% | 0.0% | 0.0% | 0.0% | -0.1% | 0.0%
RangeExt | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
SC(444) GBR Optional | 0.1% | 0.1% | 0.1% | 0.1% | 0.1% | 0.1%
SC(444) YUV Optional | -0.1% | -0.1% | -0.1% | -0.1% | -0.1% | -0.1%
Enc Time[%] | 101% |  |  | 101% |  | 
Dec Time[%] | 100% |  |  | 100% |  | 

## Slide 8
No line buffer + 1 context (lossy)
 | All Intra HE Main-tier |  |  | All Intra HE High-tier |  |  | All Intra HE Super-High-tier |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class F | 0.1% | 0.0% | 0.0% | 0.0% | 0.1% | 0.1% | 0.0% | 0.0% | 0.1%
Class B | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
SC RGB 444 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Animation RGB 444 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
SC YUV 444 | 0.1% | 0.2% | 0.1% | 0.1% | 0.1% | 0.1% | 0.0% | 0.1% | 0.1%
Animation YUV 444 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
RangeExt | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
SC(444) GBR Optional | 0.1% | 0.0% | 0.0% | 0.1% | 0.0% | 0.0% | 0.1% | -0.1% | 0.0%
SC(444) YUV Optional | 0.1% | 0.1% | 0.1% | 0.1% | 0.1% | 0.1% | 0.1% | 0.1% | 0.1%
Enc Time[%] | 98% |  |  | 99% |  |  | 99% |  | 
Dec Time[%] | 100% |  |  | 100% |  |  | 100% |  | 
 | Low delay B HE Main-tier |  |  | Low delay B HE High-tier |  | 
 | Y | U | V | Y | U | V
Class F | 0.1% | -0.1% | -0.2% | 0.1% | 0.0% | 0.1%
Class B | 0.1% | -0.1% | -0.1% | 0.0% | -0.1% | 0.1%
SC RGB 444 | 0.1% | 0.0% | 0.0% | 0.1% | 0.0% | -0.1%
Animation RGB 444 | 0.1% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
SC YUV 444 | 0.0% | 0.0% | -0.1% | 0.0% | 0.1% | -0.1%
Animation YUV 444 | 0.1% | 0.0% | 0.1% | 0.0% | 0.0% | 0.0%
RangeExt | 0.0% | 0.0% | -0.1% | 0.0% | 0.0% | -0.1%
SC(444) GBR Optional | -0.3% | -0.2% | -0.3% | -0.1% | -0.1% | -0.3%
SC(444) YUV Optional | -0.2% | 0.1% | -0.1% | 0.7% | 1.1% | 0.7%
Enc Time[%] | 100% |  |  | 100% |  | 
Dec Time[%] | 101% |  |  | 100% |  | 
 | Random Access HE Main-tier |  |  | Random Access HE High-tier |  | 
 | Y | U | V | Y | U | V
Class F | 0.0% | 0.0% | 0.1% | 0.0% | 0.0% | 0.1%
Class B | 0.0% | 0.0% | -0.1% | 0.0% | 0.0% | 0.0%
SC RGB 444 | 0.1% | 0.1% | 0.1% | 0.0% | -0.1% | -0.1%
Animation RGB 444 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
SC YUV 444 | 0.0% | -0.1% | 0.0% | 0.0% | -0.1% | 0.0%
Animation YUV 444 | 0.0% | 0.0% | 0.1% | 0.0% | 0.0% | 0.0%
RangeExt | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | -0.1%
SC(444) GBR Optional | 0.0% | 0.0% | 0.0% | 0.1% | 0.1% | 0.1%
SC(444) YUV Optional | -0.1% | -0.1% | -0.1% | -0.2% | 0.0% | 0.0%
Enc Time[%] | 102% |  |  | 101% |  | 
Dec Time[%] | 100% |  |  | 108% |  | 

## Slide 9: Context Derivation Method for intra_bc_flag Coding JCTVC-N0158
Chao Pang, Joel Sole, Liwei Guo, Rajan Joshi, Marta Karczewicz