## Slide 1: JCTVC-O0161 Non-SCE4/AHG14: Combined bit-depth and color gamut conversion with 3D LUT for SHVC color gamut scalability
Yuwen He, Yan Ye, Jie Dong
InterDigital Communications, Inc.
15th JCT-VC meeting, Oct.23 - Nov.1, 2013

## Slide 2: Introduction
  SHVC needs to support HDTV and UHDTV applications efficiently
    Base layer: BT.709 8-bit, 1080p
    Enhancement layer: BT.2020 10-bit, 4k x 2k or 8k x 4k
  Inter-layer process needs multiple conversions due to difference between BL and EL
    Bit-depth conversion (8-bit -> 10-bit)
    Color gamut conversion (BT.709 -> BT.2020)
    Upsampling (1080p -> 4K/8K)
  Combined bit-depth and color gamut conversion using 3D LUT is investigated in this proposal
    Higher coding efficiency
    Higher precision and fewer rounding errors
    No change to upsampling specified in SHVC

## Slide 3: Combined bit-depth and color gamut conversion
    Scheme 1 (proposed): Bit-depth conversion and color gamut conversion combined into one step
      Placing color conversion before upsampling can reduce the complexity
    Scheme 2 (for comparison): Bit-depth conversion is separated from color gamut conversion, but combined with upsampling
      Combined bit-depth conversion and upsampling is the same as JCTVC-O0194

## Slide 4: 3D LUT derived using offline training
  3D LUT for scheme 1: the proposed combined bit-depth and color gamut conversion
  3D LUT for scheme 2: 8-bit color gamut conversion for comparison
  3D LUT for 10-bit color gamut conversion: no normative change from JCTVC-O0159

## Slide 5: 3D LUT Signaling
  3D LUT is coded in PPS, one set for one bitstream
  bit_depth_input_luma_minus8 : (bit_depth_input_luma_minus8+8) is the bit-depth of the luma component for the input of 3D LUT interpolation (bit_depth_input_luma)
  bit_depth_input_chroma_delta : (bit_depth_input_chroma_delta + bit_depth_input_luma) is the bit-depth of the chroma component for the input of 3D LUT interpolation
  bit_depth_output_luma_delta : (bit_depth_output_luma_delta + bit_depth_input_luma) is the bit-depth of the luma component for the output of 3D LUT interpolation
  bit_depth_output_chroma_delta : (bit_depth_output_chroma_delta + bit_depth_input_luma) is the bit-depth of the chroma component for the output of 3D LUT interpolation
  layer_num_of_3D_LUT : the number of layers of 3D LUT octant tree
  3D_LUT() : 3D LUT information coded based on octant tree structure, the same as 3D LUT defined in JCTVC-O0159
color_gamut_conversion_param( ) { | Descriptor
bit_depth_input_luma_minus8 | ue(v)
bit_depth_input_chroma_delta | ue(v)
bit_depth_output_luma_delta | ue(v)
bit_depth_output_chroma_delta | ue(v)
layer_num_of_3D_LUT | ue(v)
3D_LUT() | 
} | 

## Slide 6: Simulation Results: the proposed scheme 1
 | AI HEVC 2x 10-bit base |  |  | AI HEVC 2x 8-bit base |  | 
 | Y | U | V | Y | U | V
Class A+ | -15.4% | -15.5% | -22.2% | -15.3% | -15.7% | -22.9%
Overall (Test vs Ref) | -15.4% | -15.5% | -22.2% | -15.3% | -15.7% | -22.9%
Overall (Test vs single layer) | 7.1% | 9.3% | 0.5% | 9.8% | 11.3% | 1.9%
Overall (Ref vs single layer) | 26.8% | 29.4% | 28.9% | 29.8% | 32.1% | 32.1%
EL only (Test vs Ref) | -28.2% | -27.8% | -33.7% | -28.3% | -28.3% | -34.6%
Overall (Test EL+BL vs single EL+BL) | -30.0% | -28.5% | -35.2% | -28.2% | -27.3% | -34.4%
 | RA HEVC 2x 10-bit base |  |  | RA HEVC 2x 8-bit base |  | 
 | Y | U | V | Y | U | V
Class A+ | -10.5% | -9.1% | -17.2% | -10.0% | -8.7% | -16.6%
Overall (Test vs Ref) | -10.5% | -9.1% | -17.2% | -10.0% | -8.7% | -16.6%
Overall (Test vs single layer) | 18.3% | 23.3% | 9.6% | 20.3% | 24.7% | 11.2%
Overall (Ref vs single layer) | 32.3% | 35.5% | 33.0% | 33.8% | 36.4% | 33.9%
EL only (Test vs Ref) | -18.9% | -17.0% | -24.6% | -18.4% | -16.5% | -23.9%
Overall (Test EL+BL vs single EL+BL) | -21.3% | -17.0% | -27.0% | -20.1% | -16.4% | -26.2%
  Scheme 1 compared with SCE4 anchors
    Combined bit-depth and color gamut conversion
    17x17x17 3D LUT

## Slide 7: Simulation Results: scheme 2 for comparison
 | AI HEVC 2x 10-bit base |  |  | AI HEVC 2x 8-bit base |  | 
 | Y | U | V | Y | U | V
Class A+ | -15.4% | -15.5% | -22.2% | -13.2% | -13.2% | -18.9%
Overall (Test vs Ref) | -15.4% | -15.5% | -22.2% | -13.2% | -13.2% | -18.9%
Overall (Test vs single layer) | 7.1% | 9.3% | 0.5% | 12.6% | 14.7% | 7.2%
Overall (Ref vs single layer) | 26.8% | 29.4% | 28.9% | 29.8% | 32.1% | 32.1%
EL only (Test vs Ref) | -28.2% | -27.8% | -33.7% | -24.6% | -24.3% | -29.4%
Overall (Test EL+BL vs single EL+BL) | -30.0% | -28.5% | -35.2% | -26.0% | -24.7% | -30.5%
 | RA HEVC 2x 10-bit base |  |  | RA HEVC 2x 8-bit base |  | 
 | Y | U | V | Y | U | V
Class A+ | -10.5% | -9.1% | -17.2% | -9.1% | -7.3% | -13.2%
Overall (Test vs Ref) | -10.5% | -9.1% | -17.2% | -9.1% | -7.3% | -13.2%
Overall (Test vs single layer) | 18.3% | 23.3% | 9.6% | 21.5% | 26.7% | 15.7%
Overall (Ref vs single layer) | 32.3% | 35.5% | 33.0% | 33.8% | 36.4% | 33.9%
EL only (Test vs Ref) | -18.9% | -17.0% | -24.6% | -16.8% | -14.4% | -19.9%
Overall (Test EL+BL vs single EL+BL) | -21.3% | -17.0% | -27.0% | -19.1% | -15.0% | -22.9%
  Scheme 2 compared with SCE4 anchors
    Separate color gamut conversion, combined bit depth conversion and upsampling (JCTVC-O0194)
    17x17x17 3D LUT

## Slide 8: Simulation results: scheme 1 (test) compared to scheme 2 (ref)
 | AI HEVC 2x 8-bit base |  | 
 | Y | U | V
Class A+ | -2.4% | -2.9% | -5.3%
Overall (Test vs Ref) | -2.4% | -2.9% | -5.3%
EL only (Test vs Ref) | -5.0% | -5.4% | -8.0%
 | RA HEVC 2x 8-bit base |  | 
 | Y | U | V
Class A+ | -1.0% | -1.5% | -4.1%
Overall (Test vs Ref) | -1.0% | -1.5% | -4.1%
EL only (Test vs Ref) | -2.0% | -2.5% | -5.4%

## Slide 9: Conclusions
  Combined bit-depth and color gamut conversion achieves higher coding efficiency compared with separate process
    {-2.4%, -2.9%, -5.3%} for AI-2x
    {-1.0%, -1.5%, -4.1%} for RA-2x
  The bit-depth difference between BL and EL is taken into account in 3D LUT interpolation
  No need to make any changes in upsampling
Thanks Technicolor for cross-checking!
(JCTVC-O0160)