## Slide 1: Non-SCE4: Weighted Prediction Based Color Gamut Scalability (JCTVC-O0180)
X. Li, V. Seregin, J. Chen, K. Rapaka, Y. Chen, and M. Karczewicz (Qualcomm Inc.)

## Slide 2: Overview
Weighted prediction based color gamut scalability
A new flag in PPS is signaled to avoid unnecessary cost

## Slide 3: WP based Color Gamut Scalability
Gain-offset model for inter-layer color prediction
  Pred[c][x][y] = (gain[c]*In[x][y] + (1<<(numFractionBits-1))>> numFractionBits + offset[c]
Weighted prediction based inter-layer color prediction
  Signaling gain and offset under the framework of weighted prediction
  Encoder only change

## Slide 4: A New Flag in PPS to Avoid Unnecessary Signaling Cost (I)
Weighted prediction is applied to inter-layer reference picture only
  No weighting for temporal references
Proposed syntax in PPS
pic_parameter_set_rbsp( ) { | Descriptor | 
pps_pic_parameter_set_id | ue(v) | 
…… |  | 
weighted_pred_flag | u(1) | 
weighted_bipred_flag | u(1) | 
if( nuh_layer_id > 0 && ( weighted_pred_flag ¦ ¦ weighted_bipred_flag ) ) |  | 
ilr_weight_only_flag | u(1) | 
} |  | 

## Slide 5: A New Flag in PPS to Avoid Unnecessary Signaling Cost (II)
Proposed changes in pred_weight_table
pred_weight_table( ) { | Descriptor
…. | ue(v)
for( i = 0; i <= num_ref_idx_l0_active_minus1; i++ ) | 
if(!ilr_weight_only_flag ¦ ¦ nuh_layer_id of RefPicList0[ i ] != currLayerId) | 
luma_weight_l0_flag[ i ] | u(1)
if( chroma_format_idc != 0 ) | 
for( i = 0; i <= num_ref_idx_l0_active_minus1; i++ ) | 
if(!ilr_weight_only_flag ¦ ¦ nuh_layer_id of RefPicList0[ i ] != currLayerId) | 
chroma_weight_l0_flag[ i ] | u(1)
for( i = 0; i <= num_ref_idx_l0_active_minus1; i++ ) { | 
if( luma_weight_l0_flag[ i ] ) { | 
delta_luma_weight_l0[ i ] | se(v)
luma_offset_l0[ i ] | se(v)
} | 
… | 
} | 
if( slice_type = = B ) { | 
for( i = 0; i <= num_ref_idx_l1_active_minus1; i++ ) | 
if(!ilr_weight_only_flag ¦ ¦ nuh_layer_id of RefPicList1[ i ] != currLayerId) | 
luma_weight_l1_flag[ i ] | u(1)
if( chroma_format_idc != 0 ) | 
for( i = 0; i <= num_ref_idx_l1_active_minus1; i++ ) | 
if(!ilr_weight_only_flag ¦ ¦ nuh_layer_id of RefPicList1[ i ] != currLayerId) | 
chroma_weight_l1_flag[ i ] | u(1)
… | 
} | 

## Slide 6: Simulation Results

## Slide 7: Conclusions
Weighted prediction based color gamut scalability is proposed without low level decoding process change.
Moreover, a flag in PPS is further introduced to indicate whether the weighted prediction is only applied to inter-layer reference pictures