## Slide 1: HLS: Non-significant tile set for tiled streaming with single layer HEVC extensions
Cheung Auyeung
Sony Electronics Inc.
Oct 22, 2013

## Slide 2: Tiled Streaming Example
8Kx4K at server
4Kx2K at server
HD to client
4Kx2K to client
4Kx2K to client

## Slide 3: Pan and Zoom
ROI
ROI
pan
ROI
zoom
(a)
(b)
(c)

## Slide 4: Non-Significant Tiles
non-significant tiles
Re-encoded with minimal bits
ROI
tiles
8K4K@60P at server
HD@60P to client
4K2K@60P to client
Decoder is not required to decode and display the pixels of non-significant tiles

## Slide 5: Purpose of Non-Significant Tiles
Provide a signal to the decoder that the decoder is not required to decode and store the pixels in the non-significant tile sets to reduce computation and memory usage.
The server may re-encode the non-significant tiles with a minimal number of bits to form a valid bitstream and to save transmission bandwidth while keeping the slice segment headers intact for decoding the regions of interest.

## Slide 6: Modification to Temporal MCTS
temporal_motion _constrained_tile_sets ( payloadSize ) { | Descriptor
mc_all_tiles_exact_sample_value_match_flag | u(1)
each_tile_one_tile_set_flag | u(1)
if (!each_tile_one_tile_set_flag) { | 
num_sets_in_message_minus1 | ue(v)
if(num_sets_in_message_minus1) | 
non_signficant_tile_set_present_flag | u(1)
numSignificantSets = num_sets_in_message_minus1– non_signficant_tile_set_present_flag +1 | 
for( i = 0; i <= numSignificantSets; i++) { | 
mcts_id[ i ] | ue(v)
num_tile_rects_in_set_minus1[ i | ue(v)
for( j = 0; j <= num_tile_rects_in_set_minus1[ i ]; j++) { | 
iop_left_tile_index[ i ][ j ] | ue(v)
bottom_right_tile_index[ i ][ j ] | ue(v)
} | 
if ( ! mc_all_tiles_exact_sample_value_match_flag ) | 
exact_sample_value_match_flag[ i ] | u(1)
} | 
} | 
} | 
non_significant_tile_set_present_flag equal to 1 specifies that the last tile set consists of those tiles that are not included in any earlier tile sets in the same message. The last tile sets are not required to provide decoded pixels. non_significant_tile_set_present_flag equal to 0 indicates that the last tile set may or may not consist of those tiles that are not included in any earlier tile sets in the same message.

## Slide 7: Conclusions
  Presented the signaling of non-significant tiles to support tiled streaming for reducing
    Channel bandwidth
    Decoder computation
    Decoder memory
Propose to be adopted to HEVC extension.