## Slide 1: AhG5 and AhG18: Bypass of the coefficient level flags for higher throughput JCTVC-O0208
Joel Sole, Rajan Joshi, Marta Karczewicz

## Slide 2: Introduction
High bit-depths and extended chroma formats impose increased demands on the throughput of the codec
  Large amount of context-coded and bypass bins to code for residual data
    Bypass bins allow easier parallelization (no context derivation and adaptation), especially if the binary code is regular
Rice parameter correlates well with the amount of data to be coded
  For common test conditions, Rice is equal to 4 for less than 1% of the sub-blocks
  For high bit-rate (AhG18), Rice is equal to 4 for more than 95% of the sub-blocks
Proposal: Bypass the coefficient level flags if the Rice parameter is above a threshold
  Reduction of the number of coded bins in average and in the worst-case

## Slide 3: Technical Description – Method 1
In HEVC, for each 4×4 sub-block, the Rice parameter is initialized to 0 and updated for each coefficient
Propose to use the Rice parameter at the end of previous sub-block to bypass the coefficient level flags
  If previousRiceGolomb=4, then coeff_abs_level_remaining encodes the absolute level of the coefficient minus 1
HEVC | Proposed Method 1
Loop to encode significance_coeff_flag Loop to encode coeff_abs_level_greater1_flag Loop to encode coeff_abs_level_greater2_flag Loop to encode coeff_sign_flag Loop to encode coeff_abs_level_remaining | Loop to encode significance_coeff_flag If ( previousRiceGolomb < 4 ) Loop to encode coeff_abs_level_greater1_flag Loop to encode coeff_abs_level_greater2_flag Loop to encode coeff_sign_flag Loop to encode coeff_abs_level_remaining

## Slide 4: Technical Description – Method 2
In RCE2 test D1, it is proposed to
  Initialize the Rice parameter to a value different from 0 depending on statistics
  Increase the maximum Rice parameter (which currently is 4)
On top of RCE2 test D1, method 1 is modified in two ways:
  Threshold on Rice parameter larger than 4
  Re-use of the initial Rice parameter derived by method RCE2 test D1 (instead of storing the parameter of the previous sub-block)
Proposed Method 2
Loop to encode significance_coeff_flag If ( initialRiceGolomb < 5 ) Loop to encode coeff_abs_level_greater1_flag Loop to encode coeff_abs_level_greater2_flag Loop to encode coeff_sign_flag Loop to encode coeff_abs_level_remaining
HEVCv1 behavior is achieved whenever Rice is equal or less than 4

## Slide 5: Results
BD-rates for
  Range Extensions common test conditions (CTC)
  AhG18 test conditions for high bit-depth (HBD)
Method 2 results also provided on top of RCE2 test D1 results
Bin count reduction

## Slide 6: Performance for CTC - method 1
 | All Intra HE Main-tier |  |  | All Intra HE High-tier |  |  | All Intra HE Super-High-tier |  | 
 | Y | U | V | Y | U | V | Y | U | V
RGB 4:4:4 | 0.0% | 0.0% | 0.0% | 0.0% | 0.1% | 0.1% | 0.1% | 0.1% | 0.1%
YCbCr 4:4:4 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.1% | 0.1%
YCbCr 4:2:2 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Overall | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.1% | 0.1% | 0.1%
 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.1% | 0.1% | 0.1%
Enc Time[%] | 105% |  |  | 105% |  |  | 106% |  | 
Dec Time[%] | 100% |  |  | 100% |  |  | 100% |  | 
 | Random Access HE Main-tier |  |  | Random Access HE High-tier |  |  |  |  | 
 | Y | U | V | Y | U | V |  |  | 
RGB 4:4:4 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% |  |  | 
YCbCr 4:4:4 | 0.0% | 0.0% | 0.0% | 0.0% | 0.1% | 0.0% |  |  | 
YCbCr 4:2:2 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% |  |  | 
Overall | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% |  |  | 
 | 0.0% | 0.0% | 0.0% | 0.0% | -0.1% | 0.0% |  |  | 
Enc Time[%] | 107% |  |  | 107% |  |  |  |  | 
Dec Time[%] | 98% |  |  | 98% |  |  |  |  | 
 | Low delay B HE Main-tier |  |  | Low delay B HE High-tier |  |  |  |  | 
 | Y | U | V | Y | U | V |  |  | 
RGB 4:4:4 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% |  |  | 
YCbCr 4:4:4 | 0.1% | 0.0% | -0.1% | 0.1% | 0.0% | 0.0% |  |  | 
YCbCr 4:2:2 | 0.0% | -0.1% | -0.1% | 0.0% | 0.0% | -0.1% |  |  | 
Overall | 0.0% | 0.0% | -0.1% | 0.0% | 0.0% | 0.0% |  |  | 
 | 0.0% | -0.1% | -0.1% | 0.0% | 0.0% | 0.0% |  |  | 
Enc Time[%] | 106% |  |  | 106% |  |  |  |  | 
Dec Time[%] | 101% |  |  | 101% |  |  |  |  | 

## Slide 7: Performance for CTC - method 2
 | All Intra HE Main-tier |  |  | All Intra HE High-tier |  |  | All Intra HE Super-High-tier |  | 
 | Y | U | V | Y | U | V | Y | U | V
RGB 4:4:4 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | -0.1% | -0.1%
YCbCr 4:4:4 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
YCbCr 4:2:2 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Overall | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Enc Time[%] | 106% |  |  | 105% |  |  | 106% |  | 
Dec Time[%] | 98% |  |  | 98% |  |  | 95% |  | 
 | Random Access HE Main-tier |  |  | Random Access HE High-tier |  |  |  |  | 
 | Y | U | V | Y | U | V |  |  | 
RGB 4:4:4 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% |  |  | 
YCbCr 4:4:4 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% |  |  | 
YCbCr 4:2:2 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% |  |  | 
Overall | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% |  |  | 
 | 0.0% | -0.1% | 0.0% | 0.0% | 0.0% | 0.0% |  |  | 
Enc Time[%] | 99% |  |  | 98% |  |  |  |  | 
Dec Time[%] | 99% |  |  | 99% |  |  |  |  | 
 | Low delay B HE Main-tier |  |  | Low delay B HE High-tier |  |  |  |  | 
 | Y | U | V | Y | U | V |  |  | 
RGB 4:4:4 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% |  |  | 
YCbCr 4:4:4 | 0.0% | 0.1% | 0.0% | 0.0% | 0.1% | 0.0% |  |  | 
YCbCr 4:2:2 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% |  |  | 
Overall | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% |  |  | 
 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% |  |  | 
Enc Time[%] | 107% |  |  | 106% |  |  |  |  | 
Dec Time[%] | 103% |  |  | 103% |  |  |  |  | 

## Slide 8: Performance for HBD
Method 1
Method 2
Method 2
(anchor RCE2 test D1)
 | All Intra |  | 
 | Y | U | V
12-bit | 0.6% | 0.7% | 0.7%
14-bit | 0.2% | 0.3% | 0.3%
16-bit | 0.0% | 0.0% | 0.0%
Enc Time[%] | 98% |  | 
Dec Time[%] | 94% |  | 
 | All Intra |  | 
 | Y | U | V
12-bit | 0.0% | 0.0% | 0.0%
14-bit | -0.1% | 0.0% | 0.0%
16-bit | -0.1% | -0.1% | -0.1%
Enc Time[%] | 105% |  | 
Dec Time[%] | 103% |  | 
 | All Intra |  | 
 | Y | U | V
12-bit | -7.1% | -6.8% | -6.8%
14-bit | -18.7% | -18.4% | -18.4%
16-bit | -28.7% | -28.5% | -28.6%
Enc Time[%] | 92% |  | 
Dec Time[%] | 89% |  | 

## Slide 9: Bin usage of method 1 with respect to anchor for HBD
Bin category | Bin usage (%)
All bins | 96.8%
Context-coded | 73.9%
Bypass | 101.3%
Greater than 1 | 5.2%
Greater than 2 | 5.2%
95% bin reduction for the coefficient level flags

## Slide 10: Conclusions
Method to increase throughput for high bit-depths by bypassing coefficient flags
  Two loops for residual coding are removed
  Decrease of the number of context-coded bins by 26%
No performance impact on CTC
No performance impact or even small gains for HBD when the maximum Rice parameter is larger than 4

## Slide 11: AhG5 and AhG18: Bypass of the coefficient level flags for higher throughput JCTVC-O0208
Joel Sole, Rajan Joshi, Marta Karczewicz