## Slide 1: JCTVC-O0232 On Intra block copying in RExt
Jun Xu, Ali Tabatabai, Ohji Nakagami
SONY

## Slide 2: Summary
Several modifications to Intra block copying (IntraBC) in RExt
  MV range restriction
  MV coding of IntraBC
  IntraBC and constrained_intra_pred_flag

## Slide 3: Point 1
Problem
  Implementation concerns on MV range
    Referring to upper CTU would be expensive for CTU based architecture.
  HM12.0+Rext-4.1 restricts MV range to only one CTU line.
Proposal
  Restrict vertical component within one CTU.
  Horizontal component needs further study.
    bvIntra[ 0 ] shall be in the range of –( 2 * CtbSizeY ) to (CtbSizeY – nCbS).
    bvIntra[ 1 ] shall be in the range of −(yTbCmp % CtbSizeY) to (CtbSizeY – nCbS).

## Slide 4: Point 2
Redundancy in MV coding for IntraBC
  Invalid range due to causality
  A referenced block cannot overlap with the target CU

## Slide 5: Point 2
Proposed solutions
  Condition on MVx, modify MVy
    Encoder: If abs(MVx)<W, Mvy+=H
    Decoder: If abs(MVx)<W, Mvy-=H
  Condition on MVy, modify MVx
    Encoder: If abs(MVy)<H, MVx+=W
    Decoder: If abs(MVy)<H, MVx-=W
  No condition check
    Encoder: MVx+=W
    Decoder: MVx-=W
|MVx| and |Mvy| cannot be both less than the size.
peak for MVx at negative range

## Slide 6: Point 2
Simulation results
  Anchor: RExt4.1 AHG8
  Test: Solution 1
 | All Intra HE Main-tier |  |  | All Intra HE High-tier |  |  | All Intra HE Super-High-tier |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class F | -0.1% | -0.1% | -0.1% | -0.1% | -0.1% | -0.1% | -0.1% | -0.1% | -0.1%
Class B | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
SC RGB 444 | -0.2% | -0.2% | -0.2% | -0.1% | -0.2% | -0.1% | -0.1% | -0.1% | -0.1%
Animation RGB 444 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
SC YUV 444 | -0.2% | -0.2% | -0.2% | -0.2% | -0.1% | 0.0% | -0.2% | -0.1% | 0.0%
Animation YUV 444 | 0.0% | 0.0% | -0.1% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
RangeExt | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
SC(444) GBR Optional | -0.5% | -0.5% | -0.6% | -0.5% | -0.5% | -0.5% | -0.5% | -0.4% | -0.4%
SC(444) YUV Optional | -0.6% | -0.6% | -0.6% | -0.4% | -0.5% | -0.5% | -0.4% | -0.4% | -0.4%
 | Random Access HE Main-tier |  |  | Random Access HE High-tier |  |  |  |  | 
 | Y | U | V | Y | U | V |  |  | 
Class F | -0.2% | -0.3% | -0.1% | -0.1% | -0.2% | -0.1% |  |  | 
Class B | 0.0% | 0.0% | 0.1% | 0.0% | 0.0% | 0.0% |  |  | 
SC RGB 444 | -0.1% | -0.1% | -0.1% | -0.1% | -0.1% | -0.1% |  |  | 
Animation RGB 444 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% |  |  | 
SC YUV 444 | -0.1% | -0.1% | 0.0% | 0.0% | -0.1% | 0.0% |  |  | 
Animation YUV 444 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% |  |  | 
RangeExt | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% |  |  | 
SC(444) GBR Optional | -0.5% | -0.6% | -0.6% | -0.5% | -0.4% | -0.5% |  |  | 
SC(444) YUV Optional | -0.9% | -0.8% | -0.9% | -0.5% | -0.5% | -0.6% |  |  | 
 | Low delay B HE Main-tier |  |  | Low delay B HE High-tier |  |  |  |  | 
 | Y | U | V | Y | U | V |  |  | 
Class F | -0.1% | -0.8% | -0.4% | 0.0% | -0.4% | -0.2% |  |  | 
Class B | 0.0% | -0.3% | -0.3% | 0.0% | -0.1% | -0.1% |  |  | 
SC RGB 444 | 0.3% | 0.1% | 0.2% | 0.2% | 0.1% | 0.1% |  |  | 
Animation RGB 444 | 0.0% | 0.0% | -0.1% | 0.0% | 0.0% | 0.0% |  |  | 
SC YUV 444 | -0.1% | -0.2% | -0.3% | -0.1% | -0.1% | -0.1% |  |  | 
Animation YUV 444 | 0.0% | -0.2% | 0.0% | 0.0% | -0.1% | 0.0% |  |  | 
RangeExt | 0.0% | 0.1% | 0.0% | 0.0% | 0.0% | -0.1% |  |  | 
SC(444) GBR Optional | 0.8% | 0.7% | 0.6% | 0.2% | 0.2% | 0.1% |  |  | 
SC(444) YUV Optional | -1.8% | -1.6% | -1.7% | -0.2% | 0.0% | -0.3% |  |  | 

## Slide 7: Point 2
Simulation results
  Anchor: RExt4.1 AHG8
  Test: Solution 2
 | All Intra HE Main-tier |  |  | All Intra HE High-tier |  |  | All Intra HE Super-High-tier |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class F | -0.4% | -0.4% | -0.4% | -0.3% | -0.3% | -0.3% | -0.2% | -0.3% | -0.3%
Class B | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
SC RGB 444 | -0.8% | -0.7% | -0.8% | -0.6% | -0.6% | -0.6% | -0.5% | -0.5% | -0.5%
Animation RGB 444 | -0.1% | -0.1% | -0.1% | -0.1% | -0.1% | -0.1% | 0.0% | 0.0% | 0.0%
SC YUV 444 | -1.1% | -1.1% | -1.1% | -0.9% | -0.9% | -0.8% | -0.7% | -0.6% | -0.6%
Animation YUV 444 | -0.1% | -0.1% | -0.1% | -0.1% | -0.1% | -0.1% | 0.0% | 0.0% | 0.0%
RangeExt | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
SC(444) GBR Optional | -1.1% | -1.1% | -1.1% | -0.9% | -1.0% | -0.9% | -0.8% | -0.8% | -0.8%
SC(444) YUV Optional | -1.6% | -1.6% | -1.5% | -1.3% | -1.3% | -1.3% | -1.0% | -1.1% | -1.0%
 | Random Access HE Main-tier |  |  | Random Access HE High-tier |  |  |  |  | 
 | Y | U | V | Y | U | V |  |  | 
Class F | -0.3% | -0.3% | -0.2% | -0.3% | -0.2% | -0.1% |  |  | 
Class B | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% |  |  | 
SC RGB 444 | -0.5% | -0.4% | -0.4% | -0.4% | -0.4% | -0.4% |  |  | 
Animation RGB 444 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% |  |  | 
SC YUV 444 | -0.9% | -0.8% | -0.9% | -0.8% | -0.7% | -0.7% |  |  | 
Animation YUV 444 | -0.1% | -0.1% | -0.1% | 0.0% | -0.1% | -0.1% |  |  | 
RangeExt | 0.0% | 0.0% | 0.1% | 0.0% | 0.0% | 0.0% |  |  | 
SC(444) GBR Optional | -1.0% | -0.9% | -1.0% | -0.8% | -0.7% | -0.7% |  |  | 
SC(444) YUV Optional | -2.0% | -1.8% | -1.9% | -1.8% | -1.6% | -1.6% |  |  | 
 | Low delay B HE Main-tier |  |  | Low delay B HE High-tier |  |  |  |  | 
 | Y | U | V | Y | U | V |  |  | 
Class F | -0.4% | -0.7% | -0.7% | -0.3% | -0.5% | -0.4% |  |  | 
Class B | 0.0% | -0.3% | -0.1% | 0.0% | -0.1% | 0.0% |  |  | 
SC RGB 444 | -0.6% | -0.3% | -0.4% | -0.1% | 0.2% | 0.0% |  |  | 
Animation RGB 444 | -0.1% | -0.2% | -0.1% | 0.0% | -0.1% | -0.1% |  |  | 
SC YUV 444 | -0.8% | -0.7% | -0.8% | -0.6% | -0.4% | -0.5% |  |  | 
Animation YUV 444 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | -0.1% |  |  | 
RangeExt | 0.0% | 0.0% | -0.1% | 0.0% | 0.0% | -0.2% |  |  | 
SC(444) GBR Optional | 0.3% | 0.3% | 0.4% | 0.2% | 0.7% | 0.7% |  |  | 
SC(444) YUV Optional | -2.0% | -1.6% | -1.9% | -1.5% | -1.0% | -1.2% |  |  | 

## Slide 8: Point 2
Simulation results
  Anchor: RExt4.1 AHG8
  Test: Solution 3
 | All Intra HE Main-tier |  |  | All Intra HE High-tier |  |  | All Intra HE Super-High-tier |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class F | -0.4% | -0.4% | -0.4% | -0.3% | -0.3% | -0.3% | -0.2% | -0.2% | -0.2%
Class B | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
SC RGB 444 | -0.5% | -0.5% | -0.5% | -0.4% | -0.4% | -0.4% | -0.3% | -0.3% | -0.3%
Animation RGB 444 | -0.1% | -0.1% | -0.1% | -0.1% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
SC YUV 444 | -0.7% | -0.6% | -0.7% | -0.6% | -0.5% | -0.5% | -0.5% | -0.4% | -0.4%
Animation YUV 444 | -0.1% | -0.1% | -0.1% | -0.1% | -0.1% | -0.1% | 0.0% | 0.0% | 0.0%
RangeExt | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
SC(444) GBR Optional | -0.2% | -0.3% | -0.2% | -0.2% | -0.2% | -0.1% | -0.2% | -0.1% | -0.1%
SC(444) YUV Optional | -0.6% | -0.6% | -0.5% | -0.4% | -0.5% | -0.4% | -0.2% | -0.4% | -0.3%
 | Random Access HE Main-tier |  |  | Random Access HE High-tier |  |  |  |  | 
 | Y | U | V | Y | U | V |  |  | 
Class F | -0.4% | -0.3% | -0.4% | -0.3% | -0.3% | -0.3% |  |  | 
Class B | 0.0% | -0.1% | 0.0% | 0.0% | -0.1% | 0.0% |  |  | 
SC RGB 444 | -0.2% | -0.2% | -0.2% | -0.2% | -0.1% | -0.1% |  |  | 
Animation RGB 444 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% |  |  | 
SC YUV 444 | -0.5% | -0.5% | -0.4% | -0.3% | -0.3% | -0.3% |  |  | 
Animation YUV 444 | 0.0% | -0.1% | 0.0% | 0.0% | -0.1% | -0.1% |  |  | 
RangeExt | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% |  |  | 
SC(444) GBR Optional | -0.1% | -0.1% | -0.1% | -0.2% | -0.1% | 0.0% |  |  | 
SC(444) YUV Optional | -0.9% | -0.6% | -0.9% | -0.7% | -0.4% | -0.6% |  |  | 
 | Low delay B HE Main-tier |  |  | Low delay B HE High-tier |  |  |  |  | 
 | Y | U | V | Y | U | V |  |  | 
Class F | -0.3% | -0.5% | -0.9% | -0.2% | -0.3% | -0.5% |  |  | 
Class B | 0.0% | 0.1% | -0.1% | 0.0% | 0.0% | 0.0% |  |  | 
SC RGB 444 | 0.2% | 0.6% | 0.4% | 0.2% | 0.7% | 0.5% |  |  | 
Animation RGB 444 | -0.1% | -0.1% | -0.1% | 0.0% | 0.0% | 0.0% |  |  | 
SC YUV 444 | -0.5% | -0.4% | -0.5% | -0.3% | -0.1% | -0.2% |  |  | 
Animation YUV 444 | 0.0% | 0.0% | 0.1% | -0.1% | -0.1% | 0.0% |  |  | 
RangeExt | 0.0% | 0.1% | -0.1% | 0.0% | 0.0% | -0.2% |  |  | 
SC(444) GBR Optional | 0.3% | 0.4% | 0.3% | 0.8% | 1.0% | 0.7% |  |  | 
SC(444) YUV Optional | -0.9% | -0.5% | -0.8% | -0.4% | 0.3% | -0.2% |  |  | 

## Slide 9: Point 3
Problem
  Constrained_intra_pred_flag serves for error resiliency purpose.
  IntraBC is treated as Intra in current RExt.
  Potential error propagation exists when IntraBC is used.

## Slide 10: Point 3
Solutions
  Apply to P/B slices.
  Encoder side solution
    Intra block copying motion vector shall not point where the reference pixels are derived from Intra block copying or Inter mode.
    Same as JCTVC-O0183 4.5 method 1
  Decoder side solution
    Reference pixels are unavailable if they are derived from Intra block copying or Inter mode.
    Same as JCTVC-O0155 method 2

## Slide 11: Conclusion
Clean-up and bug-fix for IntraBC in Rext
Recommend to adopt those modifications.
  MV range restriction
  MV coding of IntraBC
  IntraBC and constrained_intra_pred_flag