## Slide 1: Motion Compensation Interpolation with 16 Bit Intermediate Buffer for HEVC Range Extension JCTVC-O0233
Wei Pu, Jianle Chen, Woo-Shik Kim, Marta Karczewicz, Joel Sole, Liwei Guo

## Slide 2: Introduction
HEVC Motion Interpolation
  1-D horizontal interpolation to generated intermediate value for the following 1-D vertical interpolation
  16 bits intermediate value in HEVC main profile
  With 14/16 bits, intermediate values exceed 16 bits
    Increased storage and access cost for memory/cache
Proposed solution
  Intermediate values are kept with 16 bit
  No performance drop introduced

## Slide 3: In Current HEVC Range Extension
HEVC Luma Motion Interpolation
  a, b, c, d, h, n:
    8-Tap filtering, then (>> shift1)
      Intermediate value for 1-D vertical filtering
  e, f, g, I, j, k, p, q, r:
    8-Tap filtering, then (>>shift2).
Dynamic Range Analysis (16bit input as an example)
  Half Pel Filter: [-1, 4, -11, 40, 40, -11, 4, -1]
  Sum of positive: 88 (7 bit), Sum of negative: -24
  shift1 = Min(4, BitDepth − 8) = 4
  The largest intermediate value is at b0,0 (with all inputs being 216-1 = 65535)
    ((216 – 1) * 88) >> 4  19 bit
  Total bits for intermediate results is 20 bit
    19 bit + 1 sign bit as the value can be negative

## Slide 4
Dynamic Range Analysis (continue)
  Similarly, for 14 bit input, total bit to represent each output pixel is 18
  Table I. Summary of Interpolation Process’s Bit Depth
Increased memory/cache burden for 14/16 bits
Input bit | Bit Expansion | Sign bit | Shift1 | Output bit
12 | 7 | 1 | -4 | 16
14 | 7 | 1 | -4 | 18
16 | 7 | 1 | -4 | 20

## Slide 5: Proposed Method
16 Bit Intermediate Value
  1. Change shift1 from min(4, BitDepth-8) to max(4, BitDepth – 10)
    For 16 bit, shift1 changed from 4 to 6
  Result: Dynamic range reduced from 20 bits to 18 bits.
  2. Clip the value to [0, 65535]
  Result: Dynamic range reduced from 18 bits to 16 bits.
Similar operations are also applied to 14 bit input sequences
 | Input | Bit Expan. | Sign | Shift1 |  | Clip | Output
Current | 16 | 7 | 1 | -4 | 20 | NA | 20
Proposed | 16 | 7 | 1 | -6 | 18 | Yes | 16

## Slide 6: Performance (I)
Proposed v.s. HM Rext 4.1 High Precision Processing Enabled
Conclusion: No meaningful loss observed.

## Slide 7: Performance (I)
Proposed v.s. HM Rext 4.1 High Precision Processing (HEVCv1 Interpolation)
Conclusion: Meaningful gain observed.

## Slide 8: Conclusions
Restricting motion interpolation model’s intermediate data width within 16
Reduce cache and memory cost

## Slide 9: Motion Compensation Interpolation with 16 Bit Intermediate Buffer for HEVC Range Extension JCTVC-O0233
Wei Pu, Jianle Chen, Woo-Shik Kim, Marta Karczewicz, Joel Sole, Liwei Guo

## Slide 10: Backup: For Bi-Prediction
To ease SIMD, the current Implementation
  Step 1: pL0’[x][y] = pL0[x][y] – 8192 (pL0’[x][y] is at most 15bit)
  Step 2: pL1’[x][y] = pL1[x][y] – 8192 (pL1’[x][y] is at most 15bit)
  Step 3: Calculate pL[x][y] = pL0’[x][y] + pL1’[x][y];
  Step 4: Calculate pL’[x][y] = pL [x][y] + offset) >> shift;
  Step 5: Calculate p’[x][y] = Clip3(0, (1 << bitDepth) − 1, pL’[x][y]);
  Step 6: p [x][y] = 8192 + p’[x][y].
The proposed method
  If (shift == 1)
    p[x][y] = ROUND_AVER(pL0[x][y] + pL1[x][y])
  If (shift > 1)
  Step 1: p’[x][y] = AVER(pL0[x][y], pL1[x][y])
  Step 2: p[x][y] = ROUND_SHIFT(p’[x][y], shift - 1)

## Slide 11
Corresponding SIMD instructions in ARM ISA (NEON)
  ROUND_AVER: VHRAAD.U16
  AVER: VHAAD.U16
  ROUND_SHIFT: VRSHR.U16