## Slide 1: RCE2: Results of Test D1 on Rice Parameter Initialization (JCTVC-O0219)
Marta Karczewicz, Liwei Guo, Joel Sole, Rajan Joshi (Qualcomm)
Karl Sharman, Nick Saunders, James Gamei (Sony Europe)

## Slide 2: Introduction
Coefficient level coding in HEVC
  Rice parameter reset to 0 for each 4x4 CG and may increase with coding levels in the CG
  Screen content video or high bit-depth video tends to have large coefficients levels
    A higher starting point (rice parameter) is expected.
RCE2 Test D1 – Rice parameter initialization
  A combination of test RCE2 C1 (N0181) and C2 (N0189)
  Derive the initial rice parameter based on already encoded coefficients

## Slide 3: Method Description
Classification of sub-blocks - sbType
  Whether the sub-block is transform skip coded
  Whether the sub-block is luma block or chroma block
    controlled by a PPS flag useSeparateStatsFlag
Statistics collection
  Variable statCoeff set to 0 at the beginning of the slice
  Updated for the first coded remaining level in the sub-block
    if (uiLevel >=3*(1<<(statCoeff /4))) statCoeff ++;
    if ((2* uiLevel)<(1<<( statCoeff/4))) statCoeff --;
Rice parameter derivation
  For each 4×4 sub-block, the Rice parameter is initialized by
cRiceParam = statCoeff/4

## Slide 4: Simulation
Implemented on top of HM12.0-Rext 4.1
Tested under RCE2 common test conditions
  useSeparateStatsFlag = 0 for RGB and = 1 for YUV
Setting 1
  MAX_RICE_PARAM = 7 for AHG8 and = 16 for AHG18
Setting 2
  MAX_RICE_PARAM = MAX_TR_DYNAMIC_RANGE
  Remove the clipping in RiceParams update
    Before: uiGoRiceParam = min (uiGoRiceParam+1, MAX_RICE_PARAM);
    After: uiGoRiceParam ++;
Setting 3
  Same as Setting 2 except a RDOQ change
    Use derived initial Rice parameter instead of 0 in the RDOQ decision

## Slide 5: Setting 1 (1) –AHG8 Lossless
 | AI |  |  |  | RA |  |  |  | LD |  |  | 
 | Bit-rate saving (Total) | Bit-rate saving (Average) | Bit-rate saving (Min) | Bit-rate saving (Max) | Bit-rate saving (Total) | Bit-rate saving (Average) | Bit-rate saving (Min) | Bit-rate saving (Max) | Bit-rate saving (Total) | Bit-rate saving (Average) | Bit-rate saving (Min) | Bit-rate saving (Max)
Class F | 1.4% | 1.5% | 0.1% | 3.4% | 0.2% | 0.7% | 0.0% | 2.0% | 0.1% | 0.4% | 0.0% | 1.0%
Class B | 0.1% | 0.1% | 0.0% | 0.2% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
SC RGB 444 | 6.8% | 9.2% | 1.5% | 19.4% | 3.1% | 7.5% | 1.2% | 19.4% | 2.1% | 6.6% | 1.0% | 19.3%
Animation RGB 444 | 0.3% | 0.3% | 0.1% | 0.5% | 0.0% | 0.0% | 0.0% | 0.1% | 0.0% | 0.0% | 0.0% | 0.0%
SC YUV 444 | 4.2% | 5.6% | 0.7% | 13.5% | 1.7% | 4.5% | 0.5% | 13.5% | 1.1% | 4.1% | 0.5% | 13.3%
Animation YUV 444 | 0.4% | 0.3% | 0.1% | 0.7% | 0.2% | 0.1% | 0.0% | 0.4% | 0.2% | 0.1% | 0.0% | 0.3%
RangeExt | 3.8% | 3.6% | 1.2% | 5.7% | 2.8% | 2.7% | 0.3% | 5.0% | 2.8% | 2.7% | 0.3% | 5.0%
SC GBR 444 Optional | 18.8% | 21.2% | 13.0% | 26.7% | 12.4% | 20.7% | 11.2% | 27.3% | 11.4% | 21.1% | 10.9% | 27.4%
SC YUV 444 Optional | 15.4% | 15.7% | 12.4% | 18.1% | 11.8% | 15.2% | 10.7% | 18.6% | 10.9% | 14.5% | 10.5% | 19.6%
Enc Time[%] | 103% |  |  |  | 103% |  |  |  | 102% |  |  | 
Dec Time[%] | 98% |  |  |  | 101% |  |  |  | 99% |  |  | 

## Slide 6: Setting 1 (2) –AHG8 Lossy AI
 | All Intra HE Main-tier |  |  | All Intra HE High-tier |  |  | All Intra HE Super-High-tier |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class F | -0.5% | -0.6% | -0.6% | -0.9% | -0.9% | -0.9% | -1.3% | -1.3% | -1.3%
Class B | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
SC RGB 444 | -1.5% | -1.6% | -1.6% | -2.9% | -2.8% | -2.8% | -4.4% | -4.6% | -4.6%
Animation RGB 444 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
SC YUV 444 | -0.6% | -0.7% | -0.7% | -1.3% | -1.2% | -1.3% | -2.2% | -2.2% | -2.2%
Animation YUV 444 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
RangeExt | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
SC(444) GBR Optional | -6.0% | -5.8% | -5.7% | -9.5% | -9.2% | -9.6% | -13.0% | -13.6% | -13.7%
SC(444) YUV Optional | -1.7% | -1.9% | -1.8% | -3.7% | -3.6% | -3.4% | -6.4% | -6.4% | -6.9%
Enc Time[%] | 100% |  |  | 100% |  |  | 100% |  | 
Dec Time[%] | 100% |  |  | 100% |  |  | 100% |  | 

## Slide 7: Setting 1 (3) –AHG8 Lossy RA
 | Random Access HE Main-tier |  |  | Random Access HE High-tier |  | 
 | Y | U | V | Y | U | V
Class F | -0.3% | -0.4% | -0.4% | -0.6% | -0.6% | -0.6%
Class B | 0.0% | 0.0% | -0.1% | 0.0% | 0.0% | 0.0%
SC RGB 444 | -1.3% | -1.3% | -1.3% | -2.4% | -2.4% | -2.4%
Animation RGB 444 | -0.1% | -0.1% | 0.0% | 0.0% | 0.0% | 0.0%
SC YUV 444 | -0.6% | -0.7% | -0.7% | -1.0% | -1.0% | -1.1%
Animation YUV 444 | 0.0% | 0.0% | -0.1% | 0.0% | -0.1% | -0.1%
RangeExt | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
SC(444) GBR Optional | -5.7% | -5.5% | -5.3% | -9.0% | -8.9% | -9.2%
SC(444) YUV Optional | -1.7% | -1.8% | -1.8% | -3.3% | -3.2% | -3.2%
Enc Time[%] | 100% |  |  | 100% |  | 
Dec Time[%] | 100% |  |  | 100% |  | 

## Slide 8: Setting 1 (4) –AHG8 Lossy LD
 | Low delay B HE Main-tier |  |  | Low delay B HE High-tier |  | 
 | Y | U | V | Y | U | V
Class F | -0.1% | -0.1% | -0.3% | -0.3% | -0.5% | -0.5%
Class B | 0.0% | 0.1% | -0.1% | 0.0% | 0.0% | 0.0%
SC RGB 444 | -0.7% | -0.8% | -0.7% | -1.5% | -1.5% | -1.5%
Animation RGB 444 | -0.1% | -0.1% | -0.1% | 0.0% | -0.1% | 0.0%
SC YUV 444 | -0.7% | -0.8% | -0.9% | -1.0% | -0.9% | -1.1%
Animation YUV 444 | 0.0% | 0.0% | 0.1% | 0.0% | 0.0% | 0.0%
RangeExt | 0.0% | 0.0% | -0.2% | 0.0% | 0.0% | -0.2%
SC(444) GBR Optional | -5.6% | -5.8% | -5.4% | -9.1% | -9.4% | -9.6%
SC(444) YUV Optional | -1.8% | -1.7% | -1.7% | -2.6% | -2.6% | -2.8%
Enc Time[%] | 100% |  |  | 100% |  | 
Dec Time[%] | 100% |  |  | 100% |  | 

## Slide 9: Setting 1 (5) –AHG18 High bit depth
With HM forward transform
With High precision forward transform
 | All Intra |  | 
 | Y | U | V
12-bit | -7.1% | -6.8% | -6.8%
14-bit | -18.7% | -18.4% | -18.3%
16-bit | -28.6% | -28.5% | -28.5%
Enc Time[%] | 86% |  | 
Dec Time[%] | 84% |  | 
 | All Intra |  | 
 | Y | U | V
12-bit | -6.9% | -7.1% | -7.1%
14-bit | -18.2% | -18.1% | -18.1%
16-bit | -27.9% | -27.7% | -27.7%
Enc Time[%] | 85% |  | 
Dec Time[%] | 84% |  | 

## Slide 10: Setting 2 (1) –AHG8 Lossless
 | AI |  |  |  | RA |  |  |  | LD |  |  | 
 | Bit-rate saving (Total) | Bit-rate saving (Average) | Bit-rate saving (Min) | Bit-rate saving (Max) | Bit-rate saving (Total) | Bit-rate saving (Average) | Bit-rate saving (Min) | Bit-rate saving (Max) | Bit-rate saving (Total) | Bit-rate saving (Average) | Bit-rate saving (Min) | Bit-rate saving (Max)
Class F | 1.4% | 1.5% | 0.1% | 3.4% | 0.2% | 0.7% | 0.0% | 2.0% | 0.1% | 0.4% | 0.0% | 1.0%
Class B | 0.1% | 0.1% | 0.0% | 0.2% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
SC RGB 444 | 6.8% | 9.2% | 1.5% | 19.4% | 3.1% | 7.5% | 1.2% | 19.4% | 2.1% | 6.6% | 1.0% | 19.3%
Animation RGB 444 | 0.3% | 0.3% | 0.1% | 0.5% | 0.0% | 0.0% | 0.0% | 0.1% | 0.0% | 0.0% | 0.0% | 0.0%
SC YUV 444 | 4.2% | 5.6% | 0.7% | 13.5% | 1.7% | 4.5% | 0.5% | 13.5% | 1.1% | 4.1% | 0.5% | 13.3%
Animation YUV 444 | 0.4% | 0.3% | 0.1% | 0.7% | 0.2% | 0.1% | 0.0% | 0.4% | 0.2% | 0.1% | 0.0% | 0.3%
RangeExt | 3.8% | 3.6% | 1.2% | 5.7% | 2.8% | 2.7% | 0.3% | 5.0% | 2.8% | 2.7% | 0.3% | 5.0%
SC GBR 444 Optional | 18.8% | 21.2% | 13.0% | 26.7% | 12.4% | 20.7% | 11.2% | 27.3% | 11.4% | 21.1% | 10.9% | 27.4%
SC YUV 444 Optional | 15.4% | 15.7% | 12.4% | 18.1% | 11.8% | 15.2% | 10.7% | 18.6% | 10.9% | 14.5% | 10.5% | 19.6%
Enc Time[%] | 100% |  |  |  | 99% |  |  |  | 96% |  |  | 
Dec Time[%] | 98% |  |  |  | 99% |  |  |  | 98% |  |  | 

## Slide 11: Setting 2 (2) –AHG8 Lossy AI
 | All Intra HE Main-tier |  |  | All Intra HE High-tier |  |  | All Intra HE Super-High-tier |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class F | -0.5% | -0.6% | -0.6% | -0.9% | -0.9% | -0.9% | -1.3% | -1.3% | -1.3%
Class B | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
SC RGB 444 | -1.5% | -1.6% | -1.6% | -2.9% | -2.8% | -2.8% | -4.4% | -4.6% | -4.6%
Animation RGB 444 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
SC YUV 444 | -0.6% | -0.7% | -0.7% | -1.3% | -1.2% | -1.3% | -2.2% | -2.2% | -2.2%
Animation YUV 444 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
RangeExt | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
SC(444) GBR Optional | -6.0% | -5.8% | -5.7% | -9.5% | -9.2% | -9.6% | -12.9% | -13.6% | -13.7%
SC(444) YUV Optional | -1.7% | -1.9% | -1.8% | -3.7% | -3.6% | -3.4% | -6.4% | -6.4% | -6.9%
Enc Time[%] | 99% |  |  | 99% |  |  | 98% |  | 
Dec Time[%] | 100% |  |  | 100% |  |  | 100% |  | 

## Slide 12: Setting 2 (3) –AHG8 Lossy RA
 | Random Access HE Main-tier |  |  | Random Access HE High-tier |  | 
 | Y | U | V | Y | U | V
Class F | -0.3% | -0.4% | -0.4% | -0.6% | -0.6% | -0.6%
Class B | 0.0% | 0.0% | -0.1% | 0.0% | 0.0% | 0.0%
SC RGB 444 | -1.3% | -1.3% | -1.3% | -2.4% | -2.4% | -2.4%
Animation RGB 444 | -0.1% | -0.1% | 0.0% | 0.0% | 0.0% | 0.0%
SC YUV 444 | -0.6% | -0.7% | -0.7% | -1.0% | -1.0% | -1.1%
Animation YUV 444 | 0.0% | 0.0% | -0.1% | 0.0% | -0.1% | -0.1%
RangeExt | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
SC(444) GBR Optional | -5.7% | -5.5% | -5.3% | -9.0% | -8.9% | -9.2%
SC(444) YUV Optional | -1.7% | -1.8% | -1.8% | -3.3% | -3.2% | -3.2%
Enc Time[%] | 101% |  |  | 101% |  | 
Dec Time[%] | 99% |  |  | 99% |  | 

## Slide 13: Setting 2 (4) –AHG8 Lossy LD
 | Low delay B HE Main-tier |  |  | Low delay B HE High-tier |  | 
 | Y | U | V | Y | U | V
Class F | -0.1% | -0.1% | -0.3% | -0.3% | -0.5% | -0.5%
Class B | 0.0% | 0.1% | -0.1% | 0.0% | 0.0% | 0.0%
SC RGB 444 | -0.7% | -0.8% | -0.7% | -1.5% | -1.5% | -1.5%
Animation RGB 444 | -0.1% | -0.1% | -0.1% | 0.0% | -0.1% | 0.0%
SC YUV 444 | -0.7% | -0.8% | -0.9% | -1.0% | -0.9% | -1.1%
Animation YUV 444 | 0.0% | 0.0% | 0.1% | 0.0% | 0.0% | 0.0%
RangeExt | 0.0% | 0.0% | -0.2% | 0.0% | 0.0% | -0.2%
SC(444) GBR Optional | -5.6% | -5.8% | -5.4% | -9.1% | -9.4% | -9.6%
SC(444) YUV Optional | -1.8% | -1.7% | -1.7% | -2.6% | -2.6% | -2.8%
Enc Time[%] | 101% |  |  | 101% |  | 
Dec Time[%] | 100% |  |  | 100% |  | 

## Slide 14: Setting 2 (5) –AHG18 High bit depth
With HM forward transform
With High precision forward transform
 | All Intra |  | 
 | Y | U | V
12-bit | -7.1% | -6.8% | -6.8%
14-bit | -18.7% | -18.4% | -18.3%
16-bit | -28.6% | -28.5% | -28.5%
Enc Time[%] | 88% |  | 
Dec Time[%] | 92% |  | 
 | All Intra |  | 
 | Y | U | V
12-bit | -6.9% | -7.1% | -7.1%
14-bit | -18.2% | -18.1% | -18.1%
16-bit | -27.9% | -27.7% | -27.7%
Enc Time[%] | 92% |  | 
Dec Time[%] | 90% |  | 

## Slide 15: Setting 3 (1) –AHG8 Lossless
 | AI |  |  |  | RA |  |  |  | LD |  |  | 
 | Bit-rate saving (Total) | Bit-rate saving (Average) | Bit-rate saving (Min) | Bit-rate saving (Max) | Bit-rate saving (Total) | Bit-rate saving (Average) | Bit-rate saving (Min) | Bit-rate saving (Max) | Bit-rate saving (Total) | Bit-rate saving (Average) | Bit-rate saving (Min) | Bit-rate saving (Max)
Class F | 1.4% | 1.5% | 0.1% | 3.4% | 0.2% | 0.7% | 0.0% | 2.0% | 0.1% | 0.4% | 0.0% | 1.0%
Class B | 0.1% | 0.1% | 0.0% | 0.2% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
SC RGB 444 | 6.8% | 9.2% | 1.5% | 19.4% | 3.1% | 7.5% | 1.2% | 19.4% | 2.1% | 6.6% | 1.0% | 19.3%
Animation RGB 444 | 0.3% | 0.3% | 0.1% | 0.5% | 0.0% | 0.0% | 0.0% | 0.1% | 0.0% | 0.0% | 0.0% | 0.0%
SC YUV 444 | 4.2% | 5.6% | 0.7% | 13.5% | 1.7% | 4.5% | 0.5% | 13.5% | 1.1% | 4.1% | 0.5% | 13.3%
Animation YUV 444 | 0.4% | 0.3% | 0.1% | 0.7% | 0.2% | 0.1% | 0.0% | 0.4% | 0.2% | 0.1% | 0.0% | 0.3%
RangeExt | 3.8% | 3.6% | 1.2% | 5.7% | 2.8% | 2.7% | 0.3% | 5.0% | 2.8% | 2.7% | 0.3% | 5.0%
SC GBR 444 Optional | 18.8% | 21.2% | 13.0% | 26.7% | 12.4% | 20.7% | 11.2% | 27.3% | 11.4% | 21.1% | 10.9% | 27.4%
SC YUV 444 Optional | 15.4% | 15.7% | 12.4% | 18.1% | 11.8% | 15.2% | 10.7% | 18.6% | 10.9% | 14.5% | 10.5% | 19.6%
Enc Time[%] | 100% |  |  |  | 99% |  |  |  | 96% |  |  | 
Dec Time[%] | 98% |  |  |  | 98% |  |  |  | 99% |  |  | 

## Slide 16: Setting 3 (2) –AHG8 Lossy AI
 | All Intra HE Main-tier |  |  | All Intra HE High-tier |  |  | All Intra HE Super-High-tier |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class F | -0.5% | -0.6% | -0.6% | -0.9% | -1.0% | -1.0% | -1.3% | -1.4% | -1.4%
Class B | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
SC RGB 444 | -1.6% | -1.6% | -1.6% | -3.0% | -2.8% | -2.9% | -4.4% | -4.6% | -4.6%
Animation RGB 444 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
SC YUV 444 | -0.6% | -0.6% | -0.7% | -1.3% | -1.2% | -1.3% | -2.2% | -2.3% | -2.2%
Animation YUV 444 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
RangeExt | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
SC(444) GBR Optional | -6.1% | -5.8% | -5.7% | -9.5% | -9.2% | -9.6% | -13.0% | -13.6% | -13.7%
SC(444) YUV Optional | -1.8% | -1.9% | -1.8% | -3.8% | -3.6% | -3.5% | -6.5% | -6.4% | -7.0%
Enc Time[%] | 100% |  |  | 100% |  |  | 100% |  | 
Dec Time[%] | 99% |  |  | 100% |  |  | 100% |  | 

## Slide 17: Setting 3 (3) –AHG8 Lossy RA
 | Random Access HE Main-tier |  |  | Random Access HE High-tier |  | 
 | Y | U | V | Y | U | V
Class F | -0.3% | -0.4% | -0.4% | -0.6% | -0.6% | -0.6%
Class B | 0.0% | 0.0% | -0.1% | 0.0% | 0.0% | -0.1%
SC RGB 444 | -1.4% | -1.4% | -1.4% | -2.5% | -2.4% | -2.4%
Animation RGB 444 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
SC YUV 444 | -0.6% | -0.6% | -0.7% | -1.0% | -1.0% | -1.1%
Animation YUV 444 | 0.0% | 0.0% | -0.1% | 0.0% | -0.1% | 0.0%
RangeExt | 0.0% | 0.0% | -0.1% | 0.0% | 0.0% | -0.1%
SC(444) GBR Optional | -5.8% | -5.6% | -5.4% | -9.2% | -9.0% | -9.3%
SC(444) YUV Optional | -1.9% | -1.9% | -1.8% | -3.6% | -3.5% | -3.3%
Enc Time[%] | 100% |  |  | 100% |  | 
Dec Time[%] | 99% |  |  | 99% |  | 

## Slide 18: Setting 3 (4) –AHG8 Lossy LD
 | Low delay B HE Main-tier |  |  | Low delay B HE High-tier |  | 
 | Y | U | V | Y | U | V
Class F | -0.2% | -0.3% | -0.4% | -0.3% | -0.3% | -0.5%
Class B | 0.0% | 0.1% | -0.1% | 0.0% | 0.1% | 0.1%
SC RGB 444 | -1.0% | -1.1% | -1.1% | -2.0% | -2.0% | -2.0%
Animation RGB 444 | 0.0% | 0.0% | -0.1% | 0.0% | 0.0% | 0.0%
SC YUV 444 | -0.2% | -0.2% | -0.1% | -0.5% | -0.4% | -0.4%
Animation YUV 444 | 0.0% | 0.0% | 0.1% | 0.0% | 0.0% | 0.0%
RangeExt | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
SC(444) GBR Optional | -5.3% | -5.3% | -5.2% | -9.2% | -9.3% | -9.7%
SC(444) YUV Optional | -2.1% | -2.1% | -2.0% | -3.3% | -3.2% | -3.3%
Enc Time[%] | 100% |  |  | 100% |  | 
Dec Time[%] | 100% |  |  | 100% |  | 

## Slide 19: Setting 3 (5) –AHG18 High bit depth
With HM forward transform
With High precision forward transform
 | All Intra |  | 
 | Y | U | V
12-bit | -7.2% | -6.8% | -6.9%
14-bit | -18.7% | -18.4% | -18.3%
16-bit | -28.6% | -28.5% | -28.5%
Enc Time[%] | 94% |  | 
Dec Time[%] | 88% |  | 
 | All Intra |  | 
 | Y | U | V
12-bit | -7.0% | -7.1% | -7.1%
14-bit | -18.2% | -18.1% | -18.1%
16-bit | -27.9% | -27.7% | -27.7%
Enc Time[%] | 91% |  | 
Dec Time[%] | 88% |  | 

## Slide 20: Conclusions:
Rice parameter initialization method is presented
  The statistics is collected at most once per sub-block
  The initial rice parameter is derived from the statistics (of the same sbType) using a linear function (>>2)
The method tested with different settings
  Provide good gain for screen content, animation and high-bit depth video

## Slide 21: Setting 1: AHG8 Lossless MAX Rice Parameter = 4
 | AI |  |  |  | RA |  |  |  | LD |  |  | 
 | Bit-rate saving (Total) | Bit-rate saving (Average) | Bit-rate saving (Min) | Bit-rate saving (Max) | Bit-rate saving (Total) | Bit-rate saving (Average) | Bit-rate saving (Min) | Bit-rate saving (Max) | Bit-rate saving (Total) | Bit-rate saving (Average) | Bit-rate saving (Min) | Bit-rate saving (Max)
Class F | 1.2% | 1.3% | 0.1% | 2.8% | 0.2% | 0.7% | 0.0% | 1.8% | 0.1% | 0.4% | 0.0% | 0.9%
Class B | 0.1% | 0.1% | 0.0% | 0.2% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
SC RGB 444 | 5.1% | 6.4% | 1.4% | 11.4% | 2.4% | 5.1% | 1.1% | 11.4% | 1.9% | 4.7% | 0.9% | 11.1%
Animation RGB 444 | 0.3% | 0.3% | 0.1% | 0.5% | 0.0% | 0.0% | 0.0% | 0.1% | 0.0% | 0.0% | 0.0% | 0.0%
SC YUV 444 | 3.6% | 4.8% | 0.7% | 10.8% | 1.7% | 4.0% | 0.6% | 10.7% | 1.0% | 3.5% | 0.5% | 10.6%
Animation YUV 444 | 0.3% | 0.3% | 0.1% | 0.6% | 0.2% | 0.1% | 0.0% | 0.4% | 0.2% | 0.1% | 0.0% | 0.3%
RangeExt | 3.3% | 3.1% | 1.0% | 4.8% | 2.6% | 2.5% | 0.3% | 4.2% | 2.6% | 2.5% | 0.3% | 4.2%
SC GBR 444 Optional | 10.6% | 11.4% | 8.5% | 13.6% | 7.9% | 10.8% | 7.4% | 13.4% | 7.5% | 9.9% | 7.3% | 11.7%
SC YUV 444 Optional | 11.8% | 12.0% | 9.0% | 13.9% | 8.2% | 11.5% | 7.1% | 14.5% | 7.3% | 10.5% | 7.0% | 15.5%
Enc Time[%] | 100% |  |  |  | 95% |  |  |  | 96% |  |  | 
Dec Time[%] | 101% |  |  |  | 100% |  |  |  | 99% |  |  | 

## Slide 22: Setting 1–AHG8 Lossy AI MAX Rice Parameter = 4
 | All Intra HE Main-tier |  |  | All Intra HE High-tier |  |  | All Intra HE Super-High-tier |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class F | -0.5% | -0.6% | -0.6% | -0.9% | -0.9% | -0.9% | -1.3% | -1.3% | -1.3%
Class B | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
SC RGB 444 | -1.5% | -1.6% | -1.6% | -2.9% | -2.8% | -2.8% | -4.3% | -4.5% | -4.4%
Animation RGB 444 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
SC YUV 444 | -0.6% | -0.7% | -0.7% | -1.3% | -1.2% | -1.3% | -2.1% | -2.2% | -2.2%
Animation YUV 444 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
RangeExt | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
SC(444) GBR Optional | -6.0% | -5.8% | -5.7% | -9.4% | -9.1% | -9.5% | -12.0% | -12.1% | -12.1%
SC(444) YUV Optional | -1.7% | -1.9% | -1.8% | -3.7% | -3.6% | -3.4% | -6.4% | -6.3% | -6.8%
Enc Time[%] | 96% |  |  | 96% |  |  | 96% |  | 
Dec Time[%] | 100% |  |  | 100% |  |  | 100% |  | 

## Slide 23: Setting 1 –AHG8 Lossy RA MAX Rice Parameter = 4
 | Random Access HE Main-tier |  |  | Random Access HE High-tier |  | 
 | Y | U | V | Y | U | V
Class F | -0.3% | -0.4% | -0.4% | -0.6% | -0.6% | -0.6%
Class B | 0.0% | 0.0% | -0.1% | 0.0% | 0.1% | 0.0%
SC RGB 444 | -1.3% | -1.3% | -1.3% | -2.4% | -2.4% | -2.4%
Animation RGB 444 | 0.0% | -0.1% | 0.0% | 0.0% | 0.0% | 0.0%
SC YUV 444 | -0.6% | -0.7% | -0.7% | -1.0% | -1.0% | -1.1%
Animation YUV 444 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
RangeExt | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
SC(444) GBR Optional | -5.7% | -5.5% | -5.3% | -8.9% | -8.8% | -9.1%
SC(444) YUV Optional | -1.7% | -1.8% | -1.8% | -3.3% | -3.2% | -3.2%
Enc Time[%] | 96% |  |  | 96% |  | 
Dec Time[%] | 100% |  |  | 100% |  | 

## Slide 24: Setting 1 –AHG8 Lossy LD MAX Rice Parameter = 4
 | Low delay B HE Main-tier |  |  | Low delay B HE High-tier |  | 
 | Y | U | V | Y | U | V
Class F | -0.1% | -0.1% | -0.3% | -0.3% | -0.5% | -0.5%
Class B | 0.0% | 0.1% | -0.1% | 0.0% | 0.0% | 0.0%
SC RGB 444 | -0.6% | -0.7% | -0.7% | -1.4% | -1.4% | -1.4%
Animation RGB 444 | 0.0% | -0.1% | -0.1% | 0.0% | 0.0% | 0.0%
SC YUV 444 | -0.8% | -0.8% | -0.9% | -1.0% | -0.8% | -1.0%
Animation YUV 444 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
RangeExt | 0.0% | 0.0% | -0.2% | 0.0% | 0.0% | -0.2%
SC(444) GBR Optional | -5.8% | -5.8% | -5.5% | -9.5% | -9.7% | -10.0%
SC(444) YUV Optional | -1.8% | -1.7% | -1.7% | -2.7% | -2.5% | -2.6%
Enc Time[%] | 96% |  |  | 96% |  | 
Dec Time[%] | 100% |  |  | 100% |  | 

## Slide 25: Setting 1 (1) –AHG8 Lossless, useSeparateStatsFlag = 1
 | AI |  |  |  | RA |  |  |  | LD |  |  | 
 | Bit-rate saving (Total) | Bit-rate saving (Average) | Bit-rate saving (Min) | Bit-rate saving (Max) | Bit-rate saving (Total) | Bit-rate saving (Average) | Bit-rate saving (Min) | Bit-rate saving (Max) | Bit-rate saving (Total) | Bit-rate saving (Average) | Bit-rate saving (Min) | Bit-rate saving (Max)
Class F | 1.4% | 1.5% | 0.1% | 3.4% | 0.2% | 0.7% | 0.0% | 2.0% | 0.1% | 0.4% | 0.0% | 1.0%
Class B | 0.1% | 0.1% | 0.0% | 0.2% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
SC RGB 444 | 6.6% | 9.0% | 1.4% | 19.1% | 3.0% | 7.2% | 1.0% | 19.0% | 2.0% | 6.5% | 0.9% | 18.9%
Animation RGB 444 | 0.3% | 0.2% | 0.1% | 0.5% | 0.0% | 0.0% | 0.0% | 0.1% | 0.0% | 0.0% | 0.0% | 0.0%
SC YUV 444 | 4.2% | 5.6% | 0.7% | 13.5% | 1.7% | 4.5% | 0.5% | 13.5% | 1.1% | 4.1% | 0.5% | 13.3%
Animation YUV 444 | 0.4% | 0.3% | 0.1% | 0.7% | 0.2% | 0.1% | 0.0% | 0.4% | 0.2% | 0.1% | 0.0% | 0.3%
RangeExt | 3.8% | 3.6% | 1.2% | 5.7% | 2.8% | 2.7% | 0.3% | 5.0% | 2.8% | 2.7% | 0.3% | 5.0%
SC GBR 444 Optional | 18.6% | 21.1% | 12.7% | 26.7% | 12.1% | 20.5% | 10.9% | 27.2% | 11.1% | 20.8% | 10.6% | 27.1%
SC YUV 444 Optional | 15.4% | 15.7% | 12.4% | 18.1% | 11.8% | 15.2% | 10.7% | 18.6% | 10.9% | 14.5% | 10.5% | 19.6%
Enc Time[%] | 103% |  |  |  | 102% |  |  |  | 104% |  |  | 
Dec Time[%] | 98% |  |  |  | 101% |  |  |  | 99% |  |  | 

## Slide 26: Setting 1 (2) –AHG8 Lossy AI, useSeparateStatsFlag = 1
 | All Intra HE Main-tier |  |  | All Intra HE High-tier |  |  | All Intra HE Super-High-tier |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class F | -0.5% | -0.6% | -0.6% | -0.9% | -0.9% | -0.9% | -1.3% | -1.3% | -1.3%
Class B | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
SC RGB 444 | -1.5% | -1.5% | -1.5% | -2.8% | -2.7% | -2.7% | -4.3% | -4.5% | -4.5%
Animation RGB 444 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
SC YUV 444 | -0.6% | -0.7% | -0.7% | -1.3% | -1.2% | -1.3% | -2.2% | -2.2% | -2.2%
Animation YUV 444 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
RangeExt | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
SC(444) GBR Optional | -6.0% | -5.8% | -5.7% | -9.4% | -9.2% | -9.5% | -12.8% | -13.5% | -13.6%
SC(444) YUV Optional | -1.7% | -1.9% | -1.8% | -3.7% | -3.6% | -3.4% | -6.4% | -6.4% | -6.9%
Enc Time[%] | 99% |  |  | 100% |  |  | 100% |  | 
Dec Time[%] | 100% |  |  | 100% |  |  | 100% |  | 

## Slide 27: Setting 1 (3) –AHG8 Lossy RA, useSeparateStatsFlag = 1
 | Random Access HE Main-tier |  |  | Random Access HE High-tier |  | 
 | Y | U | V | Y | U | V
Class F | -0.3% | -0.4% | -0.4% | -0.6% | -0.6% | -0.6%
Class B | 0.0% | 0.0% | -0.1% | 0.0% | 0.0% | 0.0%
SC RGB 444 | -1.2% | -1.3% | -1.3% | -2.3% | -2.3% | -2.3%
Animation RGB 444 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
SC YUV 444 | -0.6% | -0.7% | -0.7% | -1.0% | -1.0% | -1.1%
Animation YUV 444 | 0.0% | 0.0% | -0.1% | 0.0% | -0.1% | -0.1%
RangeExt | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
SC(444) GBR Optional | -5.6% | -5.4% | -5.3% | -8.9% | -8.7% | -9.1%
SC(444) YUV Optional | -1.7% | -1.8% | -1.8% | -3.3% | -3.2% | -3.2%
Enc Time[%] | 100% |  |  | 100% |  | 
Dec Time[%] | 100% |  |  | 100% |  | 

## Slide 28: Setting 1 (4) –AHG8 Lossy LD, useSeparateStatsFlag = 1
 | Low delay B HE Main-tier |  |  | Low delay B HE High-tier |  | 
 | Y | U | V | Y | U | V
Class F | -0.1% | -0.1% | -0.3% | -0.3% | -0.5% | -0.5%
Class B | 0.0% | 0.1% | -0.1% | 0.0% | 0.0% | 0.0%
SC RGB 444 | -0.7% | -0.8% | -0.9% | -1.7% | -1.7% | -1.8%
Animation RGB 444 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
SC YUV 444 | -0.7% | -0.8% | -0.9% | -1.0% | -0.9% | -1.1%
Animation YUV 444 | 0.0% | 0.0% | 0.1% | 0.0% | 0.0% | 0.0%
RangeExt | 0.0% | 0.0% | -0.2% | 0.0% | 0.0% | -0.2%
SC(444) GBR Optional | -5.3% | -5.3% | -5.0% | -9.0% | -9.0% | -9.4%
SC(444) YUV Optional | -1.8% | -1.7% | -1.7% | -2.6% | -2.6% | -2.8%
Enc Time[%] | 100% |  |  | 99% |  | 
Dec Time[%] | 100% |  |  | 100% |  | 

## Slide 29: Setting 1 (5) –AHG18 High bit depth, useSeparateStatsFlag = 1
With HM forward transform
With High precision forward transform
 | All Intra |  | 
 | Y | U | V
12-bit | -7.2% | -6.9% | -6.8%
14-bit | -18.7% | -18.5% | -18.4%
16-bit | -28.7% | -28.5% | -28.6%
Enc Time[%] | 95% |  | 
Dec Time[%] | 84% |  | 
 | All Intra |  | 
 | Y | U | V
12-bit | -7.0% | -7.1% | -7.1%
14-bit | -18.2% | -18.1% | -18.1%
16-bit | -27.9% | -27.7% | -27.7%
Enc Time[%] | 87% |  | 
Dec Time[%] | 83% |  | 

## Slide 30
Thank you!
Thanks to Canon (JCTVC-O0257) and Samsung (JCTVC-O0283)for cross-checking!