## Slide 1: JCTVC-O0254 / JCT3V-F0084: MV-HEVC/SHVC HLS: On Inter layer Prediction Signaling
Hendry, Y. Chen, Y.K. Wang

## Slide 2: Overview
This contribution is follow-up of JCTVC-N0118
  Additional study
  Bit-count data provided
List of inter-layer prediction reference layer set (ILP-RPS) currently only signalled in Slice Header
  all_ref_layers_active_flag and max_one_active_ref_layer_flag help to avoid always signalling the ILP-RSP for common cases.
  But, other than common cases, if will be more efficient if we can avoid always signalling ILP-RPS in SH.
Proposal:
  Signal a list of candidate ILP-RPS for each layer in VPS
  These candidate ILP-RPS can be referred by index from SH

## Slide 3: Signalling Concept
In VPS, a set of candidates ILP-RPS for each layer may be signaled in VPS
  When all_ref_layers_active_flag is not equal to 1
  When the number of direct dependent layers is greater than 1.
In slice header, two new syntax elements
  ilp_ref_pic_set_vps_flag indicates whether ILP-RPS is present in the slice header or ILP-RPS refers to one of the candidate ILP-RPS
  When ilp_ref_pics_set_vps_flag is equal to 1, ilp_ref_pic_set_idx specifies the index of the candidate ILP-RPS used for the slice.
  These two flags are not present when the number of direct dependent layers for the current layer is smaller than 2.

## Slide 4: Proposed Syntaxes
vps_extension( ) { | Descriptor
... | 
all_ref_layers_active_flag | u(1)
max_one_active_ref_layer_flag | u(1)
if (!all_ref_layers_active_flag) | 
for( i =1; i <= vps_max_layers_minus1; i++) | 
if( NumDirectRefLayers[ layer_id_in_nuh[ i ] ] > 1 ) { | 
num_ilp_ref_pic_sets[ i ] | ue(v)
for( j = 1; j < num_ilp_ref_pic_sets[ i ]; j++) | 
ilp_ref_pic_set( i, j ) | 
} | 
... | 
} | 
ilp_ref_pic_set( layerIdx, ilpRpsIdx ) { | Descriptor | 
for( i = layerIdx − 1; ( i >= 0 ) && !( max_one_active_ref_layer_flag && present_in_il_rps_flag[ i + 1 ] ); i− − ) |  | 
if( direct_dependency_flag[ layerIdx ][ i ] ) |  | 
present_in_il_rps_flag[ i ] | u(1) | 
} |  | 

## Slide 5: Proposed Syntaxes
slice_segment_header( ) { | Descriptor
... | 
if( nuh_layer_id > 0 && !all_ref_layers_active_flag && NumDirectRefLayers[ nuh_layer_id ] > 0) { | 
inter_layer_pred_enabled_flag | u(1)
if ( inter_layer_pred_enabled_flag && NumDirectRefLayers[ nuh_layer_id ]> 1 ) { | 
if( numIlpRefPicSets[ nuh_layer_id ] > 0 ) | 
ilp_ref_pic_set_vps_flag | u(1)
if( ilp_ref_pic_set_vps_flag ) { | 
if( numIlpRefPicSets[ nuh_layer_id ] > 1 ) | 
ilp_ref_pic_set_idx | u(v)
} | 
else | 
ilp_ref_pic_set( LayerIdxInVps[ nuh_layer_id ], numIlpRefPicSets[ nuh_layer_id ] ) | 
} | 
} | 
… | 

## Slide 6: Bit-count saving
Use-case #1 – Different frame-rate case
  Multi-layer bitstream
  Multi-layer bitstream with different frame-rate such as the higher layer has double frame-rate than its immediate lower layer
  Each layer has direct dependency to all layers below it
 | Bits in VPS |  | Bits in SH |  | 
 | Current | Proposed | Current | Proposed | Saving
EL 2 (per 4 picture) | 0 | 7 | 9 | 8 | 11.11%
EL 3 (per 8 picture) | 0 | 14 | 30 | 20 | 33.33%
EL 4 (per 16 picture) | 0 | 25 | 52 | 40 | 23.08%

## Slide 7: Bit-count saving
Use-case #2 – Fixed number of ILP ref pics
  Multi-layer bitstream
  Each layer has direct dependency to all layers below it
  Only two of the direct dependent layers are used
    The closest one & one of the rest.
 | Bits in VPS |  | Bits in SH |  | 
 | Current | Proposed | Current | Proposed | Saving
EL 3 | 0 | 9 | 7 | 3 | 57.14%
EL 4 | 0 | 17 | 7 | 4 | 42.86%
EL 5 | 0 | 25 | 10 | 4 | 60.00%