## Slide 1: AHG18: On Supporting Higher Bit Depth With Transform Skip Only Changes
Kiran Misra, Seung-Hwan Kim
(JCTVC-N0259)

## Slide 2: Organization
Background & Motivation
Problem Statement
Proposed Method
Results
Conclusions

## Slide 3: Background & Motivation
To support higher bit depth the current HEVC range extension draft allows values larger than 16-bits:
  For level data included within the bitstream
  For coefficient data output by the dequantizer
  For intermediate values after the first 1-D inverse transform
It is asserted that the last two changes listed above require transforms capable of processing a larger data range when compared to HEVC version 1
This contribution proposes a design where higher bit depth is supported by changing the transform skip processing path only

## Slide 4: Problem Statement
To support higher bit depth the current inverse transform needs to process values larger than 16-bits.
IT / ITS
DQ
>> bdShift1
16-bit Clip
>> bdShift2
HEVC v1:
level
residue
IT*
DQ
>> bdShift1
(BD+7)-bit Clip
>> bdShift2
Current HEVC range extensions draft (changes from HEVC v1 highlighted in red):
level
residue
ITS*
DQ
>> bdShift1
(BD+7)-bit Clip
>> bdShift2
level
residue
BD: sample bit depth
DQ: Dequantization, IT: Inverse transform, ITS: Inverse transform skip (except the right shifts)

## Slide 5: Proposed Solution
IT
DQ
>> bdShift1
16-bit Clip
>> bdShift2
level
residue
ITS*
DQ
>> bdShift1-B
C-bit Clip
>> bdShift2
level
residue
bdShift1 = BD + M – 5
bdShift2 = 20 – BD
B = Max(BD + M - 15, 0)
C = (BD <= 15) ? 16 : (BD + 1)
BD: Sample bit depth, M: Log2 of block size
DQ: Dequantization, IT: Inverse transform, ITS: Inverse transform skip (except the right shifts)
Proposed design:

## Slide 6: Experimental condition & results
Proposed modifications implemented on Range Extension 4.1 software
Test Conditions as defined in AHG18
Cross-check document: JCTVC-O0314
Thank you - Samsung
Note, RExt-4.1 anchor software dequantizer and inverse transform/inverse transform-skip right shift differs from draft as described in bug-report #1185
 | All Intra |  | 
 | Y | U | V
12-bit | 0.6% | 0.9% | 0.9%
14-bit | 1.1% | 2.3% | 2.6%
16-bit | 0.6% | 0.4% | 0.4%

## Slide 7: Conclusions
Proposed modifications to transform skip processing path to support high bit depth coding.
With the proposed design no change is required to the core transform processing capabilities when compared to an HEVC v1 decoder.
Simulations demonstrate that for the proposed design under AHG18 test conditions, the average luma BD rate change is 0.6% (12-bit), 1.0% (14-bit), 0.5% (16-bit).