## Slide 1: Non-RCE1: Inter colour-component residual coefficients prediction
K. Kawamura, S. Naito
KDDI Corp. (KDDI R&D Labs., Inc.)
Notes: Cross-check is JCTVC-O0319

## Slide 2: Overview
Residual-coefficients prediction is proposed
  Based on inter colour-component,
  Before inverse transform like DCT/DST/TS.
    After inverse quantization.
  No syntax changes from RCE1’s syntax.
Small BD-rate losses compared to RCE1
  1.3% / 0.8% / 0.2% for AI / RA / LDB Main-tier
Recommend to adopt the proposal to HM-RExt

## Slide 3: Motivation
Inter component operation can become forward in the decoder pipeline.
  Benefit to implement a hardware decoder

## Slide 4: RCE1 proposal
Inter Colour-Component Residual Prediction for each TU
  : Chroma reconstructed residual signal
  : Decoded chroma signal from the bit-stream
  : Reconstructed luma residual signal

## Slide 5: Decoder pipeline in ILP
Parse
Luma IQ
Luma IT
Luma reconst.
Chroma IQ
Chroma IT
Chroma Reconst.
+
Parse
Luma IQ
Luma IT
Luma reconst.
Chroma IQ
Chroma IT
Chroma Reconst.
ILP

## Slide 6: Proposed pipeline
+
Parse
Luma IQ
Luma IT
Luma reconst.
Chroma IQ
Chroma IT
Chroma Reconst.
ILP
Parse
Luma IQ
Luma IT
Luma reconst.
Chroma IQ
Chroma IT
Chroma Reconst.
+
ILCP

## Slide 7: Some limitation
Luma and chroma base should be identical.
  Intra 4x4 uses DST/DCT for luma/chroma
  TS is independent of the component type
Solutions
  Encoder decides on/off.
  ILCP is disabled for 4x4 TU.
    Some redundant syntax can be reduced.
  Chroma DST is introduced.

## Slide 8: Combined Solutions
 | Domain | Encoder decision | Chroma DST (4x4 enable) | Parsing dependency
RCE1-2 | Signal | N/A | N/A | N/A
Limited ILP | Signal | Yes | Yes | No
Proposal 3 | Coeff. | Yes | Yes | No
Proposal 2 | Coeff. | Yes | No | Yes
Proposal 1 | Coeff. | Yes | No | No

## Slide 9: Experimental Results 1
Implemented on HM12.0-RExt4.1-RCE1-2
No syntax change and no chroma DST
 |  | HE Main-tier |  | 
 |  | G | B | R
RGB | AI | -16.5 | -15.3 | -15.9
 | RA | -13.0 | -11.0 | -12.5
 | LDB | -12.3 | -8.5 | -9.8
 |  | Y | U | V
YUV 4:4:4 | AI | -1.2 | -5.8 | -5.6
 | RA | -0.4 | -7.4 | -6.2
 | LDB | -0.2 | -5.5 | -5.4

## Slide 10: Experimental Results 1’
RCE1-2 vs Proposal 1
Small losses are observed.
 |  | HE Main-tier |  | 
 |  | G | B | R
RGB | AI | 2.3 | 1.7 | 1.9
 | RA | 1.4 | 0.9 | 1.3
 | LDB | 0.4 | 0.3 | 0.4
 |  | Y | U | V
YUV 4:4:4 | AI | 0.2 | 0.9 | 1.5
 | RA | 0.1 | 0.9 | 1.1
 | LDB | 0.0 | 0.4 | 0.0

## Slide 11: Experimental Results 2
Small syntax change and no chroma DST
 |  | HE Main-tier |  | 
 |  | G | B | R
RGB | AI | -16.7 | -15.5 | -16.0
 | RA | -13.1 | -11.0 | -12.6
 | LDB | -12.4 | -8.5 | -9.8
 |  | Y | U | V
YUV 4:4:4 | AI | -1.4 | -6.1 | -5.8
 | RA | -0.5 | -7.7 | -6.4
 | LDB | -0.1 | -5.6 | -5.4

## Slide 12: Experimental Results 3
Chroma DST is introduced.
 |  | HE Main-tier |  | 
 |  | G | B | R
RGB | AI | -17.9 | -16.4 | -17.0
 | RA | -13.9 | -11.4 | -13.1
 | LDB | -12.6 | -8.6 | -10.0
 |  | Y | U | V
YUV 4:4:4 | AI | -1.4 | -6.3 | -6.3
 | RA | -0.5 | -7.7 | -6.7
 | LDB | -0.1 | -5.5 | -5.5

## Slide 13: Performance Comparison All Intra / RGB condition
Chart: 
| G | B | R
RCE1-2 | -0.18103 | -0.16584 | -0.17279
Limited Trans. | -0.1794 | -0.16342 | -0.17012
Proposal 3 | -0.17944 | -0.16352 | -0.17029
Proposal 2 | -0.16707 | -0.15453 | -0.16032
Proposal 1 | -0.16473 | -0.15314 | -0.15904

## Slide 14: Conclusion
New residual-coefficients prediction for 4:4:4
  BD-rate gains are 9.4% / 7.1% / 6.7%.
    AI / RA / LDB main tier for RExt RGB/YUV
  Small losses are observed compared to RCE1.
  Inter colour-component operation moved forward stage in a decoder pipeline
Recommend to adopt the proposal to HM-RExt