## Slide 1
RExt: On intra block copy motion
vector coding
JCTVC-O0277
Guoxin Jin, Ankur Saxena and Felix Fernandes
Samsung Electronics, Co. Ltd.
Dallas R & D Research Center

## Slide 2: Motivation
Intra_BlockCopy mode was adopted in the July 2013 JCTVC meeting.
In HM12.0+RExt4.1, the IntraBC Motion Vector difference is not coded properly.
Current CU
Prediction
Current CTU
Left CTU
Left Left CTU

## Slide 3: Brief Overview
Currently Exponential-Golomb code IntraBC Mvd in HEVC
Technique 1 :
  Fixed-length coding for IntraBC Mvd instead of Exponential-Golomb.
  BD-Rate gains of 1 % for Lossy SC YUV 444 in All Intra
  Bit-rate saving of 0.3% for Lossless SC YUV 444.
Technique 2 :
  Use Huffman coding for IntraBC Mvd
  BD-Rate gains of 1.5 % for Lossy SC YUV 444.
  Bit-rate saving of 0.4% for Lossless SC YUV 444.

## Slide 4: Statistics of Mvd
Motion vector differences are not symmetric.
For a period of 8, there is a strong peak compared to the neighboring values.
Exponential-Golomb code does not performs efficiently for coding the Intra Block Copy motion vector differences.
Horizontal (-120~56) Vertical (-56 ~ 56 )
could use 8 bits fixed-length could use 7 bits fixed-length

## Slide 5: Coding Algorithm
Encoding Given IntraBC motion vector difference x: if x is 0 encode 0 and return else encode 1 use proposed coding for abs(x) encode sign
Decoding read a bit if bit is 0 return 0 else value = use proposed coding method to decode read a bit if bit is 1 return (-value) else return (value)

## Slide 6: Complexity
Fixed-length coding comparing to Exp-Golomb code does not require any computation at the encoder.
Huffman coding scheme requires storage of a code-book at both encoder and decoder side.
  For the decoder, O(log(N)) time required to parse the code-word.

## Slide 7: Proposed Fixed-Length Coding for IntraBC Mvd
Table 1. Lossy setting IntraBC Mvd
 | All Intra HE Main-tier |  |  | All Intra HE High-tier |  |  | All Intra HE Super-High-tier |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class F | -0.5% | -0.5% | -0.5% | -0.4% | -0.4% | -0.4% | -0.3% | -0.3% | -0.3%
Class B | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
SC RGB 444 | -0.6% | -0.6% | -0.6% | -0.5% | -0.5% | -0.5% | -0.4% | -0.4% | -0.4%
Animation RGB 444 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
SC YUV 444 | -1.0% | -1.0% | -1.0% | -0.8% | -0.8% | -0.7% | -0.6% | -0.5% | -0.5%
Animation YUV 444 | 0.0% | 0.0% | -0.1% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
RangeExt | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
SC(444) GBR Optional | -0.4% | -0.4% | -0.4% | -0.3% | -0.4% | -0.3% | -0.3% | -0.4% | -0.3%
SC(444) YUV Optional | -0.9% | -0.9% | -0.9% | -0.8% | -0.8% | -0.8% | -0.7% | -0.7% | -0.7%
Enc Time[%] | 101% |  |  | 101% |  |  | 101% |  | 
Dec Time[%] | 101% |  |  | 101% |  |  | 101% |  | 
 | Random Access HE Main-tier |  |  | Random Access HE High-tier |  | 
 | Y | U | V | Y | U | V
Class F | -0.4% | -0.4% | -0.5% | -0.3% | -0.2% | -0.3%
Class B | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
SC RGB 444 | -0.5% | -0.6% | -0.6% | -0.5% | -0.6% | -0.5%
Animation RGB 444 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
SC YUV 444 | -0.9% | -0.9% | -0.9% | -0.7% | -0.7% | -0.7%
Animation YUV 444 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
RangeExt | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
SC(444) GBR Optional | -0.3% | -0.3% | -0.4% | -0.2% | -0.1% | -0.1%
SC(444) YUV Optional | -1.2% | -1.2% | -1.2% | -0.9% | -0.8% | -0.8%
Enc Time[%] | 101% |  |  | 101% |  | 
Dec Time[%] | 102% |  |  | 102% |  | 
Low delay B HE Main-tier |  |  | Low delay B HE High-tier |  | 
Y | U | V | Y | U | V
-0.3% | -0.5% | -0.7% | -0.1% | -0.3% | -0.3%
0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
0.2% | 0.1% | 0.2% | 0.0% | 0.1% | 0.0%
0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
-0.4% | -0.4% | -0.4% | -0.4% | -0.3% | -0.4%
0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
0.0% | -0.1% | -0.1% | 0.0% | 0.0% | -0.1%
-0.1% | -0.1% | -0.1% | 0.2% | 0.1% | 0.0%
-1.6% | -1.3% | -1.6% | -0.8% | -0.6% | -1.0%
101% |  |  | 101% |  | 
102% |  |  | 102% |  | 

## Slide 8: Proposed Fixed-Length Coding for IntraBC Mvd
Table 2 Intra. Lossless setting IntraBC Mvd
 | AI Main |  |  |  |  |  |  |  |  |  |  | 
 | compression ratio (Total) |  | compression ratio (Average) |  | compression ratio (min) |  | compression ratio (max) |  | Bit-rate saving (Total) | Bit-rate saving (Average) | Bit-rate saving (Min) | Bit-rate saving (Max)
 | Ref. | Tested | Ref. | Tested | Ref. | Tested | Ref. | Tested |  |  |  | 
Class F | 4.57 | 4.58 | 5.57 | 5.58 | 2.27 | 2.27 | 11.14 | 11.15 | 0.1% | 0.1% | 0.0% | 0.3%
Class B | 2.24 | 2.24 | 2.26 | 2.26 | 2.08 | 2.08 | 2.44 | 2.44 | 0.0% | 0.0% | 0.0% | 0.0%
SC RGB 444 | 7.88 | 7.89 | 9.5 | 9.54 | 5.23 | 5.23 | 14.73 | 14.78 | 0.2% | 0.2% | 0.0% | 0.4%
Animation RGB 444 | 2.48 | 2.48 | 2.5 | 2.52 | 2.15 | 2.15 | 3.05 | 3.05 | 0.0% | 0.0% | 0.0% | 0.0%
SC YUV 444 | 11.09 | 11.12 | 13.2 | 13.26 | 7.87 | 7.87 | 19.32 | 19.41 | 0.2% | 0.3% | 0.0% | 0.5%
Animation YUV 444 | 3.00 | 3.00 | 3.2 | 3.16 | 2.57 | 2.57 | 3.93 | 3.93 | 0.0% | 0.0% | 0.0% | 0.0%
RangeExt | 1.92 | 1.92 | 2.38 | 2.38 | 1.46 | 1.46 | 4.37 | 4.37 | 0.0% | 0.0% | 0.0% | 0.0%
SC GBR 444 Optional | 20.30 | 20.34 | 24.82 | 24.93 | 9.69 | 9.68 | 36.10 | 36.27 | 0.2% | 0.3% | -0.1% | 0.6%
SC YUV 444 Optional | 31.85 | 32.00 | 34.39 | 34.64 | 22.30 | 22.28 | 51.97 | 52.58 | 0.5% | 0.5% | -0.1% | 1.1%
Enc Time[%] |  |  | 100% |  |  |  |  |  |  |  |  | 
Dec Time[%] |  |  | 100% |  |  |  |  |  |  |  |  | 

## Slide 9: Proposed Fixed-Length Coding for IntraBC Mvd
Table 2 Random Access. Lossless setting IntraBC Mvd
RA Main |  |  |  |  |  |  |  |  |  |  | 
compression ratio (Total) |  | compression ratio (Average) |  | compression ratio (min) |  | compression ratio (max) |  | Bit-rate saving (Total) | Bit-rate saving (Average) | Bit-rate saving (Min) | Bit-rate saving (Max)
Ref. | Tested | Ref. | Tested | Ref. | Tested | Ref. | Tested |  |  |  | 
8.66 | 8.66 | 36.22 | 36.26 | 3.01 | 3.01 | 90.48 | 90.56 | 0.0% | 0.1% | 0.0% | 0.2%
2.60 | 2.60 | 2.60 | 2.60 | 2.57 | 2.57 | 2.64 | 2.64 | 0.0% | 0.0% | 0.0% | 0.0%
53.71 | 53.73 | 117.01 | 117.34 | 19.48 | 19.49 | 225.68 | 226.70 | 0.0% | 0.2% | -0.1% | 0.4%
3.58 | 3.58 | 3.60 | 3.60 | 3.43 | 3.43 | 3.70 | 3.70 | 0.0% | 0.0% | 0.0% | 0.0%
73.79 | 73.86 | 157.08 | 157.58 | 24.42 | 24.43 | 287.13 | 288.37 | 0.1% | 0.2% | 0.0% | 0.4%
3.8 | 3.84 | 4.48 | 4.48 | 2.75 | 2.75 | 5.70 | 5.70 | 0.0% | 0.0% | 0.0% | 0.0%
2.1 | 2.1 | 2.5 | 2.5 | 1.5 | 1.53 | 4.41 | 4.41 | 0.0% | 0.0% | 0.0% | 0.0%
42.0 | 42.0 | 254.1 | 255.6 | 11.5 | 11.45 | 395.52 | 397.89 | 0.0% | 0.4% | -0.1% | 0.6%
101.1 | 101.1 | 314.9 | 318.0 | 30.5 | 30.42 | 531.53 | 538.93 | 0.1% | 0.6% | -0.1% | 1.4%
100% |  |  |  |  |  |  |  |  |  |  | 
100% |  |  |  |  |  |  |  |  |  |  | 

## Slide 10: Modified Fixed-Length Coding for IntraBC Mvd
Table 2 Low Delay. Lossless setting IntraBC Mvd
LB Main |  |  |  |  |  |  |  |  |  |  | 
compression ratio (Total) |  | compression ratio (Average) |  | compression ratio (min) |  | compression ratio (max) |  | Bit-rate saving (Total) | Bit-rate saving (Average) | Bit-rate saving (Min) | Bit-rate saving (Max)
Ref. | Tested | Ref. | Tested | Ref. | Tested | Ref. | Tested |  |  |  | 
8.9 | 8.9 | 57.8 | 57.7 | 3.0 | 3.0 | 169.5 | 169.3 | 0.0% | 0.0% | -0.1% | 0.0%
2.6 | 2.6 | 2.6 | 2.6 | 2.6 | 2.6 | 2.6 | 2.6 | 0.0% | 0.0% | 0.0% | 0.0%
62.2 | 62.3 | 355.6 | 356.6 | 20.5 | 20.5 | 1618.0 | 1624.6 | 0.0% | 0.1% | -0.1% | 0.4%
3.6 | 3.6 | 3.6 | 3.6 | 3.4 | 3.4 | 3.7 | 3.7 | 0.0% | 0.0% | 0.0% | 0.0%
85.1 | 85.2 | 469.0 | 470.8 | 25.7 | 25.7 | 2105.0 | 2114.8 | 0.1% | 0.2% | 0.0% | 0.5%
4 | 3.9 | 4.5 | 4.5 | 2.8 | 2.8 | 5.8 | 5.8 | 0.0% | 0.0% | 0.0% | 0.0%
2.1 | 2.1 | 2.5 | 2.5 | 1.5 | 1.5 | 4.4 | 4.4 | 0.0% | 0.0% | 0.0% | 0.0%
45 | 45.0 | 1010.8 | 1013.1 | 11.6 | 11.6 | 2253.7 | 2266.3 | -0.1% | -0.1% | -0.8% | 0.6%
117.1 | 116.9 | 1139.4 | 1115.7 | 31.0 | 31.0 | 2208.6 | 2124.9 | -0.1% | -1.0% | -3.9% | 1.1%
99% |  |  |  |  |  |  |  |  |  |  | 
100% |  |  |  |  |  |  |  |  |  |  | 

## Slide 11: Proposed Huffman Coding for IntraBC Mvd
Table 3. Lossy setting IntraBC Mvd
 | All Intra HE Main-tier |  |  | All Intra HE High-tier |  |  | All Intra HE Super-High-tier |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class F | -0.8% | -0.7% | -0.7% | -0.6% | -0.6% | -0.5% | -0.4% | -0.4% | -0.4%
Class B | -0.1% | -0.1% | -0.1% | -0.1% | 0.0% | -0.1% | 0.0% | 0.0% | 0.0%
SC RGB 444 | -0.9% | -0.9% | -1.0% | -0.8% | -0.7% | -0.8% | -0.6% | -0.6% | -0.6%
Animation RGB 444 | -0.1% | -0.1% | -0.1% | -0.1% | -0.1% | -0.1% | 0.0% | 0.0% | 0.0%
SC YUV 444 | -1.5% | -1.4% | -1.5% | -1.2% | -1.1% | -1.1% | -0.9% | -0.8% | -0.8%
Animation YUV 444 | -0.1% | -0.2% | -0.2% | -0.1% | -0.1% | -0.1% | 0.0% | -0.1% | -0.1%
RangeExt | 0.0% | 0.0% | -0.1% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
SC(444) GBR Optional | -1.2% | -1.2% | -1.2% | -1.0% | -1.0% | -1.0% | -1.0% | -0.8% | -0.8%
SC(444) YUV Optional | -2.2% | -2.2% | -2.2% | -1.9% | -1.9% | -1.9% | -1.6% | -1.6% | -1.5%
Enc Time[%] | 101% |  |  | 101% |  |  | 101% |  | 
Dec Time[%] | 101% |  |  | 101% |  |  | 101% |  | 
 | Random Access HE Main-tier |  |  | Random Access HE High-tier |  | 
 | Y | U | V | Y | U | V
Class F | -0.5% | -0.6% | -0.5% | -0.4% | -0.4% | -0.3%
Class B | -0.1% | -0.1% | 0.0% | -0.1% | 0.0% | -0.1%
SC RGB 444 | -0.9% | -0.9% | -1.0% | -0.9% | -0.9% | -0.9%
Animation RGB 444 | -0.1% | -0.1% | -0.1% | 0.0% | 0.0% | 0.0%
SC YUV 444 | -1.2% | -1.2% | -1.2% | -0.9% | -1.0% | -1.0%
Animation YUV 444 | -0.1% | -0.1% | -0.1% | -0.1% | -0.1% | -0.1%
RangeExt | -0.1% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
SC(444) GBR Optional | -1.0% | -1.0% | -1.1% | -0.9% | -0.8% | -0.8%
SC(444) YUV Optional | -2.0% | -2.0% | -1.9% | -1.7% | -1.6% | -1.5%
Enc Time[%] | 101% |  |  | 101% |  | 
Dec Time[%] | 102% |  |  | 103% |  | 
Low delay B HE Main-tier |  |  | Low delay B HE High-tier |  | 
Y | U | V | Y | U | V
-0.4% | -0.8% | -0.5% | -0.3% | -0.3% | -0.5%
0.0% | -0.1% | -0.2% | 0.0% | 0.0% | 0.0%
-0.5% | -0.5% | -0.5% | -0.5% | -0.3% | -0.4%
-0.1% | -0.1% | -0.1% | -0.1% | -0.1% | -0.1%
-1.4% | -1.5% | -1.4% | -1.0% | -0.9% | -0.9%
0.0% | -0.1% | 0.0% | 0.0% | 0.0% | 0.0%
0.0% | 0.0% | -0.1% | 0.0% | 0.0% | -0.1%
-0.3% | -0.1% | 0.0% | -0.5% | -0.3% | -0.2%
-1.8% | -1.6% | -1.9% | -1.1% | -0.8% | -1.2%
101% |  |  | 102% |  | 
103% |  |  | 103% |  | 

## Slide 12: Huffman Coding for IntraBC Mvd
Table 4 Intra. Lossless setting IntraBC Mvd
 | AI Main |  |  |  |  |  |  |  |  |  |  | 
 | compression ratio (Total) |  | compression ratio (Average) |  | compression ratio (min) |  | compression ratio (max) |  | Bit-rate saving (Total) | Bit-rate saving (Average) | Bit-rate saving (Min) | Bit-rate saving (Max)
 | Ref. | Tested | Ref. | Tested | Ref. | Tested | Ref. | Tested |  |  |  | 
Class F | 4.57 | 4.58 | 5.57 | 5.58 | 2.27 | 2.27 | 11.14 | 11.15 | 0.2% | 0.2% | 0.0% | 0.7%
Class B | 2.24 | 2.24 | 2.26 | 2.26 | 2.08 | 2.08 | 2.44 | 2.44 | 0.0% | 0.0% | 0.0% | 0.0%
SC RGB 444 | 7.88 | 7.90 | 9.5 | 9.55 | 5.23 | 5.23 | 14.73 | 14.81 | 0.2% | 0.3% | 0.0% | 0.5%
Animation RGB 444 | 2.48 | 2.48 | 2.5 | 2.52 | 2.15 | 2.15 | 3.05 | 3.05 | 0.0% | 0.0% | 0.0% | 0.0%
SC YUV 444 | 11.09 | 11.13 | 13.2 | 13.28 | 7.87 | 7.88 | 19.32 | 19.45 | 0.3% | 0.4% | 0.1% | 0.6%
Animation YUV 444 | 3.00 | 3.00 | 3.2 | 3.16 | 2.57 | 2.57 | 3.93 | 3.93 | 0.0% | 0.0% | 0.0% | 0.0%
RangeExt | 1.92 | 1.92 | 2.38 | 2.38 | 1.46 | 1.46 | 4.37 | 4.37 | 0.0% | 0.0% | 0.0% | 0.0%
SC GBR 444 Optional | 20.30 | 20.41 | 24.82 | 24.99 | 9.69 | 9.72 | 36.10 | 36.34 | 0.5% | 0.6% | 0.3% | 0.8%
SC YUV 444 Optional | 31.85 | 32.14 | 34.39 | 34.79 | 22.30 | 22.44 | 51.97 | 52.80 | 0.9% | 1.0% | 0.6% | 1.6%
Enc Time[%] |  |  | 101% |  |  |  |  |  |  |  |  | 
Dec Time[%] |  |  | 101% |  |  |  |  |  |  |  |  | 

## Slide 13: Huffman Coding for IntraBC Mvd
Table 4 Random Access. Lossless setting IntraBC Mvd
RA Main |  |  |  |  |  |  |  |  |  |  | 
compression ratio (Total) |  | compression ratio (Average) |  | compression ratio (min) |  | compression ratio (max) |  | Bit-rate saving (Total) | Bit-rate saving (Average) | Bit-rate saving (Min) | Bit-rate saving (Max)
Ref. | Tested | Ref. | Tested | Ref. | Tested | Ref. | Tested |  |  |  | 
8.66 | 8.66 | 36.22 | 36.35 | 3.01 | 3.01 | 90.48 | 90.90 | 0.0% | 0.2% | 0.0% | 0.5%
2.60 | 2.60 | 2.60 | 2.60 | 2.57 | 2.57 | 2.64 | 2.64 | 0.0% | 0.0% | 0.0% | 0.0%
53.71 | 53.76 | 117.01 | 117.42 | 19.48 | 19.50 | 225.68 | 226.68 | 0.1% | 0.2% | -0.1% | 0.5%
3.58 | 3.58 | 3.60 | 3.60 | 3.43 | 3.43 | 3.70 | 3.70 | 0.0% | 0.0% | 0.0% | 0.0%
73.79 | 73.91 | 157.08 | 157.73 | 24.42 | 24.44 | 287.13 | 289.02 | 0.2% | 0.3% | 0.1% | 0.7%
3.8 | 3.84 | 4.48 | 4.48 | 2.75 | 2.75 | 5.70 | 5.70 | 0.0% | 0.0% | 0.0% | 0.0%
2.1 | 2.1 | 2.5 | 2.5 | 1.5 | 1.53 | 4.41 | 4.41 | 0.0% | 0.0% | 0.0% | 0.0%
42.0 | 42.1 | 254.1 | 256.1 | 11.5 | 11.48 | 395.52 | 398.81 | 0.3% | 0.6% | 0.2% | 0.8%
101.1 | 101.7 | 314.9 | 317.6 | 30.5 | 30.64 | 531.53 | 536.28 | 0.6% | 0.8% | 0.6% | 0.9%
102% |  |  |  |  |  |  |  |  |  |  | 
102% |  |  |  |  |  |  |  |  |  |  | 

## Slide 14: Huffman Coding for IntraBC Mvd
Table 4 Low Delay. Lossless setting IntraBC Mvd
LB Main |  |  |  |  |  |  |  |  |  |  | 
compression ratio (Total) |  | compression ratio (Average) |  | compression ratio (min) |  | compression ratio (max) |  | Bit-rate saving (Total) | Bit-rate saving (Average) | Bit-rate saving (Min) | Bit-rate saving (Max)
Ref. | Tested | Ref. | Tested | Ref. | Tested | Ref. | Tested |  |  |  | 
8.9 | 8.9 | 57.8 | 57.9 | 3.0 | 3.0 | 169.5 | 170.1 | 0.0% | 0.1% | 0.0% | 0.3%
2.6 | 2.6 | 2.6 | 2.6 | 2.6 | 2.6 | 2.6 | 2.6 | 0.0% | 0.0% | 0.0% | 0.0%
62.2 | 62.3 | 355.6 | 357.2 | 20.5 | 20.5 | 1618.0 | 1627.9 | 0.1% | 0.2% | 0.0% | 0.6%
3.6 | 3.6 | 3.6 | 3.6 | 3.4 | 3.4 | 3.7 | 3.7 | 0.0% | 0.0% | 0.0% | 0.0%
85.1 | 85.2 | 469.0 | 471.7 | 25.7 | 25.7 | 2105.0 | 2119.9 | 0.1% | 0.3% | 0.0% | 0.7%
4 | 3.9 | 4.5 | 4.5 | 2.8 | 2.8 | 5.8 | 5.8 | 0.0% | 0.0% | 0.0% | 0.0%
2.1 | 2.1 | 2.5 | 2.5 | 1.5 | 1.5 | 4.4 | 4.4 | 0.0% | 0.0% | 0.0% | 0.0%
45 | 45.1 | 1010.8 | 1013.1 | 11.6 | 11.6 | 2253.7 | 2263.9 | 0.2% | 0.1% | -0.5% | 0.4%
117.1 | 117.7 | 1139.4 | 1117.5 | 31.0 | 31.2 | 2208.6 | 2128.5 | 0.5% | -0.7% | -3.8% | 1.2%
101% |  |  |  |  |  |  |  |  |  |  | 
103% |  |  |  |  |  |  |  |  |  |  | 

## Slide 15: Conclusions
Fixed length coding for intraBC Mvd
  Simplification.
  1 % gain for Lossy SC YUV 444 coding.
  0.3 % gain for Lossless SC YUV 444 coding.
Huffman coding for intraBC Mvd
  1.5% gain for Lossy SC YUV 444 coding.
  0.4% gain in Lossless setting
  No extra computation required in encoder side
  Same complexity as Exp-Golomb code in decoder side